## Slide 1: Redundancy reduction in Cbf and Merging coding
Bin Li
Jizheng Xu
Feng Wu
Gary Sullivan
Microsoft

## Slide 2: Outline
Possible redundancy in the current tree-based representation
Redundancy reduction in Cbf coding
Redundancy reduction in PU-based merging
Redundancy reduction in CU-based merging
Conclusion

## Slide 3: Tree-based representation
Node splitting means that the node has non-uniform attribute
When all previous sub-nodes have a same attribute,
The last one must have a different one
Tree-based structure is used to provide a hierarchical representation, which is used widely
in AVC and TMuC.

## Slide 4: Cbf coding in residue transform quadtree
Split flag=0
Send one cbf to indicate if there is non-zero coefficient
or
Split flag=1
Send 4 cbf to for 4 sub units

## Slide 5: Redundancy in cbf coding
The case that four cbf=0 should not happen
When it is detected that all the previous TU with cbf=0, no cbf for the last TU needs to be transmitted

## Slide 6: Merging coding
When it is detected that all the previous TU with a same MV, there is no need to merge the last block into that MV

## Slide 7: CU-based merging with redundancy reduction
CU-based merging as the anchor
The proposed modification leads to minor bit-saving
Average Class A | -0.1 | -0.1 |  | 
Average Class B | -0.1 | -0.1 | -0.2 | -0.1
Average Class C | -0.1 | -0.1 | -0.2 | -0.1
Average Class D | -0.1 | -0.1 | -0.2 | -0.1
Average Class E |  |  | -0.1 | -0.1
Average All | -0.1 | -0.1 | -0.2 | -0.1
RA | RA LoCo | LD | LD LoCo

## Slide 8: PU-based merging
2Nx2N, Nx2N, 2NxnU
  Reduce the number of MV candidates to be merged
    NumMergeCandidates
NxN
  Disabling merging
Experimental results
  TMuC0.7.4 with the PU-based bug fixed

## Slide 9: PU-based merging with redundancy reduction
PU-based merging as the anchor
Average Class A | -0.4 | 0.0 |  | -0.2
Average Class B | -0.6 | -0.1 | -1.0 | -0.3
Average Class C | -0.5 | -0.2 | -0.6 | -0.4
Average Class D | -0.5 | -0.1 | -0.8 | 0.0
Average Class E |  |  | -1.3 | -0.2
Average All | -0.5 | -0.1 | -0.9 | -0.1
RA | RA LoCo | LD | LD LoCo

## Slide 10: Conclusions
Current quadtree representation may have some redundancy
  Cbf
  Merging
  Hierarchical ALF signaling
Recommend to make corresponding modifications in the design