## Slide 1: CE6.a Santa Clara University and Hisilicon Report on Block Based Intra Prediction
Guichun Li
Lingzhi Liu
Nam Ling
Jianhua Zheng
Philipp Zhang
JCTVC-D026

## Slide 2: Introduction
The integration of Intra Plane mode in (Unified Intra Prediction) UIP with Multiple Predictor Sets (MPS) method was proposed in JCTVC-C111.
In this experiment, extra non-directional modes are integrated in UIP.
Simulations were performed on different combinations of Intra Modes:
  UIP with 2 Extra modes and MPS (MPS Intra)
  MPS Intra with Planar Intra Prediction enabled

## Slide 3: Introduction
The default intra prediction in TMuC, Unified Intra Prediction (UIP):
33 directional modes + 1 DC mode.
Modifications:
  Intra Plane mode and Bilinear mode are integrated
  Multiple Predictor Sets method is used
Experimental results have shown that coding efficiency can be improved by the proposed method.

## Slide 4: Grouping Predictors with Multiple Predictor Sets

## Slide 5: Simulation Result (Intra Only) - MPS Intra
TEST#1 | Intra |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.2 | -0.2 | -0.2 | -0.5 | -0.3 | -0.4
Class B | -0.2 | -0.2 | -0.3 | -0.5 | -0.4 | -0.4
Class C | -0.1 | -0.1 | -0.1 | -0.2 | -0.2 | -0.2
Class D | 0.0 | 0.0 | 0.0 | -0.2 | -0.2 | -0.2
Class E | -0.4 | -0.4 | -0.5 | -0.8 | -0.8 | -0.6
All | -0.2 | -0.2 | -0.2 | -0.4 | -0.4 | -0.3
Enc Time[%] | 102% |  |  | 99% |  | 
Dec Time[%] | 97% |  |  | 99% |  | 

## Slide 6: Simulation Result (Intra Only) - MPS Intra with Planar Enabled
TEST#2 | Intra |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.1 | -0.2 | -0.1 | 0.7 | 0.6 | 0.4
Class B | -0.2 | -0.3 | -0.3 | 0.7 | 0.5 | 0.3
Class C | 0.0 | -0.1 | -0.1 | 1.1 | 0.8 | 0.7
Class D | 0.0 | 0.0 | 0.0 | 1.0 | 0.7 | 0.6
Class E | -0.4 | -0.3 | -0.5 | 0.7 | 0.1 | 0.4
All | -0.1 | -0.2 | -0.2 | 0.9 | 0.6 | 0.5
Enc Time[%] | 103% |  |  | 101% |  | 
Dec Time[%] | 98% |  |  | 97% |  | 

## Slide 7: Mode Usage on Class B (1080P) Sequences
Rank | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Mode | 2 | 0 | 1 | 16 | 34 | 11 | 8 | 15
Usage | 13.07% | 10.47% | 8.90% | 6.24% | 4.77% | 4.27% | 4.13% | 3.38%
Rank | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
Mode | 7 | 5 | 4 | 12 | 30 | 14 | 21 | 10
Usage | 3.37% | 3.07% | 3.06% | 3.02% | 2.86% | 2.84% | 2.65% | 2.49%
Rank | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Mode | 3 | 13 | 29 | 6 | 31 | 22 | 9 | 33
Usage | 1.99% | 1.91% | 1.89% | 1.67% | 1.66% | 1.62% | 1.60% | 1.10%
Rank | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
Mode | 17 | 23 | 28 | 25 | 20 | 32 | 27 | 26
Usage | 1.07% | 0.94% | 0.87% | 0.76% | 0.75% | 0.68% | 0.65% | 0.60%
Rank | 33 | 34 | 35 | 36 |  |  |  | 
Mode | 19 | 24 | 18 | 35 |  |  |  | 
Usage | 0.56% | 0.55% | 0.53% | 0.03% |  |  |  | 

## Slide 8: Visual Quality Comparison (1)

## Slide 9: Visual Quality Comparison (2)

## Slide 10: Conclusion
The Bilinear mode is rarely used. It is not necessary to have this mode for intra prediction.
Enabling Planar Intra Prediction introduces coding loss, it is not necessary either.
MPS Intra performs better than TMuC v0.9 Anchor, on both BD-rate and subjective visual quality. The major contribution of the gain is from the Intra Plane mode.
Integrating Plane mode with MPS in UIP can improve the performance of intra prediction.