## Slide 1
CE 7 : Cross-Check for Toshiba’s proposal 1-d Directional Unified Transform by Samsung
JCTVC-D032
Ankur Saxena & Felix C. Fernandes
Samsung Electronics, Co. Ltd.
Dallas R&D Center
Notes: <number>

## Slide 2: Summary
<number>
Applied for TU sizes | 4*4 and 8*8 | For sizes 16*16 and 32*32, DCT is used
Total number of transforms for size 4*4 and 8*8 | 3 | DCT in TMuC 0.9 Modified DCT different than TMuC 0.9 DCT. KLT (1-D DUT)
Additional TMuC Quantization matrices required | Yes | Additional set of Q and Q-1 matrices at size 4 and 8 is used. Storage increases from 960 to 1920 elements.
Additional TMuC Transform cores required for DCT | Yes | Modified DCT uses a different core. Modified DCT is used only in I-slices coding
Scan modification | Yes | 9 different initial scan orders at size 4*4 and 8*8 are used. They appear to be obtained from training.

## Slide 3: Experimental Results
Cross-Check was performed for Intra HE, Intra LC, Random Access HE, Random Access LC configurations according to stipulated conditions in CE 7 description (JCTVC-C507, Robert Cohen et al.)
Same BD Results as sent by Toshiba. Slight difference in decoding times in Intra LC settings
<number>
 | Intra |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -2.70 | -2.97 | -2.86 | -2.97 | -1.35 | -0.94
Class B | -1.36 | -1.76 | -1.69 | -1.66 | -1.58 | -1.51
Class C | -2.19 | -1.96 | -1.94 | -2.37 | -1.87 | -1.91
Class D | -2.18 | -1.93 | -1.92 | -2.15 | -1.86 | -1.84
Class E | -2.84 | -2.74 | -2.45 | -3.12 | -0.91 | -1.50
All | -2.12 | -2.14 | -2.05 | -2.31 | -1.57 | -1.60
Enc Time[%] | 109% |  |  | 99% |  | 
Dec Time[%] | 106% |  |  | 111% |  | 
 |  | Random access |  |  | Random access LoCo | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -1.16 | -0.51 | -0.20 | -1.03 | -0.18 | 0.04
Class B | -0.77 | -0.53 | -0.55 | -0.63 | -0.48 | -0.51
Class C | -0.99 | -0.62 | -0.61 | -0.88 | -0.68 | -0.59
Class D | -0.95 | -0.72 | -0.33 | -0.66 | -0.37 | -0.19
Class E |  |  |  |  |  | 
All | -0.93 | -0.60 | -0.46 | -0.76 | -0.47 | -0.37
Enc Time[%] | 98% |  |  | 99% |  | 
Dec Time[%] | 107% |  |  | 105% |  | 

## Slide 4: Comments
<number>
Instead of the 2nd DCT matrix introduced in the proposal, original DCT kernels in TMuC 0.9 can be used.
This will also not require the need of additional set of quantization and inverse quantization matrices only for I-slices which are currently being used in Toshiba’s proposal.
The proposed tool from Toshiba combines transform and scanning.

## Slide 5
<number>
Thank You