## Slide 1: PSNR Computation on R′G′B′ Color System
Dzung Hoang JCTVC-D040

## Slide 2: Executive Summary
Current HM computes PSNR for Y′, CB, and CR separately. Many contributions report BD-rate results only for Y′. When BD-rate results for Y′, CB, and CR differ, it’s hard to make good conclusions. Adhoc combinations of PSNR for Y′, CB, and CR are suspect.
We propose additional computation of PSNR based upon R′G′B′ color system. Then we can get a single PSNR result that combines luma and chroma components in a meaningful way.
We examine a subset of results from JCTVC-D035 to illustrate the new measure.

## Slide 3: Motivation
Digital video capture and display devices use standardized R′G′B′ color systems.
Digital video compression works on Y′CBCR color system.
Quality, subjective or objective, should be performed with display technology in mind.
It may be desirable to compute objective distortion in R′G′B′.

## Slide 4: How to Compute R′G′B′ PSNR
Upsample Y′CBCR from 4:2:0 to 4:4:4
Convert 4:4:4 Y′CBCR to R′G′B′
Compute MSE of R′, G′, B′
Average MSE of R′, G′, B′ to form MSE of R′G′B′
Compute PSNR from MSE

## Slide 5: Y′CBCR Upsampling
Use polyphase filter coefficients borrowed from MSSG to convert 4:2:0 to 4:2:2 and then to 4:4:4
Vertical polyphase filter
  [3, -16, 67, 227, -32, 7]/256
  [7, -32, 227, 67, -16, 3]/256
Horizontal polyphase filter
  [0, 0, 256, 0, 0]/256
  [21, -52, 159, 159, -52, 21]/256

## Slide 6: Convert Y′CBCR to R′G′B′
There are different Y′CBCR and R′G′B′ color systems
  i.e., Rec. ITU-R BT.601, Rec. ITU-R BT.709, and SMPTE 240M
Color space conversion matrix for Rec. ITU-R BT.709 with R′, G′, and B′ in the range [0, 1]:

## Slide 7: Compute PSNR from MSE
Definition of PSNR for 8-bit unsigned:
HM computes average of frame PSNR:

## Slide 8: Compute PSNR of R′G′B′
R′G′B′ clipped to [0, 1]
Definition of PSNR for [0, 1] data:

## Slide 9: IBDI versus no-IBDI for LD-HE
 |  | Y | Cb | Cr | R′ | G′ | B′ | R′G′B′
Class B | Kimono | -2.2 | -4.3 | -4.8 | -3.3 | -2.4 | -3.8 | -3.3
1080p | ParkScene | -2.6 | -7.0 | -10.1 | -5.2 | -2.9 | -6.2 | -5.0
 | Cactus | -4.0 | -5.3 | -6.7 | -5.5 | -4.1 | -4.9 | -5.0
 | BasketballDrive | -3.1 | -9.1 | -7.2 | -5.6 | -3.6 | -6.9 | -5.7
 | BQTerrace | -5.1 | -25.0 | -31.0 | -11.3 | -5.5 | -14.2 | -11.1
 | Average | -3.4 | -10.2 | -11.9 | -6.2 | -3.7 | -7.2 | -6.0
Class C | BasketballDrill | -2.8 | -6.4 | -5.3 | -4.5 | -3.2 | -5.3 | -4.6
WVGA | BQMall | -3.6 | -9.1 | -9.8 | -6.3 | -4.0 | -6.7 | -6.0
 | PartyScene | -1.8 | -9.7 | -10.7 | -5.0 | -2.3 | -6.2 | -4.8
 | RaceHorses | -1.0 | -2.9 | -2.7 | -1.9 | -1.1 | -2.2 | -1.9
 | Average | -2.3 | -7.0 | -7.2 | -4.4 | -2.6 | -5.1 | -4.3
Class D | BasketballPass | -1.0 | -4.7 | -1.9 | -1.6 | -1.2 | -3.5 | -2.2
WQVGA | BQSquare | -2.2 | -29.3 | -28.9 | -8.6 | -2.8 | -10.0 | -7.5
 | BlowingBubbles | -1.9 | -10.0 | -11.4 | -5.7 | -2.5 | -6.6 | -5.3
 | RaceHorses | -1.1 | -2.8 | -2.5 | -1.8 | -1.2 | -2.1 | -1.9
 | Average | -1.5 | -11.7 | -11.2 | -4.4 | -1.9 | -5.6 | -4.2
Class E | Vidyo1 | -10.1 | -10.7 | -10.3 | -10.2 | -10.0 | -10.1 | -10.1
WQVGA | Vidyo3 | -10.4 | 1.6 | -5.3 | -9.0 | -10.0 | -5.3 | -8.0
 | Vidyo4 | -10.4 | -11.1 | -9.9 | -10.3 | -10.3 | -10.7 | -10.5
 | Average | -10.3 | -6.7 | -8.5 | -9.8 | -10.1 | -8.7 | -9.5
All | Average | -3.9 | -9.1 | -9.9 | -6.0 | -4.2 | -6.5 | -5.8

## Slide 10: Recommendations
Collect color system metadata for test sequences
Compute R′G′B′ PSNR in addition
  May want to use weighted average of MSE for R′, G′, B′
  We seek input on appropriate set of weights
Modify HM to compute PSNR instead of APSNR