## Slide 1: Benefit of the new syntax and semantics for very low delay coding in HEVC (JCTVC-D054, m18801)
4th JCT-VC meeting, Daegu/Korea
2011/1/20-28
K.Kazui, J.Koyama, and A.Nakagawa

## Slide 2: Outline
Low delay functionality is essential for real-time applications. It is important to realize efficient, interoperable low delay coding in HEVC.
We proposed the scheme which minimizes the loss of coding efficiency in very low delay coding at the 2nd meeting.
  Coding gain over the conventional multiple slices scheme using TMuC0.7.3 is 9.0% (64x64 LCU) / 15.9% (32x32 LCU) as reported at the 3rd meeting.
Overview of our proposal
  New high-level syntax and semantics for guaranteeing the correct reconstruction of all pixels.
    New syntax describes the position of the region boundary between a refreshed area and a non-refreshed area.
    New semantics restricts the reference from a CU / pixel inside a refreshed area to a CU / pixel inside a non-refreshed area.
    Those can minimize the loss of coding efficiency compared with the conventional schemes with negligible increase of decoder complexity.
  New buffer model for interoperable low delay coding of less than 1 frame period
    The decoding time of a group of LCUs in a picture is defined.
We think the proposed scheme is beneficial to HEVC for supporting low delay coding of less than 1 frame period.

## Slide 3: Very low delay coding
Codec delay of less than 1 frame period
  Real-time bi-directional video transmission applications such as TV conference require the codec delay of less than 100 ms.
  Several codec apparatus with 10 ms delay become available in the market.
    This implies there is a high demand for very low delay coding in the industry.
  The size of the bitstream buffer shall be minimized because it is proportional to the delay.
  The fluctuation of the number of bits per unit time shall be minimized.
    The bitstream buffer is used to absorb the fluctuation. If the fluctuation is smaller than the size the bitstream buffer, the bitstream buffer does not overflow /underflow.

## Slide 4: Vertical intra MB line refresh scheme
A vertical intra MB line is inserted in a picture and circulates horizontally in the picture.
Minimal buffer size is achieved.
  The number of bits in a MB line becomes almost constant in a picture because intra MBs are distributed uniformly in each MB line. Thus the buffer size can be reduced to (#bits per picture) / (#MB lines)
Minimal coding loss and random-access are also achieved
  Each MB in a picture is coded intra (i.e. refreshed) only once in a refresh cycle.
Vertical intra MB line refresh scheme

## Slide 5: Restriction of reference for correct reconstruction
Correct recovery of pixels in intra MB line scheme
  Unlike intra picture refresh, proper encoder control is needed in order to guarantee the correct recovery of whole pixels at the end of each refresh cycle when the decoding process starts from a recovery point.
  Specifically, pixels in a refreshed area should not refer to pixels in a non-refreshed area because those may not be decoded correctly.
Restriction of reference in AVC
  At motion estimation
    Search range shall be limited inside the refreshed area of a reference picture.
    Encoder issue
  At intra prediction
    The direction of intra prediction shall be limited.
    Encoder issue
  At deblocking filter
    Deblocking filter shall be disabled at the region boundary.

## Slide 6: Possible scheme in AVC
Disabling deblocking filter at MB boundary
Disabling deblocking filter at MB boundary
  Main issue: how to disable deblocking filter at the region boundary.
    Multiple slices insertion scheme was discussed in JCTVC-C021.
  Another possible scheme: disabling filter at MB boundary for all MBs.
    There is only one slice in a picture in order to avoid the overhead of slices.
    Disabling deblocking filter at MB boundary for all MBs is necessary because there is no mechanism to disable filter on MB-by-MB basis without using slices.

## Slide 7: Problem in AVC
(A) Loss of coding efficiency
Scheme Cause | Multiple slices insertion (As discussed in JCTVC-C031) | Disabling DF at MB boundary (Test result is shown in JCTVC-D052)
Restricted MV range | Yes | Yes
Multiple slices Overhead of slice header Loss of coding efficiency in MV prediction etc. | Yes | No
Disabling DF at MB boundary (+ disabling ALF in HEVC） | No | Yes

## Slide 8: Problem in AVC(Cont.)
Theoretically the buffer size can be reduced to the number of bits per MB line. (e.g. 0.2 ms * bitrate @1080p60)
However the buffer size of an AVC compliant decoder shall be larger than bits per picture (e.g. 16 ms * bitrate @1080p60).
  HRD of AVC only defines the decoding time of a picture.
  The last bit of a coded picture shall arrive at a decoder before the decoding time. An ideal decoder decodes whole picture instantly at the decoding time.
  The arrival time of each MB in a picture is not specified. In the worst case, the last bit of the first MB of the picture arrives just before the decoding time. Therefore an actual decoder cannot start the decoding process before the decoding time.
Moreover an actual decoder needs 1 frame period for decoding a picture.
  The minimum codec delay becomes larger than 2 frame period.
    buffer delay (>= 1 frame period) + decoding delay (= 1 frame period)
Interoperable very low delay coding of less than 10ms is impossible.
  There are several codec apparatus of 10ms delay in the market. But those apparatus need off-band, proprietary protocol for 10ms delay operation.
  Interoperability among apparatus of different venders is practically impossible.
(B) Interoperable low delay coding of less than 1 frame period

## Slide 9: Proposal (1): New high-level syntax/semantics
New syntax for signaling the position of the region boundary between a refreshed area and a non-refreshed area
  Simple geometric position in a picture, in unit of smallest CU width/height.
  Multiple slices are not used for describing the region boundary.
New semantics for restricting reference at the region boundary
  The reference from a CU/pixel inside a refreshed area to a CU/pixel inside a non-refreshed area is prohibited in order to guarantee the correct reconstruction of all pixels in a picture at the end of each refresh cycle.
  Modified definition of availability of a neighboring CU is applied for intra prediction, MV prediction, and deblocking filter.
  The region boundary is treated as a picture boundary in MC and ALF for pixels inside a refreshed area. This improves coding efficiency compared with the conventional schemes because a MV which refers partially inside a non-refreshed area is allowed.
  Asymmetric restriction can improve coding efficiency slightly compared with the symmetric restriction at a slice boundary.
Coding loss in the conventional schemes are removed.
  Insertion of multiple slices is unnecessary.
  Restriction of MV range is relaxed.
  Deblocking filter (and ALF in HEVC) can be applied with no restriction.

## Slide 10: Proposal (2): New buffer model
New buffer model for interoperable low delay coding of less than 1 frame
  The decoding time of a group of LCUs dtg() is defined at CPB operation.
    Each group of LCUs has (almost) equal number of bits when the vertical intra MB line scheme is used. Thus the interval of the arrival time of each group of LCUs is constant.
dtg(i, n): decoding time of n-th group
of LCUs in i-th picture
dt(i) : decoding time of i-th picture
N : number of groups in a picture
New buffer model for very low delay coding
  dtg() informs a decoder that a group of LCUs can be decoded at dtg() without underflow, which is earlier than picture-based decoding time dt().
  New buffer model can reduce the delay for display at a decoder.
    A group of LCUs can be displayed at dtg() + {(1 frame period) / N}
  Interoperable very low delay coding is assured.

## Slide 11: Merit of our proposal
Negligible increase of decoder complexity
  Description and process of the region boundary is simple.
  Restriction of reference between CUs is realized by modified definition of CU availability.
  Restriction of reference between pixels for MC and ALF is realized by similar mean for unrestricted MV of AVC.
Loss of coding gain is minimized compared with the conventional scheme.
  The gain of the proposed scheme from the “disabling deblocking filter” scheme is 6.0% (64x64 LCU), 6.3% (32x32 LCU) .
  See JCTVC-D052 for detail.
Interoperability
  New buffer model realizes interoperability of very low delay coding less than 1 frame period among apparatus of different venders.

## Slide 12: Conclusion
Low delay is essential for real-time applications. It is important to realize efficient, interoperable low delay coding in HEVC.
  The is a high demand for very low delay coding in the market.
Our proposal minimizes loss of coding efficiency in very low delay coding and guarantees interoperability.
Our proposal consists of new high-level syntax and semantics, and new buffer model.
Features
  New semantics only introduces modified definition of CU availability and so on. Increase of decoder complexity is negligible.
  Proposed scheme minimizes loss of coding efficiency in very low delay coding compared with the conventional schemes.
  New buffer model realizes interoperable low delay coding of less than 1 frame period.
We request to start the discussion of the support of very low delay coding in HEVC.