## Slide 1: Lightweight Slicing for Entropy Coding JCTVC-D070 Kiran Misra and Andrew Segall
l
Notes: <number>

## Slide 2: Overview
Goal
  Introduce flexibility in slices to support additional slice restrictions on the parsing process
Benefit
  Simple extension of legacy slices
  Interoperates with other proposed slicing methods
  Reduces the overhead of the slice header
  Support higher slice counts
  Direct approach to creating “parallel friendly” bit-stream

## Slide 3: Motivation
Traditional slice design
  Slice picture into regions that can be parsed and reconstructed independently
  Example: Slice picture into regions with same number of pixels
  Properties of example (from decoder):
    Provides similar load to reconstruction unit
    Concern: Results in wide variability in entropy complexity in each slice
    Concern: In extreme, nearly all bins can be assigned to the same slice

## Slide 4: Motivation
Distribution of bins when using one slice for LCU row (64x64 LCU). Note the heavy tails.

## Slide 5: Motivation
Traditional slice design
  To manage entropy decoding complexity, we should bound the number of bins in a slice
  This has two drawbacks
    The number of pixels within the slice is now highly variable
    The burden on encoders may be higher than when slicing by a fixed spatial region

## Slide 6: Proposed Approach
Proposed approach
  Support dividing a “traditional” slice into additional “entropy slices”
    Entropy slices can be parsed independently
  Benefits
    Allows structuring a bit-stream that is better balanced in both entropy decoding and reconstruction complexity load
    Overhead of entropy slices is smaller than traditional slices
      Better support for high slice counts anticipated for parallel applications
      Lower burden for encoders when signaling bit-stream regions with bounds on bins
Traditional Slice
Entropy Slices

## Slide 7: Proposed Approach
Syntax
  Use lightweight slice header to signal entropy slice
    Header only includes information necessary for entropy decoding
    Additional benefit: entropy slices do not require reconfiguration of the reconstruction process at the decoder

## Slide 8: Performance
Performance
  Configuration:
    1 traditional slice per picture
    Entropy slices constrained to 180,000 bins
    Target: 32x parallelism for HD
  Compared to anchor – 0.1-0.2% loss

## Slide 9: Anticipated Applications
Example application – mixed CPU/GPU
  Trend toward multi-core CPU and highly parallel GPU
  We anticipate mapping entropy decoding to CPU and reconstruction to GPU
  This is consistent with deployment of previous standards
    Software only
    CPU parsing with
    reconstruction acceleration
    Slice level acceleration
with entropy slices
without entropy slices

## Slide 10: Conclusions
Conclusions
  Propose a more flexible slice design that supports additional slice restrictions on the parsing process
  Benefits
    Simple and direct extension of legacy slices
    Interoperates with other proposed slicing methods
    Reduces the overhead of the slice header
    Better support of higher slice counts
    Direct approach to creating “parallel friendly” bit-stream
  Performance
    0.1%-0.2% decrease in coding efficiency for 32 slices (180,000 bin/slice limit)
  Method verified by NEC
  Propose adoption into HM