## Slide 1: On transform dynamic range
Kiran Misra, Louis Kerofsky, Andrew Segall
<number>
Notes: <number>

## Slide 2: Introduction
Introduction
  We propose a method to manage the bit-depth requirements of the transform
  Our approach
    We enforce bit-depth constraints prior to both inverse transforms
    This restricts/bounds the storage needs following the dequantization process
    This also restricts/bounds the storage needs of the transpose operation between the two transforms
<number>
Notes: <number>

## Slide 3: Overview
Descale
2(Period+B)
1-d Inverse transform horz.
Coefficients
A
+
+
1-d Inverse transform vert.
Decoded residue
Quantized coefficients
2-D Inverse transform
Dequantizer
Memory storage
Memory storage
<number>
Notes: <number>

## Slide 4: Proposed Approach
Descale*24
25-Period
+
+
Quantized coefficients
Clip to 16-bits prior to
memory storage
Descale
2Period+B
Coefficients
Quantized coefficients
Clip to 16-bits prior to
memory storage
8x8 dequantizer:
4x4/16x16/32x32/NXN dequantizer:
2Period-6
Coefficients
<number>
Notes: <number>

## Slide 5: Proposed Approach (continued)
1-D Inverse transform horz.
Coefficients
1-D Inverse transform vert.
Decoded residue
2-D Inverse transform NXN
Memory storage
Right bit shift by f(N)
Clip to 16-bits
Left bit shift by f(N)
<number>
Notes: <number>

## Slide 6: Advantages
Supports all tools in HM 0.9
  IBDI, TPE, all prediction modes etc.
Addresses all combinations of residue data and transform coefficients.
Improves decoder robustness to violation of dynamic range
  Due to Non-conforming encoder
  Due to bitstream error etc.
Negligible coding loss (reported on next slide)
General solution applicable to various transform designs.
<number>

## Slide 7: Results (average Y BD bitrate between +0.0% and -0.2%)
<number>
 | Intra |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
Class B | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
Class C | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
Class D | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
Class E | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
All | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
Enc Time[%] | 102% |  |  | 107% |  | 
Dec Time[%] | 102% |  |  | 102% |  | 
 |  | Random access |  |  | Random access LoCo | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.0 | 0.1 | 0.1 | 0.0 | 0.1 | 0.1
Class B | 0.0 | 0.0 | -0.1 | 0.0 | 0.1 | 0.0
Class C | 0.0 | 0.0 | 0.0 | 0.0 | 0.1 | 0.0
Class D | 0.0 | 0.0 | 0.2 | 0.0 | -0.1 | -0.1
Class E |  |  |  |  |  | 
All | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
Enc Time[%] | 98% |  |  | 102% |  | 
Dec Time[%] | 99% |  |  | 97% |  | 
 | Low delay |  |  | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | 0.0 | -0.2 | -0.1 | 0.0 | 0.0 | -0.1
Class C | 0.0 | -0.1 | 0.1 | 0.0 | -0.1 | 0.0
Class D | 0.0 | -0.6 | 0.1 | 0.0 | 0.2 | 0.1
Class E | -0.2 | 0.0 | -0.1 | -0.2 | -0.5 | -0.2
All | 0.0 | -0.2 | 0.0 | 0.0 | -0.1 | 0.0
Enc Time[%] | 100% |  |  | 98% |  | 
Dec Time[%] | 102% |  |  | 103% |  | 

## Slide 8: Conclusion
We propose a method to manage the dynamic range of the inverse transform
  We observe that it is possible to enforce bit-limits after de-quantization and for transpose.
  Little impact on coding efficiency
  Benefit: we assert that this makes the video codec more accessible to architectures with hardware limitations on bus-width / memory.
We propose further study of the method in CE
<number>