## Slide 1: Periodic initializations for wavefront coding
Kiran Misra, Andrew Segall
<number>

## Slide 2: Goal
Goal
  Provide support for wave-front processing in the HM design
  Others have proposed solutions to this problem that require transmitting LCUs out-of-order
  Here, we seek to maintain the raster-scan order within the picture
<number>

## Slide 3: Proposed Approach
Approach
  Re-initialize the entropy coder at the start of each LCU row
  Transmit the locations of the “start of LCU row” location within the bitstream to decoder:
    Method 1: use explicit location information in slice header
    Method 2: use headers
    The two methods support different encoder scenarios
<number>

## Slide 4: Illustration for proposed approach
Raster-Scan Bitstream
Parallel Decoder
Decoder
Decoder
Decoder
Decoder
Decoder
Sequential Decoder
Decoder
<number>

## Slide 5: Bitstream Syntax
Syntax
  LCU resets enabled in the SPS
  Location of entry points in the bit-stream signaled in the slice header (optional)
  cabac_init_idc sent in first LCU of row (optional)
<number>

## Slide 6: Performance
Performance evaluation
  Technology integrated into HM
  Entry point at each LCU row
  Tested two scenarios
    Location of LCU rows written in slice header
    Location of LCU rows marked with headers in the bit-stream
Confidential
<number>

## Slide 7: Performance
Confidential
<number>
Entry point Headers
Entry points in SH

## Slide 8: Performance
Observation
  We observe larger losses on low delay compared to random access
  As a second set of results, we used an alternative initialization table for CABAC
    Results – Low delay improves by 1.2%
Confidential
<number>

## Slide 9: Performance
Confidential
<number>
Entry point Headers
Entry points in SH
Using cabac_init_idc

## Slide 10: Conclusion
Conclusions
  System to enable wavefront coding/decoding
  Bit-stream maintains raster scan of LCU information
  Two encoder scenarios are supported
    Location information in the slice header (better coding efficiency; requires bit-stream buffering at encoder)
    Location information by header (lower coding efficiency but no write backs at encoder)
  Compatible with all slicing methods under consideration
  Results
    0.2%, 1.4% and 2.8% for entry point for each LCU row (~32x parallelism for 4k)
    0.2%, 1.5% and 1.6% for same configuration and alternative CABAC tables
<number>