## Slide 1: Parallel Prediction Unit for Parallel Intra Coding JCTVC-D074 Jie Zhao and Andrew Segall
l
Notes: <number>

## Slide 2: Overview
Goal :
  Reduce serial dependencies in the intra-prediction process
Overview
  Parallel Prediction Unit
  Parallel intra-prediction
  Syntax
  Performance

## Slide 3: Parallel Prediction Unit
Motivation:
  Serial bottleneck in intra-prediction
    Due to the casual prediction of pixel values (top/left/left top neighbors)
    Small block sizes results in more dependencies within an LCU
Our solution –Parallel Prediction Unit
  Defines a CU size within a LCU that can be encoded/decoded in parallel
  For CUs that are larger than a defined PPU size, traditional sequential prediction is performed
  Benefit: Enables parallelism as dependencies increase within an LCU
LCU
CU/PU/TU
CU
CU
CU
CU/PU/TU
CU/PU/TU
CU/PU/TU
PPU

## Slide 4: Parallel Prediction Block
Parallel Prediction Block (PPB)
  Refers to a block within a PPU that uses parallel intra prediction
  For example, for a 16x16 PPU, we support two types of PPBs
    A PPU is split into 4-8x8 blocks, and at least one of these blocks is further divided into 4x4 blocks.
    A 16x16 PPU that is split entirely into 4x4 sub-blocks and is an entire PPB.
  This design is motivated by encoder design
CU/PU/TU
CU/PU/TU
CU/PU/TU
CU/PU/TU
PPU
1) One type of PPB
PPB
CU/PU/TU
CU/PU/TU
CU/PU/TU
CU/PU/TU
PPB=
PPU
2) Another type of PPB

## Slide 5: Parallel Intra Prediction
Parallel Intra Prediction
  Partitioning a PPB to two sets
    Using Checker-board pattern
    Shaded blocks are one set
    White blocks are the other set
  Blocks within each partition are predicted in parallel and use reconstruct pixels from outside the PPB
  Note: This is compatible with all intra-prediction methods considered at this meeting
Second set blocks
First set blocks
PPB
PPB
First set blocks
First set blocks
Second set blocks

## Slide 6
Parallel Intra Prediction
Parallel Processing 8 blocks at a time.
8x speed up (5x compared to wavefront)
1
2
5
6
9
10
13
14
0
3
4
7
8
11
12
15
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Parallel intra prediction
Serial intra prediction
Notes: <number>

## Slide 7: Parallel Intra Prediction
Prediction of First Set Blocks
  Use only reconstructed pixels from neighboring PPBs
  Prediction uses existing intra-prediction techniques.
  Only change: for DC prediction, we compute the DC as a weighted function of the distance between the block and the horizontal and left PPU boundaries
LCU
CU/PU
CU
CU
CU
CU/PU
CU/PU
CU/PU
PPB

## Slide 8: Parallel Intra Prediction
Prediction of Second Set Blocks
  Uses pixels in neighboring PPBs AND pixel in first set blocks
  The bottom and right boundaries may be available
    We use prediction from the bottom/right neighbors.
    The causal and non-causal predictions can be weighted.
    Note: the prediction from the bottom/right neighbors use the existing prediction mode. We only alter the definition of the source pixels.

## Slide 9: Signaling
Signaling
  We signal the PPU size in the sequence header

## Slide 10: Signaling
Signaling
  Weighted prediction is signaled in the prediction unit syntax

## Slide 11: Performance
Parallel Intra Prediction
  We compared our technology with the current, serial approach for intra-prediction in anchor
  Conditions
    HM0.9
    All 6 standard test Configurations
    PPU of 16x16 (HD only)
  Average Impact on BD rate
    Intra (HC&LC): 0.3%
    Randomaccess (HC&LC): 0.1%
    Lowdelay (HC&LC): 0.0%

## Slide 12: Performance
Parallel Intra Prediction (Fast search)
  We also report the case for fast encoding.
  Here, we only check the case when the PPB and PPU size are the same when the existing, recursive encoding strategy results in at least one PPB.
  Conditions
    HM0.9
    All 6 standard test Configurations
    PPU of 16x16
  Average Coding Impact on BD rate Vs. anchor
    Intra (HC&LC): 0.3%
    Randomaccess (HC&LC): 0.1%
    Lowdelay (HC&LC): 0.0%

## Slide 13: Conclusions
Conclusions
  We presented parallel intra prediction technique for HEVC design.
    Provides parallelism for both encoder and decoder.
    Parallelism is achieved by partitioning a PPB into two sets
      First set predicted from boundaries of PPB
      Second set predicted from reconstructed first set and/or boundaries of PPB
  Performance -- impact on average BD rate
    Intra (both HC and LC): 0.3%
    Random access (both HC and LC): 0.1%
    Low delay (both HC and LC): 0.0%
  Method verified by Toshiba (JCTVC-D111)
  Propose to adopt this technique to HM.