## Slide 1: Improvement on signaling method for prediction modes
Jaehyun Lim
LG Electronics
JCTVC-D084

## Slide 2: Introduction
Prediction mode signaling in HM S/W
  Joint coding of prediction mode & partition size for coding efficiency
  Set of unary-code is used
coding_unit( x0, y0, log2CUSize ) { | Descriptor
︙ | 
if( slice_type != I ) | 
pred_mode | u(1) ¦ ae(v)
︙ | 
if( PredMode = = MODE_INTER ) | 
inter_partitioning_idc | ue(v) ¦ ae(v)
︙ | 
} | 
prediction mode | partition | codewords | 
direct |  | 0 | 
intra | 2Nx2N | 1 | 00000
 | NxN | 1 | 00001
inter | 2Nx2N | 1 | 1
 | 2NxN | 1 | 01
 | Nx2N | 1 | 001
 | NxN | 1 | 0001

## Slide 3: Introduction
Motivation
  The codeword for each prediction mode has different length.
  By the source coding theorem,
  the length of each codeword is approximately proportional to the negative logarithm of the probability.
  Therefore, the best coding efficiency is achieved when the most common symbols use the shortest codes.
  For better coding efficiency, it is required to rearrange the codewords reflecting the distribution of each prediction mode in inter slice.

## Slide 4: Introduction
Prediction mode signaling
  At first, MODE_SKIP, MODE_MERGE is signaled by flag
  And then, Other prediction modes are signaled by corresponding codewords

## Slide 5: Prediction mode distribution analysis
Distribution of prediction modes in inter slices (CU MRG case)
Chart: Distribution of prediction modes in inter slices (CU MRG)
| 2Nx2N | NxN | 2Nx2N | 2NxN | Nx2N | NxN | skip | mrg | direct | intra | Inter
RAHE | 40.61 | 26.48 | 8.51 | 2.92 | 1.26 | 11.4 | 3.92 | 4.35 | 0.55
LDHE | 37.26 | 25.59 | 12.22 | 1.85 | 0.62 | 11.86 | 4.53 | 5.43 | 0.63
RALC | 54.86 | 13.6 | 6.46 | 1.82 | 1.93 | 10.67 | 4.97 | 4.5 | 1.19
LDLC | 48.03 | 19.64 | 7.19 | 1.13 | 0.94 | 11.62 | 5.33 | 4.99 | 1.12
Characteristics in prediction mode distribution
portion of direct mode < portion of 2Nx2N inter mode
portion of 2NxN inter mode < portion of Nx2N inter mode
class | skip | mrg | direct | intra |  | Inter |  |  | 
 |  |  |  | 2Nx2N | NxN | 2Nx2N | 2NxN | Nx2N | NxN
RAHE | 40.6 | 26.5 | 8.5 | 2.9 | 1.3 | 11.4 | 3.9 | 4.4 | 0.6
LDHE | 37.3 | 25.6 | 12.2 | 1.9 | 0.6 | 11.9 | 4.5 | 5.4 | 0.6
RALC | 54.9 | 13.6 | 6.5 | 1.8 | 1.9 | 10.7 | 5.0 | 4.5 | 1.2
LDLC | 48.0 | 19.6 | 7.2 | 1.1 | 0.9 | 11.6 | 5.3 | 5.0 | 1.1
avg. | 45.2 | 21.3 | 8.6 | 1.9 | 1.2 | 11.4 | 4.7 | 4.8 | 0.9

## Slide 6: Proposed method
4 Prediction modes are rearranged for the codeword
2Nx2N inter mode is switched with direct mode
2NxN inter mode is switched with Nx2N inter mode
[ Current Codeword ]
[ New Codeword ]
prediction mode | partition | codewords | 
direct |  | 0 | 
intra | 2Nx2N | 1 | 00000
 | NxN | 1 | 00001
inter | 2Nx2N | 1 | 1
 | 2NxN | 1 | 01
 | Nx2N | 1 | 001
 | NxN | 1 | 0001
prediction mode | partition | codewords | 
direct |  | 1 | 1
intra | 2Nx2N | 1 | 00000
 | NxN | 1 | 00001
inter | 2Nx2N | 0 | 
 | 2NxN | 1 | 001
 | Nx2N | 1 | 01
 | NxN | 1 | 0001

## Slide 7: Proposed method
Apply to PU MRG case
  Same codewords are used for signaling prediction mode
  After MODE_SKIP signaling, other prediction modes are signaled by corresponding codewords
[ CU MRG case ]
[ PU MRG case ]

## Slide 8: Prediction mode distribution analysis
Same distribution characteristics as CU MRG case
portion of direct mode < portion of 2Nx2N inter mode
portion of 2NxN inter mode < portion of Nx2N inter mode
Distribution of prediction modes in inter slices (PU MRG case)
Chart: Distribution of prediction modes in inter slices (PU MRG)
| 2Nx2N | NxN | 2Nx2N | 2NxN | Nx2N | NxN | skip | direct | intra | Inter
RAHE | 42.77 | 7.8 | 2.87 | 1.24 | 32.17 | 5.43 | 6.48 | 1.24
LDHE | 36.62 | 13.27 | 1.8 | 0.61 | 33.01 | 5.96 | 7.3 | 1.43
RALC | 53.18 | 12.24 | 1.86 | 1.93 | 13.7 | 7.39 | 6.64 | 3.04
LDLC | 46.83 | 14.81 | 1.18 | 0.95 | 18.68 | 7.75 | 7.02 | 2.78
class | skip | direct | intra |  | Inter |  |  | 
 |  |  | 2Nx2N | NxN | 2Nx2N | 2NxN | Nx2N | NxN
RAHE | 42.8 | 7.8 | 2.9 | 1.2 | 32.2 | 5.4 | 6.5 | 1.2
LDHE | 36.6 | 13.3 | 1.8 | 0.6 | 33.0 | 6.0 | 7.3 | 1.4
RALC | 53.2 | 12.2 | 1.9 | 1.9 | 13.7 | 7.4 | 6.6 | 3.0
LDLC | 46.8 | 14.8 | 1.2 | 1.0 | 18.7 | 7.8 | 7.0 | 2.8
avg. | 44.9 | 12.0 | 1.9 | 1.2 | 24.4 | 6.6 | 6.9 | 2.1

## Slide 9: Test condition
Test condition for the proposed method
software | CU MRG case : HM S/W (TMuC 0.9) PU MRG case : CE9 S/W (modified TMuC 0.9 for PU MRG)
test sequences | All seq. (class A/B/C/D for RA, class B/C/D/E for LD)
coding structure | Random Access HE/LC Low Delay HE/LC
etc | the same as the HM (TMuC 0.9) S/W configuration

## Slide 10: Experimental Results
BD rate(%) reduction of the proposed method
BD-rate reduction & complexity
  Avg. gain for HE & LC (CU MRG): 0.0%(HE), -0.3%(LC)
  Avg. gain for HE & LC (PU MRG): 0.0%(HE), -0.5%(LC)
  No encoder/decoder complexity differences
  (Because the proposed method deals with only the codeword change)
class | CU MRG case (anchor: HM) |  |  |  | PU MRG case (anchor: HM with PU MRG) |  |  | 
 | RAHE | LDHE | RALC | LDLC | RAHE | LDHE | RALC | LDLC
A | 0.0 |  | -0.2 |  | 0.0 |  | -0.3 | 
B | 0.0 | 0.0 | -0.2 | -0.2 | -0.1 | 0.0 | -0.4 | -0.6
C | 0.0 | 0.0 | -0.3 | -0.3 | 0.0 | 0.0 | -0.5 | -0.7
D | 0.0 | 0.0 | -0.3 | -0.4 | -0.1 | 0.0 | -0.5 | -0.7
E |  | -0.2 |  | -0.4 |  | -0.1 |  | -0.7
avg. | 0.0 | 0.0 | -0.2 | -0.3 | 0.0 | 0.0 | -0.4 | -0.7
HE/LC avg. | 0.0 |  | -0.3 |  | 0.0 |  | -0.5 | 
Enc Time | 100% | 100% | 100% | 102% | 99% | 99% | 101% | 101%
Dec Time | 100% | 100% | 100% | 100% | 100% | 100% | 100% | 100%

## Slide 11: Conclusion
Enhanced prediction mode signaling method is proposed.
The best coding efficiency is achieved when the most common symbols use the shortest codes
The proposed scheme shows bit-rate reduction without any additional signal overhead and complexity change.
- avg. gain for HE & LC (CU MRG): 0.0%(HE), -0.3%(LC)
- avg. gain for HE & LC (PU MRG): 0.0%(HE), -0.5%(LC)
- No complexity differences
LG Electronics recommends including the codeword table for joint coding of the prediction mode and the partitioning type in the decoding process for coding unit,
and also using the proposed codeword rearrangement in order to achieve better coding efficiency.