## Slide 1
CE8 Subtest1 Informal Subjective Viewing Report
CE8 Coordinators

## Slide 2: Schedule and place
Jan 19: Coordinators copy reference data to the computer and test viewing software;
Jan 20: CE8 Subtest1 proponents copy their data to the computer;
Jan 20 and 21: CE8 Subtest1 proponents and volunteers view results in room “Arte” (no scoring);
Jan 23: Dr. Vittorio Baroncini checked results and determined that scoring is unnecessary due to insignificant visual differences.

## Slide 3: Viewing equipments
[Computer] Windows
  CPU : Intel(R) Core i7 860 Quad 2.80GHz
  Graphic: NVIDIA GeForce GTX 260
  Memory : 3GB
  HDD* : 148GB (Raid-SSD) SATA + 1TB SATA
[Display] Samsung SyncMaster 305T PLUS
  Diagonal Size : TFT - 30"
  Dot Pitch / Pixel Pitch : 0.25mm
  Image Contrast Ratio : 1000:1
  2560 x 1600 / 60 Hz - 300.

## Slide 4: Sequences and coding conditions
[Test sequences]
  ClassB: Kimono (1080p 24Hz)
  ClassC: BQMall (WVGA 60Hz)
  ClassE: Vidyo3 (720 60Hz)
[Coding conditions]
  ClassB: Kimono (HE RA w/o ALF QP=27 and 32)
  ClassC: BQ_Mall (LC RA QP=27 and 32)
  ClassE: Vidyo3 (LC LD QP=27 and 32)
  Note1: The reason of selecting these sequences is that performance of the available computer is not fast enough to playback 1080 50/60p sequences.
  Note2: If time allows, other sequences of Class B, C , and D, and other coding conditions specified in CE8 document can are additionally used.

## Slide 5: Bit-rates

## Slide 6: Preliminary informal viewing on Jan 20 and 21
(Casual) Double Stimulus Continuous Quality Scale Method
- No scoring
- Anchor is played first; ProposalX is played next.
- Viewers do not know who ProponentX is.
Three proponents
- Proponent1: MediaTek deblocking
- Proponent2: NEC debanding
- Proponent3: SKKU deblocking
Seven viewing volunteers (excluding proponents)

## Slide 7: Summary of viewers' comments on preliminary informal viewing
Proponents' qualities are the same as Anchors’
Scoring is unnecessary because the level of differences is small
Kimono QP=27 Proponent1 looks smoothed.
Proponent2 shows better visual quality in sky regions; it shows blur around the face.
Kimono QP=32 Proponent1 is worse than Anchor.
Proponent2 shows better visual quality in sky regions; it worse in other scene.
Proponent3 shows worse visual quality in sky region.
BQ QP=27 Proponent1 have jaggy motion.
Proponent2 shows motion blur around the wall.
Proponent3 shows less motion blur around the wall.
BQ QP=32 Proponent2 looks smooth in flat area.
Proponent3 looks sharper in edges.
Vidyo3 QP=27 Proponent2 shows better visual quality in wall regions; it slightly degrades text regions
Proponent3 shows less color degradation.
Vidyo3 QP=32 Proponent1 shows blocking artifacts and degrades text regions.
Proponent2 has dragging artifacts.
Proponent3 degrade text regions
Representative positive and negative comments
Notes: [Viewer1]
Kimono QP=27 All results look similar.
Kimono QP=32 Proponent1 and Proponent3 are worse than Anchor. Proponent2 looks similar to Anchor.
BQ QP=27 All results look similar.
BQ QP=32 All results look similar.
Vidyo3 QP=27 All results look similar.
Vidyo3 QP=32 Anchor is the best. Proponent 2 has artifacts (dragging).
[Viewer2]
Kimono QP=27 Proponent 1 looks smoothed. Proponent 2 and 3 look similar to Anchor.
Kimono QP=32 All results look similar.
BQ QP=27 Proponent 1 and 3 have jaggy motion.
BQ QP=32 Proponent 1 looks similar to Anchor. Proponent2 looks smooth in flat area. Proponent 3 looks sharper in edges.
Vidyo3 QP=27 All results look similar.
Vidyo3 QP=32 Proponent 3 > Proponent2 > Proponent1
[Viewer3]
Kimono QP=27 All results look similar.
Kimono QP=32 Proponent1 is worse than Anchor. Proponent2 and Proponent3 look similar to Anchor.
BQ QP=27 All results look similar.
BQ QP=32 Proponent 1 is worse than Anchor. Proponent1 and Proponent2 look similar to Anchor.
Vidyo3 QP=27 Proponent2 slightly degrades text regions. Proponent1 and Proponent3 look similar to Anchor.
Vidyo3 QP=32 Proponent1 and Proponent3 degrade text regions.
[Viewer4]
Some regions are differ. However, all results look similar.
[Viewer5]
Proponent2 looks better in some scene but worse in other scene in Kimono QP32.
[Viewer6]
Kimono QP=27 Proponent1 and Proponent3 look similar to Anchor. Proponent2 shows better visual quality in sky regions.
Kimono QP=32 Proponent1 and Proponent3 look similar to Anchor. Proponent2 shows better visual quality in sky regions.
BQ QP=27 Perceiving visual differences is difficult.
BQ QP=32 Perceiving visual differences is difficult.
Vidyo3 QP=27 Proponent1 and Proponent3 look similar to Anchor. Proponent2 shows slightly better visual quality in wall regions.
Vidyo3 QP=32 Proponent1 and Proponent3 degrade text regions.
[Viewer7]
Kimono QP=27 Proponent1 is similar to Anchor.
Proponent2 shows better visual quality in sky regions but shows motion blur the face.
Proponent3 shows worse visual quality in sky region.
Kimono QP=32 Proponent1 is similar to Anchor.
Proponent2 shows motion blur around the face.
Proponent3 shows less motion blur around the face.
BQ QP=27 Proponent1 is similar to Anchor. Proponent2 shows motion blur around the wall. Proponent3 shows less motion blur around the wall.
BQ QP=32 Proponent1 shows motion blur around the wall. Proponent2 shows slight blocking noise. Proponent3 looks the best.
Vidyo3 QP=27 Proponent1, Proponent2 and Proponent3 looks slightly shaper. Proponent3 shows less color degradation.
Vidyo3 QP=32 Proponent1 shows blocking artifacts. Proponen2 and Proponent3 are similar to Anchor..
<number>