## Slide 1: CE10: Summary of CE10 on number of intra prediction directions
Kazuo Sugimoto
Mitsubishi Electric Corporation
JCTVC-D100

## Slide 2: Introduction
Purpose: to characterize the performance and complexity of using different numbers of intra prediction directions
9 organizations conducted verifications on 12 different settings.

## Slide 3: Related documents
  JCTVC-D063 Cross-check report from INRIA
  JCTVC-D050 Cross-check report from I2R
  JCTVC-D207 Cross-check report from NEC
    An additional test on cropped version of SHV sequences
  JCTVC-D291 Cross-check report from MediaTek
  JCTVC-D101 Cross-check report from Mitsubishi
    An additional test on cropped version of SHV sequences
    An additional test on a recommended settings
  JCTVC-D198 Cross-check report from Nokia
  JCTVC-D358 Cross-check report from Samsung
  JCTVC-D102 Cross-check report from Toshiba
    An additional test on a recommended settings

## Slide 4: Test Condition
Software: TMuC v0.9
Anchor: C500 Intra only both HE and LC conditions
Tests
Test #12: the reference without fast mode decisions

## Slide 5: Results on the common test sequences
Decoding time for each test was almost the same.

## Slide 6: Results on cropped SHV sequences
Decoding time for each test was almost the same.

## Slide 7: Conclusions
Numbers of directions to avoid significant performance loss are:
  17 modes for 4x4 (9 modes for SHV sequences)
  34 modes for 8x8 (17 modes for SHV sequences)
  34 (or 17) modes for 16x16 (17 modes for SHV sequences)
  9 modes or less for 32x32
  3 modes or less for 64x64
Recommendations
  Consider these results to decide the number of intra prediction directions when creating the next version of HM