## Slide 1: LUT-based adaptive filtering on intra prediction samples
Kazuo Sugimoto, Shun-ichi Sekiguchi, Akira Minezawa (Mitsubishi)
Kazuhisa Iguchi, Yoshiaki Shishikui (NHK)
JCTVC-D109

## Slide 2: Introduction
In JCTVC-B067, we have shown the possibility of the advantage in terms of coding efficiency using filtering on intra prediction samples compared to intra reference sample smoothing.
In this proposal, intra prediction filter is decided based on a lookup table.

## Slide 3: Intra prediction samples filtering
VLD
+
IQ/IDCT
Frame
Memory
Intra
Prediction
IP filter
Decoding process
4 filters are used for IP filtering
filter is decided according to a LUT

## Slide 4: Filters
3 three-tap filters and a 5 tap filter

## Slide 5: Look-up table
PU Size | Filter mode |  |  | 
 | Filter #0 | Filter #1 | Filter #2 | Filter #3
4x4 | - | mode 3, 6, 9 | mode 2 (DC) | -
8x8 | - | mode 2 (DC) | - | mode 3-9
16x16 | mode 2 (DC) | - | - | mode 3-33
32x32 | - | - | - | -
64x64 | - | - | - | -

## Slide 6: Simplified version
To simplify the proposed method only DC prediction samples are smoothed.
For DC prediction samples, only left and top edge pixel lines are filtered using 2 tap filters.
PU Size | Filter mode |  | 
 | Filter #0 | Filter #1 | Filter #2
4x4 | - | - | mode 2
8x8 | - | mode 2 | -
16x16 | mode 2 | - | -
32x32 | - | - | -
64x64 | - | - | -

## Slide 7: Simulation Results
Simulation are conducted using TMuC 0.9 Intra Only default conditions with SHV sequences
Test Results on the proposed method
-0.6% for HE, -1.3% for LC on common test sequences

## Slide 8: Simulation Results
Simplified version
Test Results on the simplified version of the proposed method
-0.3% for HE, -0.5% for LC on common test sequences

## Slide 9: Simulation Results
Combination of the simplified version and C234
Test Results on the simplified version of the proposed method + C234
-0.5% for HE, -1.0% for LC on common test sequences

## Slide 10: Conclusions
Intra prediction filtering improves coding efficiency
  0.6% and 1.3% for Intra HE and LC respectively
  ENC time increase is 2% and 8%
  DEC time increase is 0% and 4%
Simplified version gives 0.3% and 0.5% gain with 0% ENC/DEC time increase.
Simplified version with C234 gives 0.5% and 1.0% gain with 0% ENC/DEC time increase.
Propose this method to be evaluated in a CE

## Slide 12: Filtering on DC prediction samples
Just top and left edge samples are filtered using 2 tap filters for 4x4, 8x8 and 16x16 blocks.

## Slide 13: Complexity of MDIS vs DCpredFilter+C234
C234
{0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0}, //2x2
{0, X, 0, 1, 0, 0, 1, 0, 0, 1, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0}, //4x4
{0, X, 0, 1, 1, 1, 1, 1, 1, 1, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0}, //8x8
{0, X, 0, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0}, //16x16
{0, 0, 0, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 0, 0, 0, 0, 0, 0}, //32x32
{0, 0, 0, 1, 1, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0}, //64x64
{0, 0, 0, 1, 1, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0} //128x128
MDIS
{0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0}, //2x2
{0, 0, 0, 1, 0, 0, 1, 0, 0, 1, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0}, //4x4
{0, 0, 0, 1, 1, 2, 2, 2, 1, 1, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0}, //8x8
{0, 0, 0, 2, 2, 2, 2, 2, 2, 2, 2, 2, 2, 2, 2, 2, 2, 2, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0}, //16x16
{0, 0, 0, 2, 2, 2, 2, 2, 2, 2, 2, 2, 2, 2, 2, 2, 2, 2, 2, 2, 2, 2, 2, 2, 2, 2, 2, 2, 2, 2, 2, 2, 2, 2, 0, 0, 0, 0, 0, 0}, //32x32
{0, 0, 0, 2, 2, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0}, //64x64
{0, 0, 0, 2, 2, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0} //128x128