## Slide 1: Constrained temporal motion vector prediction for error resilience
Bin Li, Jizheng Xu, Feng Wu, Houqiang Li
University of Science and Technology of China
Microsoft

## Slide 2: AMVP
Up to 5 MVPs in the current design
  One from the temporal co-located block
The max value is used in decoding
  The process of reducing the number of MVP changes the max value

## Slide 3: Frame lost
Temporal MVP is unavailable or incorrect
  The max value is incorrect
  The number of bits read from the bit-stream is incorrect
  The syntax elements read from the bit-stream is meaningless
Fail to decode all the following inter frames
  May cause decoder crash
  Recover until next IDR frame

## Slide 4: Possible solution 1
Disable TMVP
Loss too much
 | RA_HE | RA_LC | LD_HE | LD_LC
Class A | 2.5 | 2.7 |  | 
Class B | 1.8 | 1.4 | 1.8 | 3.0
Class C | 1.6 | 1.7 | 2.3 | 3.3
Class D | 2.0 | 1.9 | 2.2 | 2.8
Class E |  |  | 2.5 | 3.0
All | 1.9 | 1.8 | 2.2 | 3.0

## Slide 5: Possible solution 2
Always code last bit, do not use max value
Loss too much and do not solve the problem
May be even worse than disabling TMVP
 | RA_HE | RA_LC | LD_HE | LD_LC
Class A | 1.6 | 2.3 |  | 
Class B | 1.1 | 2.1 | 0.8 | 2.6
Class C | 1.2 | 1.9 | 1.1 | 2.3
Class D | 1.4 | 2.1 | 1.3 | 2.3
Class E |  |  | 2.6 | 7.3
All | 1.3 | 2.1 | 1.3 | 3.3

## Slide 6: Proposed algorithm
Some entropy decoding recovery point
  Some frames without TMVP
A tradeoff between RD performance and error robustness

## Slide 7: Details
Insert one frame without TMVP do not solve the problem
  The number of reference frame is 2
  Insert two consecutive frames without TMVP

## Slide 8: Experiment result
LD case: inserting two consecutive frames in 8 frames without TMVP
  Can recover very soon, will be shown
RA case: inserting one frame without TMVP in every 8 frames
  Can recover until the next B frame with temporal 0 for regular hierarchical B structure

## Slide 9: Summary result
 | RA_HE | RA_LC | LD_HE | LD_LC
Class A | 0.2 | 0.2 |  | 
Class B | 0.2 | 0.2 | 0.4 | 0.7
Class C | 0.2 | 0.2 | 0.5 | 0.8
Class D | 0.6 | 0.6 | 0.5 | 0.7
Class E |  |  | 0.5 | 0.6
All | 0.3 | 0.3 | 0.5 | 0.7

## Slide 10: Robust decoding
Bit-stream: BasketballPass, LD_LC, QP=32, the 7th frame lost
Anchor: crash at once
Proposed: successful entropy decoding

## Slide 11
Crosschecked by Samsung
Recommend to be included in HM

## Slide 12
Thank you!