## Slide 1: Adaptive Coding order of skip and split flags in LCEC
Bin Li, Jizheng Xu, Feng Wu, Houqiang Li
University of Science and Technology of China
Microsoft

## Slide 2: Split and skip flags
Three cases:
  Further split
  Not further split and skip
  Not further split and not skip
Current design: always coding split flags first

## Slide 3: Bits cost
Possible problem: cost more bits for high temporal correlation sequence
Skip mode cost 2 bits to represent
 | Split flag first | Skip flag first
Further split | 1 | 01
Not further split and skip | 01 | 1
Not further split and not skip | 00 | 00

## Slide 4: Straightforward solution
Code skip flag first
 | Random access low complexity |  |  | Low delay low complexity |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.0 | 0.1 | 0.1 |  |  | 
Class B | -0.4 | -0.3 | -0.3 | 0.1 | 0.1 | 0.1
Class C | 0.2 | 0.2 | 0.2 | 0.6 | 0.6 | 0.6
Class D | 0.1 | 0.1 | 0.1 | 0.6 | 0.6 | 0.6
Class E |  |  |  | -2.3 | -2.3 | -2.2
All | 0.0 | 0.0 | 0.0 | -0.1 | -0.1 | -0.1
Enc Time | 100% |  |  | 100% |  | 

## Slide 5: Adaptive coding order
Always coding skip flag first does not work
Adaptive coding order is necessary
Decide which flag to code first using the information of three surrounding LCUs
  A counter for number of “further split” case (maximum 21)
  A counter for number of “Not further split and skip” case (maximum 16)
Do not change the RD process
  PSNR exactly the same as the anchor

## Slide 6: Simulation result
Always gain, not loss observed
No complexity increase
 | Random access low complexity |  |  | Low delay low complexity |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.3 | -0.3 | -0.3 |  |  | 
Class B | -0.6 | -0.6 | -0.6 | -0.3 | -0.3 | -0.3
Class C | -0.2 | -0.2 | -0.2 | 0.0 | 0.0 | 0.0
Class D | -0.3 | -0.3 | -0.3 | 0.0 | 0.0 | 0.0
Class E |  |  |  | -2.5 | -2.4 | -2.4
All | -0.4 | -0.4 | -0.4 | -0.6 | -0.6 | -0.6
Enc Time | 99% |  |  | 100% |  | 
Dec Time | 99% |  |  | 98% |  | 

## Slide 7: Low delay low complexity

## Slide 8: Random access low complexity

## Slide 9: Best Result
When large numbers of skip mode
  Such as class E high QP
Up to 7% bits saving
  Vidyo1 and Vidyo4, low delay, low complexity, QP 37

## Slide 10
Thank you!