## Slide 1: A unified design of RQT cbf coding in LCEC
Bin Li, Jizheng Xu, Feng Wu, Houqiang Li
University of Science and Technology of China
Microsoft

## Slide 2: Current design of signaling cbf
For max transform depth = 2, combined coding works well
For max transform depth > 2, combined coding leads to performance loss
#define LCEC_CBP_YUV_ROOT 0
#define QC_BLK_CBP 0
works better when depth > 2

## Slide 3: Possible reason of performance loss
Combined coding, must encode 4 cbfs together
Max depth > 2, in intermediate layers, some blocks will be further split, no need to code cbf here

## Slide 4: Proposed scheme
Only code cbf for blocks that do not split
  Add tables to handle combined coding for 2 blocks, and 3 blocks.
For intra, do not code RQT_CBF_ROOT
A unified design of max transform depth = 2 and > 2
Coding gain without complexity increase

## Slide 5: For max RQT depth = 2 (default)
 | All intra LC |  |  | Random access LC |  |  | Low delay LC |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | 0.0 | -1.0 | -1.0 | 0.0 | -1.1 | -1.2 |  |  | 
Class B | -0.1 | -0.9 | -1.0 | 0.0 | -1.2 | -1.3 | -0.1 | -2.3 | -2.6
Class C | 0.0 | -0.8 | -0.9 | 0.0 | -1.0 | -1.0 | -0.1 | -2.2 | -2.0
Class D | -0.1 | -1.0 | -1.0 | -0.1 | -1.4 | -1.0 | -0.2 | -3.3 | -2.9
Class E | -0.1 | -1.6 | -1.3 |  |  |  | -0.1 | -2.4 | -1.5
All | -0.1 | -1.0 | -1.0 | 0.0 | -1.2 | -1.1 | -0.1 | -2.5 | -2.3
Enc T | 100% |  |  | 100% |  |  | 100% |  | 
Dec T | 101% |  |  | 103% |  |  | 99% |  | 

## Slide 6: For max RQT depth = 3 (default+1)
The anchor is TMuC 0.9, disabling cbf combined coding (better RD performance)
QuadtreeTUMaxDepthInter: 3 QuadtreeTUMaxDepthIntra: 2

## Slide 7: RQT depth=3, not combined coding Vs. proposed method
 | All intra LC |  |  | Random access LC |  |  | Low delay LC |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -1.8 | -1.1 | -0.8 | -1.2 | -1.3 | -1.1 |  |  | 
Class B | -2.0 | -1.2 | -0.9 | -1.3 | -2.4 | -2.1 | -1.1 | -3.7 | -4.1
Class C | -1.5 | -1.0 | -1.0 | -1.0 | -1.9 | -1.6 | -0.9 | -2.8 | -3.0
Class D | -1.3 | -0.9 | -0.9 | -0.9 | -1.9 | -2.0 | -0.9 | -3.5 | -3.9
Class E | -3.2 | -1.3 | -1.7 |  |  |  | -1.6 | -2.4 | -2.1
All | -1.9 | -1.1 | -1.0 | -1.1 | -2.0 | -1.8 | -1.1 | -3.2 | -3.4
Enc T | 100% |  |  | 100% |  |  | 100% |  | 
Dec T | 102% |  |  | 100% |  |  | 100% |  | 

## Slide 8: RQT depth=2 Vs. depth=3
 | All intra LC |  |  | Random access LC |  |  | Low delay LC |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | 0.4 | 0.9 | 0.9 | 0.0 | 0.8 | 0.8 |  |  | 
Class B | 0.0 | 0.7 | 0.7 | -0.4 | 0.9 | 1.0 | -0.7 | 0.6 | 0.7
Class C | -0.1 | 0.3 | 0.4 | -0.5 | 0.4 | 0.6 | -0.8 | 0.4 | 0.4
Class D | -0.1 | 0.3 | 0.2 | -0.5 | 0.5 | 0.2 | -1.1 | 0.5 | 0.1
Class E | 0.3 | 1.7 | 1.5 |  |  |  | -0.1 | 2.6 | 1.7
All | 0.1 | 0.7 | 0.7 | -0.4 | 0.6 | 0.7 | -0.7 | 0.9 | 0.7
Enc T | 111% |  |  | 112% |  |  | 110% |  | 
Dec T | 102% |  |  | 99% |  |  | 100% |  | 

## Slide 9
Thank you!