## Slide 1: HEVC Performance with cascaded coding
R&D
© BBC MMXI
Andrea Gabriellini
David Flynn
Thomas Davies

## Slide 2: Aims
R&D
© BBC MMXI
Cascaded coding affects the performance of video codecs and it is widely used
In broadcasting, compression is typically applied at least in capture and playout
  Other processes will introduce extra compression

## Slide 3: Tests
R&D
© BBC MMXI
We tested HM0.9 on sequences using fairly mild capture and playout compression (visually lossless or near-lossless)
  We compared BD-R gain over JM for pre-compressed and original: we found increased BD-R gain for pre-compressed material
  We also tested ALF-on and off on both sets of material and found that in random access ALF substantially contributes to improved performance for pre-compressed material.

## Slide 4: First Test: HM 0.9 vs JM 16.2
Future Media & Technology
© BBC MMXI
7 HD seqs
HM 0.9
JM 16.2
HDCAM SR
+
AVC-I 100
HM 0.9
JM 16.2
A
C
B
D

## Slide 5: Second Test: HM 0.9 ALF test
Future Media & Technology
© BBC MMXI
7 HD seqs
HM 0.9
ALF=0
HM 0.9
ALF=1
HDCAM SR
+
AVC-I 100
HM 0.9
ALF=0
HM 0.9
ALF=1
A
C
B
D

## Slide 6: The Setup
R&D
© BBC MMXI
Sequences processed by double encoding, HDCAM SR followed by AVC/H.264-I 100
Visually lossless
Sequence | Y-PSNR | Cb-PSNR | Cr-PSNR
Nebuta Festival | 37.431 | 39.749 | 39.733
Steam Train | 43.919 | 48.172 | 49.015
Kimono | 44.980 | 46.824 | 47.660
Parkscene | 41.627 | 43.843 | 44.439
Cactus | 39.491 | 42.363 | 44.154
BasketballDrive | 43.394 | 44.173 | 44.951
BQTerrace | 39.957 | 42.719 | 44.295

## Slide 7: The Setup
R&D
© BBC MMXI
Two encoder configurations used for test:
  Random access high-efficiency
  Low delay high-efficiency
Second test: evaluate performance delta of HM 0.9 with and without ALF with original and processed sequences
JM 16.2 used with CfP configs, except that
  2 references were used for direct comparison with HM configurations
  QPs were adjusted to provide a similar spread of bit rates and PSNR

## Slide 8: The Results
R&D
© BBC MMXI
First Test: HM 0.9 vs JM 16.2
 | Random access |  |  | Low delay |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Original Sequences | -41.5 | -36.8 | -37.6 | -37.0 | -8.0 | -4.1
Processed Sequences | -45.0 | -40.3 | -41.4 | -39.1 | -6.8 | -2.4

## Slide 9: The Results
R&D
© BBC MMXI
Second Test: HM 0.9 ALF versus no-ALF Test
 | Random access |  |  | Low delay |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Original Sequences | -6.7 | -13.9 | -11.7 | -7.6 | -12.4 | -11.2
Processed Sequences | -8.7 | -12.1 | -10.2 | -7.4 | -11.5 | -9.0

## Slide 10: Conclusion
R&D
© BBC MMXI
HM is offering even larger gains on pre-compressed material than for original material: this is good news!
In RA configurations, ALF contributes more than half of this additional gain
We recommend that HM performance is checked on pre-processed material from time to time
We also recommend that individual tools be verified from time to time on pre-compressed material. Tools that provide additional gain on such sequences are especially valuable