## Slide 1: Hardware Friendly Rotational Transform JCTVC-D180 & D222
Xing Wen, Oscar C. Au
Hong Kong Univ of Science & Technology
January, 2011
<number>

## Slide 2: Outline
Introduction of Rotational Transform
  Rotational transform in TMuC
  Hardware implementation
Hardware Friendly ROT (HF-ROT)
  “m-set”and “n-set”transform matrices
Complexity Analysis
  HF-ROT saving about 53% and 35% add operations for forward and inverse transform
  HF-ROT saving about 49% and 60% clock cycles for forward and inverse transform
Simulation results
  BD-rate reduction 3.2%, 2.4%, 1.1%, 1.2% on average for intra HE, intra loco, RA HE, RA loco cases to TMuC 0.9 anchor respectively
<number>
Notes: Ai de..
<number>

## Slide 3: Introduction of Rotational Transform
Rotational transform is a secondary transform applied after DCT transform, the block diagram is shown:
The ROT transfomed block mo can be obtained by following equation:
Where mi is the input residue block, D is DCT matrix, are horizontal ROT and vertical ROT matrices respectively
<number>

## Slide 4: Introduction of Rotational Transform
The matrices Rh and Rv are defined as the following compund Given’s rotation matrix products:
In TMuC 0.9, there are four sets of rotation angles θ1i, θ2i, θ3i, θ4i, θ5i, θ6i (i = 1 to 4) which equals to four sets of Rh and Rv respectively.
<number>

## Slide 5: ROT in TMuC 0.9
In TMuC, four sets of ROT matrics are stored as following forms:
<number>

## Slide 6: Scanning Order
The forward ROT process can be described as follows:
<number>

## Slide 7: Hardware implementation of ROT
<number>

## Slide 8: Hardware implementation of ROT
Irregular Data flow
  For example, at Mode 2, Rv(1, 1) is “111100111111” which needs 10 times shift operation and 9 times add operation, on the other hand, Rv(1, 3) is “1100100010” which only needs 4 times shift operation and 3 times add operations.
  If we assume add and shift operation take one clock cycle each, then we could observe that Rv(1, 3) only take 7 clock cycles while Rv(1, 1) needs 19 clock cycles to finish computation
  the multiplier use Rv(1, 3) must wait the multiplier which take Rv(1, 1) for 19-7=12 clock cycles
<number>

## Slide 9: Hardware Friendly ROT
Step 1: coefficient of original inverse ROT matrices is input to get absolute value, and sign_bit_1 is stored
Step 2: the absolute value is mapping to 2a, and a is rounded to get integer shift_bits_1 and certain quantization offset. The offset can be different for different coefficients.
Step 3: the quantization error is input to the loop again and repeat step 1 and 2, and get sign_bit_2, and shift_bits_2.
Step 4: repeat step 1 and 2 for n times, and then get the “n-set” inverse HF-ROT matrix
Step 5: use inverse of “n-set” inverse HF-ROT matrix as new forward HF-ROT matrix
Step 6: loop step 1 and 2 for m times with new forward HF-ROT matrix and get “m-set” forward HF-ROT matrix
<number>

## Slide 10: Benefits for HF-ROT
There are three benefits for our proposed HF-ROT compared to original ROT.
  All coefficients can be described as following form:
  All coefficients inside transform matrices would require same clock cycle to finish multiplication operations, which result in very regular data flow.
  m and n do not need to be identical, and can be adjust to achieve different trade-off between data throughput and coding gain.
  According to our simulation results, the HF-ROT achieve similar coding gain as original ROT.
<number>

## Slide 11: Complexity Analysis
<number>

## Slide 12: Complexity Analysis
 | Forward Transform | Inverse Transform
ROT | 836 | 600
HF-ROT (m=3 n=3) | 386 | 388
HF-ROT (m=5 n=3) | 582 | 388
<number>
 | Forward Transform | Inverse Transform
ROT | 146 | 100
HF-ROT (m=5 n=3) | 72 | 40
HF-ROT (m=3 n=3) | 40 | 40
Table 1 shows number of add operations for ROT and HF-ROT
  HF-ROT (m=3, n=3) can save about 53% and 35% add operation for forward and inverse transform respectively
Table 2 show clock cycles:
  HF-ROT (m=3, n=3) can save about 72% and 60% clock cycles for forward and inverse transform respectively
  From previous page, we could find it would takes 37+37 clock cycles to finish shift operations in certain mode in fwd, and 37-4+37-4 clock cycles to finish add operations. So total clock cycles should be 146
  HF-ROT: Fwd 4*(4m-2), inv 4*(4n-2)
Table 1: number of add operation
Table 2: number of clock cycles
Notes: 37+37
37-4+37-4
ADD COUNT 30%
CLOCK 51% FOR M=5
<number>

## Slide 13: Simulation results
We have conducted simulation on TMuC 0.9 using the two intra configurations, i.e., high-efficiency and low-complexity, and the two random access configurations from the common coding configurations
Simulation environment:
  OS: Windows 7 Enterprise 64-bit
  CPU: Inter® Core (TM) i7, 2.8GHz
  Memory: 4G or 8G
  Coding times are not precise
<number>
Table 5 Test results: TMuC 0.7 ROT on MDDT off vs TMuC 0.7 ROT off MDDT off.

## Slide 14: Simulation Results of HF-ROT (m=5, n=3) VS TMuC 0.9 anchor
<number>
 | Intra |  |  | Intra LoCo |  | 
 | Y BDR | U BDR | V BDR | Y BDR | U BDR | V BDR
Class A | -2.5 | -0.3 | 0.8 | -3.4 | -0.9 | 0.5
Class B | -1.9 | 0.1 | 0.8 | -2.8 | -0.7 | 0.0
Class C | -2.6 | -0.6 | -0.6 | -3.3 | -1.8 | -1.9
Class D | -2.5 | -0.5 | -0.7 | -3.2 | -1.7 | -2.2
Class E | -2.6 | 3.1 | 1.8 | -3.6 | 3.2 | 1.3
All | -2.4 | 0.3 | 0.3 | -3.2 | -0.5 | -0.7
Enc Time[%] | -- |  |  | -- |  | 
Dec Time[%] | -- |  |  | -- |  | 
 |  | Random access |  |  | Random access LoCo | 
 | Y BDR | U BDR | V BDR | Y BDR | U BDR | V BDR
Class A | -1.1 | 0.1 | 0.9 | -1.3 | -0.3 | 0.5
Class B | -1.0 | 0.2 | 0.6 | -1.2 | -0.4 | 0.0
Class C | -1.3 | -0.6 | -0.5 | -1.3 | -0.9 | -1.1
Class D | -1.1 | -0.4 | -0.3 | -1.0 | -0.6 | -0.7
Class E |  |  |  |  |  | 
All | -1.1 | -0.2 | 0.1 | -1.2 | -0.6 | -0.4
Enc Time[%] | -- |  |  | -- |  | 
Dec Time[%] | -- |  |  | -- |  | 

## Slide 15: Coding gain for ROT
We also tested the original ROT performance on TMuC 0.9 and also submitted as a contribution (JCTVC-D222), and Table shows the BD-Bitrate results for original ROT on TMuC 0.9.
<number>
 | Intra |  |  | Intra LoCo |  | 
 | Y BDR | U BDR | V BDR | Y BDR | U BDR | V BDR
Class A | -2.8 | -0.5 | 0.7 | -3.8 | -1.0 | 0.2
Class B | -2.1 | -0.1 | 0.6 | -3.2 | -1.0 | -0.3
Class C | -2.8 | -0.6 | -0.6 | -3.5 | -1.9 | -2.0
Class D | -2.7 | -0.5 | -0.7 | -3.3 | -1.8 | -2.3
Class E | -2.8 | 3.0 | 1.8 | -3.9 | 3.0 | 1.1
All | -2.6 | 0.2 | 0.2 | -3.5 | -0.7 | -0.8
Enc Time[%] | -- |  |  | -- |  | 
Dec Time[%] | -- |  |  | -- |  | 
 |  | Random access |  |  | Random access LoCo | 
 | Y BDR | U BDR | V BDR | Y BDR | U BDR | V BDR
Class A | -1.2 | 0.0 | 0.8 | -1.5 | -0.3 | 0.4
Class B | -1.1 | -0.1 | 0.5 | -1.3 | -0.4 | -0.2
Class C | -1.3 | -0.6 | -0.6 | -1.4 | -0.9 | -1.0
Class D | -1.1 | -0.1 | -0.2 | -1.1 | -0.6 | -0.9
Class E |  |  |  |  |  | 
All | -1.2 | -0.2 | 0.1 | -1.3 | -0.6 | -0.5
Enc Time[%] | -- |  |  | -- |  | 
Dec Time[%] | -- |  |  | -- |  | 

## Slide 16: Conclusion
Original ROT cannot be easily implemented by hardware. However ROT has a good potential to be modified to be more hardware friendly.
HF-ROT can achieve similar coding gain as original ROT but can be efficiently implemented by hardware.
We suggest adopt HF-ROT into next version HM for further study in CE7 (may combined with some proposals for example: JCTVC-D357).
<number>

## Slide 17: Coding gain for ROT
As described in JCTVC-D357, the ROT was tested in TMuC 0.7 as part of TE12 in Guangzhou meeting (JCVTV-C202 and JCVTV-C036).
<number>
 |  |  | Intra |  |  |  |  |  | Intra-LC |  | 
 | Y |  | U |  | V | Y |  |  | U |  | V
Class A | -2.1 |  | 1.1 |  | 2.0 | -2.4 |  |  | -0.5 |  | -0.1
Class B | -1.9 |  | 0.6 |  | 1.2 | -2.2 |  |  | -1.3 |  | -1.0
Class C | -2.3 |  | 0.0 |  | -0.1 | -2.5 |  |  | -2.0 |  | -2.1
Class D | -2.1 |  | -0.1 |  | -0.2 | -2.2 |  |  | -1.9 |  | -2.1
Class E | -2.4 |  | 3.6 |  | 2.8 | -2.6 |  |  | 0.6 |  | -0.5
All | -2.2 |  | 0.9 |  | 0.9 | -2.3 |  |  | -1.2 |  | -1.3
Enc Time[%] | 242% |  |  |  |  | 259% |  |  |  |  | 
Dec Time[%] | 102% |  |  |  |  | 104% |  |  |  |  | 
 | Random access |  |  |  |  |  | Random access LoCo |  |  |  | 
 | Y | U |  | V |  |  | Y | U |  | V | 
Class A | -0.9 | 0.5 |  | 0.9 |  |  | -1.0 | -0.4 |  | -0.2 | 
Class B | -0.9 | 0.0 |  | 0.4 |  |  | -0.9 | -0.8 |  | -0.9 | 
Class C | -1.0 | -0.5 |  | -0.5 |  |  | -1.0 | -0.7 |  | -0.8 | 
Class D | -0.8 | 0.0 |  | -0.2 |  |  | -0.7 | -0.8 |  | -0.6 | 
Class E |  |  |  |  |  |  |  |  |  |  | 
All | -0.9 | -0.1 |  | 0.1 |  |  | -0.9 | -0.7 |  | -0.7 | 
Enc Time[%] | 105% |  |  |  |  |  | 107% |  |  |  | 
Dec Time[%] | 104% |  |  |  |  |  | 100% |  |  |  | 

## Slide 18: Simulation Results of HF-ROT vs ROT
<number>