## Slide 1: CE6: Report and evaluation of new Combined Intra Prediction settings
R&D
© BBC MMXI
Marta Mrak, Thomas Davies,
David Flynn, Andrea Gabriellini

## Slide 2: Combined Intra Prediction (CIP)
CIP comprises a weighted combination of
  angular prediction
  local mean prediction
local mean prediction
  average of the selected neighbouring pixel values
    encoder: original pixel values
    decoder: reconstructed pixel values
not only open-loop
  weighted combination
  reconstruction process is stable and controls any noise arising from different values available on enc/dec

## Slide 3: CIP: Local prediction
open-loop prediction (OLP)
  prediction from spatially closer values than in angular prediction which uses neighbouring blocks
  selected values are defined by an OLP template
templates for OLP
  depend on available pixels and chosen scan order of pixels within a block
  can be adaptively selected
    e.g. on the angular prediction direction
Current pixel X is predicted from values in "green" positions

## Slide 4: CIP: Implementation
complexity
  encoder: adding more RD search options that include CIP increases complexity and BD-rate gains
  decoder
    tests show almost no influence on the decoding time
    CIP uses averaging of up to 3 neighbouring pixel values and the angular prediction

## Slide 5: CIP: Settings
1) CIP_HC (high complexity CIP)
  uses the most comprehensive RD search, taking into account different angular modes, RQTs and all CU components (Y, UV and related signalling)
  A125, C213
  expected to deliver highest coding gains
2) CIP_MC (medium complexity CIP)
  various trade-offs between higher complexity and higher gain, and lower complexity and lower gain performances
  involves RD search CIP within the current luma PU only
  generally faster since chroma modes, other PUs in the current CU, and other CU components are not reassessed with or without CIP
3) CIP_LC (low complexity CIP)
  CIP by default on selected PUs (under certain block size)
  without increasing the RD search complexity

## Slide 6: Results for Intra coding configurations

## Slide 7: Results for inter configurations
- using high-complexity CIP

## Slide 8: Alternative implementations
0 | 1 | 2 | 3
1 | 2 | 3 | 4
2 | 3 | 4 | 5
3 | 4 | 5 | 6
0 | 0 | 0 | 0
0 | 1 | 1 | 1
0 | 1 | 2 | 2
0 | 1 | 2 | 3
0 | 1 | 2 | 3
4 | 5 | 6 | 7
8 | 9 | 10 | 11
12 | 13 | 14 | 15
N steps
N  N steps
2  N - 1 steps
(for identical result as for N  N steps)
fixed OLP template
adaptive OLP template
(dependant on pixel position)
processing way
OLP direction (template)

## Slide 9: Adaptive template, CIP_LC (results not cross-checked)

## Slide 10: Summary
CIP in intra configurations
  encoding times can vary between 100 % to 200 % depending on the chosen CIP setting
  higher complexity associated to larger BD-rate gains
  BD-rates (Y, U, V) :
    low complexity CIP encoder:
      (-0.3, -2.1, -2.1) for HE
      (-0.7, -2.9, -2.9) for LC
    high complexity CIP encoder
      (-1.5, -3.2, -3.2) for HE
      (-2.5, -2.6, -2.6) for LC
CIP high complexity in inter configurations
  average encoding time increase 1 %
  BD-rates (Y, U, V) :
    RA: (-0.8, -1.1, -0.9) for HE; (-0.7, -1.0, -1.0) for LC
    LD: (-0.1, -0.5, -0.4) for HE; (-0.1, -0.2, -0.2) for LC
alternative implementations indicated