## Slide 1: JCTVC-D219: Unified scan for high efficiency coefficient coding
Thomas Davies

## Slide 2: Summary
Current HHI_TRANSFORM_CODING and Parallel Context Processing methods for coefficient coding have several scanning tools
In addition Adaptive Coefficient Scanning (ACS) has been proposed and provides good gain
Aim of this contribution is to review the various scanning tools and propose a unified core scan which gives a good trade-off between performance and complexity. This removes the separate sub-block level/sign scan and the adaptive diagonal scan
The unified scan provides reduced complexity with an average BD-R loss of 0.2-0.5% for intra, 0.0-0.2% for RA and LD
  2/3 of this loss comes from losing adaptive diagonal scan, 1/3 from losing separate sub-block scan

## Slide 3: Scanning features of current HHI_TRANSFORM_CODING and PCP
significance and last flags are forward-scanned across the whole block using a diagonally-based scan
the diagonal sig/last scan is adapted per diagonal based on upper/lower counts of significant coefficients
level and sign are separately scanned, using a different sub-block-based scan
the level/sign scan is a reverse scan within each sub-block to improve context adaptivity
the level/sign sub-block decoding is split into 2 passes to allow for Parallel Context Processing

## Slide 4: Scanning features of current HHI_TRANSFORM_CODING and PCP
significance and last flags are forward-scanned across the whole block using a diagonally-based scan
the diagonal sig/last scan is adapted per diagonal based on upper/lower counts of significant coefficients
level and sign are separately scanned, using a different sub-block-based scan
the level/sign scan is a reverse scan within each sub-block to improve context adaptivity
the level/sign sub-block decoding is split into 2 passes to allow for Parallel Context Processing

## Slide 5: Complexity issues
Random access into a TU is inefficient
Several passes over the whole TU
Non-deterministic data access with adaptive diagonal scan
Different scan patterns imply different optimum data ordering
  like to work on the most local set of data possible at any one time
  want to take data re-ordering outside of the inner coding loop

## Slide 6: Unified scan
In order of performance, the scanning tools are (gains are for intra):
  Reverse-scanning level data by sub-unit (~0.5%)
  Adaptive diagonal scan (~0.3-0.4%)
  Using sub-blocks for level data, instead of zig-zag (~0.1-0.2% for Intra)
  PCP (no effect)
Unified scan design is chunk-based. It takes the first and last feature but drops the other two:
  Use a basic (e.g. zig-zag) scan, divided into chunks of size <= 16
  Forward scan each chunk for significant/last coefficients, determine significant chunks on the fly
  Reverse-scan each significant chunk for level/sign using PCP

## Slide 7: Unified chunk-based scan

## Slide 8: Summary performance of unified chunk scan
 | Y BD-rate | U BD-rate | V BD-rate
Intra | 0.5 | 0.7 | 0.7
 | Enc Time: 98%, Dec Time 103% |  | 
Random Access | 0.3 | 0.4 | 0.4
 | Enc Time: 101%, Dec Time 104% |  | 
Low Delay | 0.2 | 0.3 | 0.1
 | Enc Time: 99%, Dec Time: 104% |  | 

## Slide 9: Adaptive Coefficient Scan
In addition ACS has been proposed (JCTVC-D360), with 3 basic scans:
  Zig-zag, replacing adaptive diagonal (although this can be enabled)
  Horizontal
  Vertical
Other features of HHI_TRANSFORM_CODING and PCP scanning are preserved (1, 3-5)
ACS is available in 2 modes:
  Signalled: all scanning modes are evaluated, and mode is always signalled
  Optimized: scanning modes are pre-determined for intra 4x4 and 8x8 blocks
Gains of ACS are 1.2%, 0.5%, 0.6% respectively, for Intra, RA and LD
Gains of Optimized ACS are 1.0%, 0.6%, 0.6% for Intra, RA, and LD

## Slide 10: Unified scan + ACS performance
 | ACS |  |  | ACS + Unified scan |  | 
 | BD-R Y | BD-R U | BD-R V | BD-R Y | BD-R U | BD-R V
HE Intra | -1.2 | -1.6 | -1.6 | -1.0 | -1.4 | -1.4
HE Random Access | -0.5 | -0.9 | -0.8 | -0.5 | -0.6 | -0.5
HE Low Delay | -0.6 | -0.9 | -0.9 | -0.5 | -1.0 | -0.9

## Slide 11: Unified scan + Optimized ACS
 | Optimized ACS |  |  | Optimized ACS + Unified scan |  | 
 | BD-R Y | BD-R U | BD-R V | BD-R Y | BD-R U | BD-R V
HE Intra | -1.0 | -1.2 | -1.2 | -0.8 | -0.7 | -0.7
HE Random Access | -0.6 | -0.8 | -0.7 | -0.5 | -0.3 | -0.3
HE Low Delay | -0.6 | -0.9 | -0.8 | -0.5 | -0.8 | -0.8