## Slide 1
<number>
<number>
JCT-VC D221
Loop Filter with Directional Similarity Mapping
4th JCT-VC Meeting, Jan. 2011
PoLin Lai
Felix C. Fernandes Samsung Electronics Co., Ltd
Notes: <number>
겉표지 ( 타이틀 : Tahoma 46, Date : Arial 24 )

## Slide 2: Outline
<number>
Introduction: ALF in TMuC 0.9
Loop filter with directional similarity mapping
Preliminary simulation results
Conclusions
Notes: Characteristics of ALF in TMuC
<number>

## Slide 3: ALF in TMuC 0.9
<number>
Multi-pass approach
  Determine CU synchronous on/off control map. Compute filter coefficients for the selected blocks
  Reduce encoding passes: C082, C113, C143
Worst case 16 filters, 9x9 diamond shape
Observed issues in edge preserving and
ringing artifacts
BasketballDrill, QP 37
Notes: <number>

## Slide 4: Filter design with directional similarity mapping
<number>
Goals
  Reduce computational complexity & memory bandwidth  Use only 4 filters
   Worst case 7x7d size
  Improve visual quality around edge Exploit edge directionality
Combination of
  Linear spatial filter, hor / ver symmetric constraints
  Filter with simplified similarity mapping, directional constraints
  Simplified and enhanced version of [Liu et al., M17171, ICME 2010]
Algorithm highlights
  Pixel adaptation based on direction of local gradients
  Filter design considering directional feature and similarity
  Similarity mapping using simple hard-thresholding (no sorting)
Notes: *Eliminated sorting
<number>

## Slide 5: 1. Pixel adaptation
<number>
For pixel X(i,j), 4 directions: hor, ver, 45o down, 45o up
Assign pixel to Directional Class
  min_g(i,j) = min{ grad_h(i,j), grad_v(i,j), grad_d(i,j), grad_u(i,j) }
  D(i,j) = 0 if min_g(i,j) = grad_h(i,j)
  D(i,j) = 1 if min_g(i,j) = grad_v(i,j)
  D(i,j) = 2 if min_g(i,j) = grad_d(i,j)
  D(i,j) = 3 if min_g(i,j) = grad_u(i,j)
Notes: <number>

## Slide 6: 1. Pixel adaptation - Example
<number>
Dominant edge / feature directions
Blowingbubble
Notes: <number>

## Slide 7: 2. Filter design: f_h(ak,bk) and f_v(ak,bk)
<number>
Combining spatial and directional parts (7x7d example)
f_h a0~a9: spatial linear part b0~b14: Directional filter 25 coeff
f_v a0~a9: spatial linear part b0~b14: Directional filter 25 coeff
Notes: Sym prevent filtering across edges
<number>

## Slide 8: 2. Filter design: f_d(ak,bk) and f_u(ak,bk)
<number>
Combining spatial and directional parts (7x7d example)
f_d a0~a9: spatial linear part b0~b12: Directional filter 23 coeff
f_u a0~a9: spatial linear part b0~b12: Directional filter 23 coeff
Notes: <number>

## Slide 9: 3. Similarity mapping in directional filter
<number>
Goal of combined filter design
  Linear spatial filter  Bias filter toward neighbors
  Directional filter  Bias filter along edge, not across edge
Similarity mapping with hard-thresholding:
  Preserve edges by not using pixels too different from X(i,j)
For X(i,j) to be filtered, map its neighboring pixels Xn to Xn’:
XN’ = XN if | XN - X(i,j) | ≤ σ/2
= X(i,j) if | XN - X(i,j) | > σ/2
Xn
Xn’
X(i,j)
X(i,j)
X(i,j) + σ/2
X(i,j) - σ/2
Notes: <number>

## Slide 10: 3. Similarity mapping in directional filter
<number>
Goal of combined filter design
  Linear spatial filter  Bias filter toward neighbors
  Directional filter  Bias filter along edge, not across edge
Similarity mapping with hard-thresholding:
  Preserve edges by not using pixels too different from X(i,j)
For X(i,j) to be filtered, map its neighboring pixels Xn to Xn’:
XN’ = XN if | XN - X(i,j) | ≤ σ/2
= X(i,j) if | XN - X(i,j) | > σ/2
Pixels XN’ after mapping are used to calculate filter coefficients bk
Meanwhile, values XN are used to calculate filter coefficients ak
Notes: <number>

## Slide 11: Simulation results (against TMuC 0.9 with ALF = 0)
<number>
 |  | Intra HE |  |  |  |  | RA HE | 
 |  | ALF | DSM |  | ALF |  | DSM | 
Class A | Traffic | -5.3 | -5.7 |  | -4.2 |  | -3.8 | 
 | PeopleOnStreet | -6.7 | -7.0 |  | -7.5 |  | -7.3 | 
Class B | Kimono | -3.4 | -2.7 |  | -3.4 |  | -1.9 | 
 | ParkScene | -3.5 | -3.4 |  | -2.6 |  | -1.3 | 
 | Cactus | -3.6 | -3.6 |  | -5.4 |  | -2.9 | 
 | BasketballDrive | -2.6 | -2.5 |  | -5.4 |  | -5.0 | 
 | BQTerrace | -2.3 | -2.4 |  | -14.1 |  | -13.2 | 
Class C | BasketballDrill | -4.2 | -4.9 |  | -2.9 |  | -1.4 | 
 | BQMall | -2.6 | -3.2 |  | -2.5 |  | -2.3 | 
 | PartyScene | -1.0 | -1.6 |  | -1.9 |  | -1.3 | 
 | RaceHorses | -3.6 | -3.7 |  | -4.5 |  | -4.5 | 
Class D | BasketballPass | -1.5 | -1.5 |  | -1.1 |  | -0.5 | 
 | BQSquare | -0.5 | -1.4 |  | -3.0 |  | -1.0 | 
 | BlowingBubbles | -0.9 | -1.4 |  | -0.7 |  | -0.2 | 
 | RaceHorses | -3.8 | -3.9 |  | -2.7 |  | -2.5 | 
Class E | Vidyo1 | -5.4 | -5.5 |  |  |  |  | 
 | Vidyo3 | -4.7 | -5.1 |  |  |  |  | 
 | Vidyo4 | -4.1 | -4.1 |  |  |  |  | 
 | Class A | -6.0 | -6.3 |  | -5.9 |  | -5.6 | 
 | Class B | -3.1 | -2.9 |  | -6.2 |  | -4.9 | 
 | Class C | -2.8 | -3.4 |  | -3.0 |  | -2.4 | 
 | Class D | -1.6 | -2.1 |  | -1.9 |  | -1.0 | 
 | Class E | -4.7 | -4.9 |  |  |  |  | 
 |  | -3.3 | -3.5 |  | -4.1 |  | -3.3 | 
 | Encoding time | 134% | 118% |  | 108% |  | 109% | 
No control map used yet
Notes: <number>

## Slide 12: Visual quality improvements 1: Intra
<number>
Basketballdrill, QP 37
ALF
ALF
ALF
DSM
DSM
DSM
Notes: <number>

## Slide 13: Visual quality improvements 2: RA
<number>
Original ALF QP 32 DSM QP 32
Notes: <number>

## Slide 14: Visual quality improvements 2: RA
<number>
Original ALF QP 32 DSM QP 32
Notes: <number>

## Slide 15: Conclusions
<number>
Benefits
  Reduce computational complexity & memory bandwidth  Use only 4 filters
   Worst case 7x7d size
  Improve visual quality around edge Exploit edge directionality
Features
  Pixel adaptation based on direction of local gradients
  Combine linear spatial filter and directional similarity filter
  Mapping to avoid filter across edges
CE plans
  Loop filter with DSM:
  Reduce coefficients from 7x7d to 5x5d
  Incorporate with CU synchronous control map
Notes: <number>

## Slide 16: Filter design 5x5 diamond
<number>
f_h: a0~a5 and b0~b7, 14 coeff f_v: a0~a5 and b0~b7, 14 coeff
f_d: a0~a5 and b0~b6, 13 coeff f_u: a0~a5 and b0~b6, 13 coeff
Notes: Sym prevent filtering across edges
<number>