## Slide 1: JCTVC-D223
CE4:
Interpolation filtering of chroma samples using two
stage averaging
Arild Fuldseth
Gisle Bjøntegaard
Cisco

## Slide 2: Summary
Two-stage averaging filter
Lower complexity than AVC chroma interpolation filter
0.3% - 1.2% BD-Rate loss
0.12 dB – 0.26 dB decrease in chroma PSNR

## Slide 3: Description
Based on JCTVC-A119 (TENTM)
Rounding chroma motion vectors from 1/8 to 1/4 sample resolution
Half sample positions:
  X = (A+B)>>1
Quarter sample positions:
  X = (((A+B)>>1) + ((C+D)>>1) + 1)>>1

## Slide 4: Example – (1/4,1/4) position
A a b c B d e f g h i j k l m n o C D
b = (A+B)>>1
h = (A+C)>>1
e = (b+h+1)>>1

## Slide 5: Complexity analysis
No multiplications
No calculation of weights
At most 3 averaging operations per sample
Suitable for SIMD implementations: Typically 4, 8, or 16 samples simultaneously

## Slide 6: Results – random access
 | High efficiency |  |  |  | Low complexity |  |  | 
 | Y | U | V | YUV | Y | U | V | YUV
Class A | 0,4 | 7,4 | 6,7 | 2,7 | 0,3 | 6,0 | 5,9 | 2,1
Class B | 0,2 | 11,6 | 11,0 | 3,1 | 0,2 | 8,0 | 10,6 | 2,4
Class C | 0,4 | 7,3 | 8,3 | 3,0 | 0,3 | 4,7 | 4,6 | 1,7
Class D | 0,3 | 9,3 | 11,4 | 2,9 | 0,3 | 6,8 | 6,9 | 1,8
Class E |  |  |  |  |  |  |  | 
All | 0,3 | 9,3 | 9,8 | 3,0 | 0,3 | 6,5 | 7,4 | 2,0
Enc Time[%] | 100 % |  |  |  | 99 % |  |  | 
Dec Time[%] | 100 % |  |  |  | 97 % |  |  | 

## Slide 7: Results – low delay
 | High efficiency |  |  |  | Low complexity |  |  | 
 | Y | U | V | YUV | Y | U | V | YUV
Class A |  |  |  |  |  |  |  | 
Class B | 1,0 | 12,2 | 15,0 | 4,5 | 0,7 | 8,4 | 10,8 | 3,2
Class C | 1,4 | 8,1 | 8,9 | 4,3 | 0,8 | 5,1 | 5,0 | 2,4
Class D | 1,6 | 12,6 | 12,0 | 4,2 | 0,9 | 6,7 | 5,8 | 2,4
Class E | 0,6 | 17,1 | 20,9 | 6,4 | 0,4 | 16,2 | 22,2 | 5,0
All | 1,2 | 12,2 | 13,8 | 4,8 | 0,7 | 8,6 | 10,3 | 3,1
Enc Time[%] | 100 % |  |  |  | 100 % |  |  | 
Dec Time[%] | 98 % |  |  |  | 98 % |  |  | 

## Slide 8: Chroma PSNR
dPSNR = PSNRanchor – PSNRtest (average over all seqeunce/QP combinations)
Test case | BD-Rate Y | dPSNR-U | dPSNR-V
Random access HE | 0,3% | -0,16 dB | -0,19 dB
Random access LC | 0,3% | -0,12 dB | -0,13 dB
Low delay HE | 1,2% | -0,22 dB | -0,26 dB
Low delay LC | 0,7% | -0,16 dB | -0,20 dB

## Slide 9: Conclusion
Low complexity two-stage averaging filter
Suitable for SIMD architectures
0.3% - 1.2% BD-Rate loss (luma)
0.12 dB – 0.26 dB decrease in chroma PSNR