## Slide 1: JCTVC-D224
Unified transform design for HEVC with 16 bit intermediate data representation
Arild Fuldseth
Gisle Bjøntegaard
Cisco

## Slide 2: Summary
Unified transform design for HEVC (4x4,...,32x32)
16-bit intermediate storage (IBDI off, TPE=0)
Almost equal norm for all basis vectors
Matrix multiplication or partial butterfly implementation
BD-Rate gains: 0.1% - 0.6%
    Anchor: TPE=4
    Proposed: TPE=0

## Slide 3: Unified design
HM1.0 transforms:
    4x4 and 8x8: Same as AVC
    16x16 & 32x32: Based on Chen algorithm (DCT)
Proposed transforms:
    Unified design for all transform sizes
    Reuse of logic for smaller transform sizes

## Slide 4: Examples
4x4 transform: {64, 64, 64, 64} {83, 36,-36,-83} {64,-64,-64, 64} {36,-83, 83,-36}
8x8 transform:
{64, 64, 64, 64, 64, 64, 64, 64}
{89, 75, 50, 18,-18,-50,-75,-89}
{83, 36,-36,-83,-83,-36, 36, 83}
{75,-18,-89,-50, 50, 89, 18,-75}
{64,-64,-64, 64, 64,-64,-64, 64}
{50,-89, 18, 75,-75,-18, 89,-50}
{36,-83, 83,-36,-36, 83,-83, 36}
{18,-50, 75,-89, 89,-75, 50,-18}

## Slide 5: 16 bit intermediate storage (8 bit input)
HM1.0 transforms: >= 20 bit + 4 TPE bits
Proposed transforms: <= 16 bit
T1
T2
Q
IQ
IT1
IT2
9
16
16
16
16

## Slide 6: 16 bit vs. 16+ bit
 | Bytes/coefficient | SIMD efficiency
16 bit | 2 | N/2
16+ bit | 4 | N/4

## Slide 7: Proposed basis vectors
Basis vectors are almost orthogonal
Basis vectors have almost equal norm
Simplifies quantization/dequantization
No quantization/dequantization matrices

## Slide 8: Matrix multiplication or ”butterfly”
Identical results
Matrix multiplication:
    Straightforward
    Few code lines
    No cascading
    Very SIMD friendly
Partial ”butterfly” implementation:
    Utilizes symmetry/anitsymmetry properties of basis vectors
    Less multiplications/additions
    Increased number of codelines
    Cascading

## Slide 9: Matrix multiplication
for (i=0; i<uiTrSize; i++)
{
for (j=0; j<uiPartialSize; j++)
{
iSum = 0;
for (k=0; k<uiPartialSize; k++)
{
iSum += iIT[uiTrSize*k+i]*plCoef[k*uiTrSize+j];
}
tmp[i][j] = (iSum+32)>>6;
}
}
for (i=0; i<uiTrSize; i++)
{
for (j=0; j<uiTrSize; j++)
{
iSum = 0;
for (k=0; k<uiPartialSize; k++)
{
iSum += iIT[uiTrSize*k+j]*tmp[i][k];
}
pResidual[i*uiStride+j] = (iSum+4096)>>13;
}
}

## Slide 10: Other useful properties
8 bit representation of transform coefficients.
Bit width of accumulators for matrix multiplication: <= 32 bit.
Same symmetry properties as the DCT transform.
Scaled transform coefficients are very close to the DCT transform.
Same quantization/dequantization scheme for all transform sizes

## Slide 11: Intermediate scaling
Forward transform:
    First stage: >>(log2(N)-1)
    Second stage: >>(log2(N)+6)
Inverse transform:
    First stage: >>6
    Second stage: >>13

## Slide 12: Quantization/dequantization
Quantization:
level = (coeff*Q + offset)>>(22 + QP/6 – log2(N))
Dequantization:
  coeffQ = (level*IQ << (QP/6) + 2N)>>(log2(N)) +1)
Same scheme for all transform sizes, N.
No quantization matrices needed.
Q and IQ are equal for all transform coefficients

## Slide 13: Summary
Feature | HM1.0 | Proposed
Unified design | No | Yes
Bit width (IBDI=off) | >20 + TPE | 16
Equal norm | No | Almost
(De)quantization matrices | Yes | No
Matrix multiplication possible | No | Yes
TPE value in simulations | 4 | 0
Unified quantization scheme | No | Yes
Butterfly | Full | Partial

## Slide 14: BD-rate results
Simulation conditions:
    Anchor: TPE=4
    Proposed: TPE=0
Small but consistent gains over existing transforms
 | High efficiency | Low complexity
Intra | -0,2% | -0,6%
Random access | -0,1% | -0,2%
Low delay | -0,1% | -0,1%

## Slide 15: Conclusion
Unified transform design for HEVC
Several advantages for efficient implementation
Small but consistent BDR gain
Proposal: To consider for adoption in HM