## Slide 1: JCTVC-D226
Reducing the table sizes for LCEC
Arild Fuldseth
Cisco

## Slide 2: Summary
Table size for last_pos_and_one syntax element:
    Current size: 1120 bytes
    New size: 352 bytes
BDR loss:
    Intra: 0.7%
    Random acess: 0.2%
    Low delay: 0.1%

## Slide 3: Coefficient coding by LCEC
Joint coding of last significant postion and level
    last_pos_level_one (last significant possition & level>1)
    if (Ievel > 1)
      level-2
    sign
Run mode
Level mode

## Slide 4: last_pos_level_one
Lookup in adaptive ranking table
Map to binary codeword
Table size for 8x8 block: 2*8*8 = 128 bytes
Table size for 4x4 block 2*4*4 = 32 bytes

## Slide 5: HM1.0
4x4 blocks (32 bytes each):
  Intra blocks
  Inter blocks in P slices
  Inter blocks in B slices
8x8 blocks (128 bytes each):
  U
  V
  Y, intra blocks, 8x8 transform
  Y, inter blocks in P slices, 8x8 transform
  Y, inter blocks in B slices, 8x8 transform
  Y, intra blocks, >8x8 partial transform
  Y, inter blocks in P slices, >8x8 partial transform
  Y, inter blocks in B slices, >8x8 partial transform

## Slide 6: Reduced table sizes
4x4 blocks (32 bytes each):
    U, V
    Y, intra blocks
    Y, inter blocks
8x8 blocks (128 bytes each):
    U, V
    Y

## Slide 7: BD-rate results
 | Intra | Random Access | Low Delay
Class A | 1,3 | 0,5 | 
Class B | 1,1 | 0,5 | 0,3
Class C | 0,2 | 0,1 | 0,0
Class D | 0,2 | 0,0 | -0,1
Class E | 0,7 |  | 0,3
Average | 0,7 | 0,2 | 0,1

## Slide 8: Conclusion
Significant reduction in table sizes for last_pos_level_one
Small coding loss
Encourages further studies