## Slide 1: JCTVC-D227
Replacing slices with tiles for high level parallelism
Arild Fuldseth
Cisco

## Slide 2: Summary
AVC:
    Packetization: slices
    Parallel processing: slices
Proposal for HEVC:
    Packetization: slices
    Parallel processing: tiles

## Slide 3: Architecture
Multiple processing cores
Typical number of cores: 2-100
Shared memory (for e.g reference frames)

## Slide 4: Slices and slice groups (FMO)
Some undesired properties for parallel processing:
    Slice header overhead
    Dependency on raster scan order

## Slide 5: Slices vs. tiles
Slices
Tiles

## Slide 6: Tiles
Rectangular shape
Fixed number of LCUs per tile
Width and height are signaled in the SPS or in the PPS
Same dependency breaks as for slices
Tiles do not alter the raster-scan transmission order
Tiles can co-exist with slices in the same frame
Tiles are optional on the encoder side
Marginal impact on decoder (additional dependency breaks)

## Slide 7: Advantages of tiles over slices
No overhead due to slice headers
More flexibility in frame partitioning
Partitioning is independent of the raster-scan order
Support for independent mechanisms for frame partitioning:
  packetization needs
  parallelization needs

## Slide 8: Vertical dependency breaks
Vertical boundaries tend to be shorter than horizontal boundaries (e.g. 16:9 aspect ratio)
Reduced delay: N cores can start working on a new row as it arrives from camera
Finer grained parallelism and load balancing

## Slide 9: Advantages of tiles for single-core
Decoupling encoding and packetization in (alomost) fixed-sized packets
Flexibility to do ”stiching” in compressed domain
Reduced memory bandwidth by processing in smaller widths

## Slide 10: Slices, slice groups (FMO), and tiles
Feature | Tiles | Slices | Slice groups
Slice header | No | Yes | Yes
Raster scan order within the picture | Yes | Yes | No
Dependency breaks at column boundaries | Yes | No | Yes
Maximum umber of partitions supported | >8 | >8 | 8

## Slide 11: Experiment
Software: 0.9-ahg-slices
Configuration: One slice per LCU row
Two modes:
    Slice mode: Slice header for all slices
    Tile mode: Slice header only for the first slice

## Slide 12: BD-rate results
 | Slice mode |  |  | Tile mode |  | 
Sequence | BDR | BDR-low | BDR-high | BDR | BDR-low | BDR-high
class D average | 3,9 | 6,1 | 2,4 | 2,7 | 3,6 | 2,0
class C average | 4,5 | 6,6 | 2,8 | 3,3 | 4,4 | 2,4
class B average | 5,3 | 7,6 | 3,5 | 4,0 | 5,1 | 3,2
class E average | 13,4 | 21,6 | 6,1 | 6,3 | 9,1 | 3,6
Average | 6,2 | 9,6 | 3,6 | 3,9 | 5,3 | 2,8
Slice mode and tile mode vs. anchor:

## Slide 13: BD-rate results
Slice mode vs. tile mode:
Sequence | BDR | BDR-low | BDR-high
class D average | -1,2 | -2,3 | -0,4
class C average | -1,1 | -2,1 | -0,4
class B average | -1,2 | -2,3 | -0,4
class E average | -6,3 | -10,3 | -2,4
Average | -2,1 | -3,8 | -0,8

## Slide 14: Conclusion
Tiles as an alternative to slices for high level parallelism
Significant gain by eliminating slice headers
Propose to study tiles in coordination with other proposals for parallel processing