## Slide 1: Random Access for HEVC
JCTVC-D234 / m18994
A. Fujibayashi & TK Tan
NTT DOCOMO, Inc

## Slide 2: Summary
Introduction
  Random access is not implemented in HM0.9
Solutions
  Instantaneous Decoding Refresh (IDR)
  Deferred Decoding Refresh (DDR)
Results
  IDR increases the BD-rate by 6.7% and 5.8% for HE and LC, respectively
  DDR increases the BD-rate by 1.9% and 1.1% for HE and LC, respectively
  DDR vs. IDR gives a BD-rate improvements of 4.4% for both HE and LC.
Conclusions
  Proposes to adopt IDR and DDR and use DDR as the default configuration for the random access common conditions.

## Slide 3: Random access example in HM0.9
The HM0.9 only inserts Intra pictures at 1.1s intervals for the random access configurations.
There is no support for clean random access as the reference buffer is not refreshed.
Decoder usually crashes after decoding several pictures when starting from these Intra pictures at 1.1s intervals.
Random Access
High Efficiency
QP = 22
Random access into I frame at POC 64
23rd frame after
random access point
Decoder crashes after that

## Slide 4: Reason for this problem
When random accessing into the current GOP, reference pictures from the previous GOP are not available and therefore will cause decoding error.
We need to refresh the reference memory so that pictures that are not available in a random access situation are not used as reference.

## Slide 5: Solution 1: Instantaneous Decoding Refresh (IDR)
IDR pictures are inserted at 1.1s intervals instead of I pictures.
Reference memory refresh point is at the IDR picture.
  Reference to pictures from the previous GOP are disallowed therefore providing a clean random access point.
Coding efficiency suffers due to the closed GOP nature.
Useful for splicing and bit stream editing
Refresh
Refresh

## Slide 6: Solution 2: Deferred Decoding Refresh (DDR)
DDR pictures are inserted at 1.1s intervals instead of I pictures.
Reference memory refresh point is deferred to the first picture after the DDR picture in output order.
Coding efficiency is better than using IDR pictures.
Useful for higher efficiency random access for storage and video on demand.
Refresh
defer

## Slide 7: Results
Table 1: Summary results of BD-Rate comparing HM0.9 IDR to HM0.9 default
HM0.9 IDR vs. HM0.9 default |  |  |  |  |  | 
 | Random access |  |  | Random access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 7.8 | 10.3 | 9.8 | 7.1 | 7.4 | 7.4
Class B | 8.6 | 13.0 | 13.0 | 7.4 | 8.1 | 7.3
Class C | 5.4 | 6.1 | 6.5 | 4.6 | 4.9 | 5.0
Class D | 5.0 | 5.9 | 6.3 | 4.2 | 4.5 | 4.7
Class E |  |  |  |  |  | 
All | 6.7 | 8.9 | 9.0 | 5.8 | 6.2 | 6.0
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 101% |  |  | 100% |  | 
Table 4: Summary results of BD-Rate comparing HM0.9 DDR to HM0.9 default
HM0.9 DDR vs. HM0.9 default |  |  |  |  |  | 
 | Random access |  |  | Random access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 2.9 | 4.2 | 4.1 | 2.3 | 1.9 | 2.1
Class B | 2.7 | 5.6 | 6.2 | 1.7 | 1.8 | 1.5
Class C | 1.4 | 1.6 | 1.9 | 0.7 | 0.5 | 0.5
Class D | 1.0 | 1.7 | 2.0 | 0.3 | 0.2 | 0.4
Class E |  |  |  |  |  | 
All | 1.9 | 3.3 | 3.6 | 1.1 | 1.0 | 1.0
Enc Time[%] | 98% |  |  | 98% |  | 
Dec Time[%] | 100% |  |  | 101% |  | 

## Slide 8: Results (con’t)
Table 3: Summary results of BD-Rate comparing HM0.9 DDR to HM0.9 IDR
HM0.9 DDR vs. HM0.9 IDR |  |  |  |  |  | 
 | Random access |  |  | Random access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -4.4 | -5.4 | -5.1 | -4.5 | -5.1 | -4.9
Class B | -5.4 | -6.5 | -6.0 | -5.3 | -5.8 | -5.4
Class C | -3.8 | -4.3 | -4.3 | -3.8 | -4.2 | -4.3
Class D | -3.8 | -3.9 | -4.0 | -3.7 | -4.2 | -4.2
Class E |  |  |  |  |  | 
All | -4.4 | -5.1 | -4.9 | -4.4 | -4.8 | -4.7
Enc Time[%] | 98% |  |  | 98% |  | 
Dec Time[%] | 99% |  |  | 101% |  | 

## Slide 9: HM0.9 with I pictures
(Recap)

## Slide 10: HM0.9 with DDR pictures

## Slide 11: Conclusions
Current HM0.9 software does not produce bit streams that can be decoded from random access points within it.
Two methods for creating bit streams with random access support were implemented into the HM0.9 software.
  The first method inserts IDR pictures.
  The second method inserts DDR pictures. (similar to Alpha Anchor)
Inserting DDR vs. IDR pictures results in a 4.4% BD-rate improvement for both the high efficiency and low complexity test conducted.
This contribution proposes that
  Both IDR and DDR NAL unit types be supported in the HEVC.
  This capability be implemented in the HM software.
  The preferred default random access configuration for core experiments should be the DDR method.
  Suggested definition:
    deferred decoding refresh (DDR) picture: A coded picture containing only slices with I slice types that causes the decoding process to mark all reference pictures except the current DDR picture as "unused for reference" immediately before the decoding of the first picture following the current DDR with an output order greater than the current DDR picture. All coded pictures that follow a DDR picture in output order can be decoded without inter prediction from any picture that precedes the DDR picture in output order. All coded pictures with output order smaller than the current DDR are not affected by the deferred marking process.
Thanks to Samsung for cross checking the proposal (JCTVC-D265)