## Slide 1: Enhancements to Intra Coding
JCTVC-D235 / m18995
Sandeep Kanumuri, TK Tan and Frank Bossen
DOCOMO USA Labs & NTT DOCOMO, Inc.

## Slide 2: Summary
Proposed enhancements to Intra coding
  Addition of a non-directional mode
    Planar+DST mode
    No need to implement new transforms or quantization matrices
      DST supported using existing implementation of DCT
  Improved Intra Mode Coding
    Signal the most probable mode from up to 2 candidates
Coding Efficiency (Y BD-rate)
  High-Efficiency (HE): -2.1% (Intra), -1.1% (RA), -0.3% (LD)
  Low-Complexity (LD): -2.4% (Intra), -1.0% (RA), -0.3% (LD)
Encoder/Decoder run-times
  Small increase for Intra coding condition
    Encoder: 107% (HE), 111% (LC)
    Decoder: 102% (HE), 105% (LC)
  Impact is not significant for RA and LD coding conditions

## Slide 3: Planar+DST – Comparison to Planar
Value of Z is coded
Residual is NOT coded
T
L
Z
Interpolation indicated by dashed arrow
Value of Z is NOT coded
Z = (L + T) >> 1
Residual is coded using DST
Pixels being predicted
Pixels already reconstructed
Planar
Planar+DST
 | Planar | Planar+DST
Bottom-right pixel value (Z) | Coded | Not Coded
Residual | Not Coded | Coded using DST*
DST* = DST (NxN) – part of DCT (2Nx2N) when N <=16
DST* = DCT (NxN) when N = 32 (largest transform size in HM)
No need to implement new transforms or quantization tables

## Slide 4: Simpler Prediction using Planar+DST
No need for Bi-linear interpolation
Computation using additions and shifts
  No need for multiplications or divisions
  1 additions and 1 shift for each row and each column
  3 additions and 1 shift for each pixel
+
>> 1
T
L
T
T
L
L
Interpolation indicated by dashed arrow
Replication indicated by dotted arrow

## Slide 5: Improved Intra Mode Coding
Large number of intra modes in HM
  Low probability of match between most probable mode and current intra prediction mode
  Increased cost of signaling the remainder mode
Use up to 2 candidates for the most probable mode
  Intra prediction mode for Above Partition (If available)
  Intra prediction mode for Left Partition (If available)
Place the available candidates in ascending order
Signal the candidate (when 2 candidates are available)

## Slide 6: Comparison to HM V0.9 (Intra coding)
High-Efficiency | Y BD-rate | U BD-rate | V BD-rate | Enc Time | Dec Time
CABAC Bug fix | -0.2 | -0.2 | -0.2 | 99% | 100%
Bug fix + Proposal | -2.3 | -1.5 | -1.2 | 107% | 102%
Low-Complexity | Y BD-rate | U BD-rate | V BD-rate | Enc Time | Dec Time
CABAC Bug fix | 0.0 | 0.0 | 0.0 | 99% | 100%
Bug fix + Proposal | -2.4 | -2.4 | -2.3 | 111% | 105%
  CABAC Bug (Computation of RD cost in the encoder): Probability estimate used is different for different modes

## Slide 7: Comparison to HM V0.9 (Random-Access)
High-Efficiency | Y BD-rate | U BD-rate | V BD-rate | Enc Time | Dec Time
CABAC Bug fix | -0.1 | -0.1 | 0.0 | 100% | 100%
Bug fix + Proposal | -1.2 | -1.2 | -0.8 | 100% | 101%
Low-Complexity | Y BD-rate | U BD-rate | V BD-rate | Enc Time | Dec Time
CABAC Bug fix | 0.0 | 0.0 | 0.0 | 101% | 100%
Bug fix + Proposal | -1.0 | -0.5 | -0.3 | 101% | 101%

## Slide 8: Comparison to HM V0.9 (Low-Delay)
High-Efficiency | Y BD-rate | U BD-rate | V BD-rate | Enc Time | Dec Time
CABAC Bug fix | -0.1 | -0.1 | 0.0 | 100% | 100%
Bug fix + Proposal | -0.4 | -0.3 | -0.3 | 100% | 100%
Low-Complexity | Y BD-rate | U BD-rate | V BD-rate | Enc Time | Dec Time
CABAC Bug fix | 0.0 | 0.0 | 0.0 | 101% | 100%
Bug fix + Proposal | -0.3 | -0.2 | -0.2 | 101% | 102%

## Slide 9: Conclusion
JCTVC-D235 proposes two enhancements to intra coding
  Planar+DST mode
  Improved Intra Mode Coding
Strong gain in coding efficiency with minimal impact on complexity
Recommend the adoption of JCTVC-D235 into HM
Thanks to Nokia (JCTVC-D201) for doing the cross-check

## Slide 10: Additional Information

## Slide 11: Comparison to HM V0.9 (Intra coding)
High-Efficiency | Y BD-rate | U BD-rate | V BD-rate | Enc Time | Dec Time
CABAC Bug fix | -0.2 | -0.2 | -0.2 | 99% | 100%
Bug fix + Planar+DCT | -1.1 | -0.6 | -0.5 | 105% | 102%
Bug fix + Planar+DST | -1.5 | -0.7 | -0.4 | 106% | 102%
Bug fix + Proposal | -2.3 | -1.5 | -1.2 | 107% | 102%
Low-Complexity | Y BD-rate | U BD-rate | V BD-rate | Enc Time | Dec Time
CABAC Bug fix | 0.0 | 0.0 | 0.0 | 99% | 100%
Bug fix + Planar+DCT | -0.9 | -1.0 | -0.9 | 109% | 104%
Bug fix + Planar+DST | -1.6 | -1.8 | -1.7 | 110% | 104%
Bug fix + Proposal | -2.4 | -2.4 | -2.3 | 111% | 105%
  CABAC Bug (Computation of RD cost in the encoder): Probability estimate used is different for different modes