## Slide 1: JCTVC-D250
Efficient TU representation
Krit Panusopone, Xue Fang, Limin Wang

## Slide 2: TMuC Residual Quadtree (RQT) Inter Coding
QT for TU representation
RQT is applied to each CU
Leaf of QT becomes TU
RQT defined by 4 parameters; CU size, max TU size, min TU size, max RQT depth
Allow flexible representation for TU
TU split flag required for each RQT node (except node for min TU size)

## Slide 3: TMuC Residual Quadtree (RQT) Issues
No relationship between TU and PU
Suboptimal to allow TU larger than PU, minimal correlation across PU boundaries, but strong blocking artifact
Costly to implement in encoder with full RD mode decision
Increase complexity at decoder

## Slide 4: Proposed method
Improve trade-off between coding efficiency and complexity
Fix TU size, TU size links to PU size
TU size equals PU size for a square (2Nx2N, NxN) PU
2 NxN TUs are selected for a non square (2NxN, Nx2N) PU
No overhead for TU representation
Less complex encoder, no TU mode decision

## Slide 5: TU partitioning in relation to CU and PU
an LCTB and its CU
PU choice of a CU
TU given a PU

## Slide 6: Experimental Results configuration settings
Implemented in TMuC 0.9
Anchor using common test condition
TU size ranges from 32x32 to 4x4, similar to common test condition
No change in intra coding

## Slide 7: Experimental results

## Slide 8: Conclusions
Current RQT syntax and mode decision operation is suboptimal
Implicit TU representation improves coding efficiency and complexity trade-off
TU size cannot be larger than PU size
TU size is predetermined for any given PU size
No QT overhead and no TU mode decision operation
Experimental results show complexity reduction in encoder (~20-30%) and (~5-10%) in decoder with slight coding efficiency loss
Core experiment on TU representation should be set up to determine efficient TU representation