## Slide 1: Improved Intra Mode Coding by Multiple mode candidates
Wenpeng ding Xiaoyin Che Yunhui Shi and Baocai Yin
Beijing University of Technology

## Slide 2: Intra prediction Mode in TMuc
Most Probable Mode = Min(Left, Top)
1 bit to indicate whether the most probable mode hit the current mode

## Slide 3: Multiple mode candidates
 | One candidates (TMuc0.9) |  | Two candidates |  | Three candidates | 
Probability | 23.31% | 76.69% | 34.30% | 65.70% | 37.20% | 62.80%

## Slide 4: Two mode candidates

## Slide 5: Multiple mode candidates
Most Probable Modes = {Left, Top}
1 bit to indicate whether the most probable modes hit the current mode
1bit to which one hit the current mode

## Slide 6: Multiple mode candidates
Match |  |  | Not Match
One Mode Candidate | two Mode Candidates (Left!=Top && Left_Availabe&& Top_Availble) |  | 
 | ModeX==left | ModeX==right | 
Encode(1) | Encode(1) Encode(1) | Encode(1) Encode(0) | Encode(0) Encode_Mode_X

## Slide 7: Syntex
read_intra_pred_mode(){ | Descriptor
use_candidate_dir | u(1)¦ae(v)
if (use_candidate_dir){ | 
If(num_of_ candidate_num = 2) | 
candidate_num | u(1)¦ae(v)
}else{ | 
rem_intra_pred_mode | ue(v)¦ae(v)
} | 
} | 

## Slide 8: Experimental Results:Intra_CABAC
Intra |  |  |  | 
A | Traffic | -0.3 | -0.3 | -0.3
 | PeopleOnStreet | -0.2 | -0.3 | -0.3
 | Kimono | -0.2 | -0.1 | -0.2
B | ParkScene | -0.1 | -0.1 | -0.1
 | Cactus | -0.4 | -0.4 | -0.5
 | BasketballDrive | -0.7 | -0.6 | -0.7
 | BQTerrace | -0.3 | -0.4 | -0.3
C | BasketballDrill | -0.7 | -0.7 | -0.8
 | BQMall | -0.3 | -0.3 | -0.3
 | PartyScene | 0.1 | 0.0 | 0.0
 | RaceHorses | -0.2 | -0.2 | -0.2
D | BasketballPass | -0.2 | -0.2 | -0.2
 | BQSquare | -0.1 | -0.1 | -0.1
 | BlowingBubbles | -0.1 | -0.1 | -0.1
 | RaceHorses | -0.2 | -0.1 | -0.3
E | Vidyo1 | -0.7 | -0.6 | -0.7
 | Vidyo3 | -0.3 | -0.3 | -0.4
 | Vidyo4 | -0.4 | -0.5 | -0.7

## Slide 9: Experimental Results:Intra_loco
Intra_loco |  |  |  | 
A | Traffic | -0.5 | -0.3 | -0.3
 | PeopleOnStreet | -0.4 | -0.3 | -0.3
 | Kimono | -0.3 | -0.2 | -0.2
B | ParkScene | -0.3 | -0.1 | -0.2
 | Cactus | -0.6 | -0.4 | -0.4
 | BasketballDrive | -0.9 | -0.7 | -0.7
 | BQTerrace | -0.5 | -0.4 | -0.3
C | BasketballDrill | -1 | -0.8 | -0.8
 | BQMall | -0.5 | -0.3 | -0.4
 | PartyScene | -0.2 | -0.1 | -0.1
 | RaceHorses | -0.4 | -0.3 | -0.3
D | BasketballPass | -0.7 | -0.4 | -0.6
 | BQSquare | -0.4 | -0.3 | -0.3
 | BlowingBubbles | -0.4 | -0.3 | -0.2
 | RaceHorses | -0.4 | -0.3 | -0.3
E | Vidyo1 | -1.2 | -0.6 | -0.6
 | Vidyo3 | -0.5 | -0.5 | -0.5
 | Vidyo4 | -0.8 | -0.4 | -0.4

## Slide 10: Experimental Results:Summery
 | Intra |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.2 | -0.3 | -0.3 | -0.4 | -0.3 | -0.3
Class B | -0.3 | -0.3 | -0.4 | -0.5 | -0.4 | -0.4
Class C | -0.3 | -0.3 | -0.3 | -0.5 | -0.4 | -0.4
Class D | -0.2 | -0.2 | -0.2 | -0.5 | -0.3 | -0.3
Class E | -0.5 | -0.5 | -0.6 | -0.8 | -0.5 | -0.5
All | -0.3 | -0.3 | -0.4 | -0.6 | -0.4 | -0.4
Enc Time[%] | 98% |  |  | 108% |  | 
Dec Time[%] | 96% |  |  | 109% |  | 

## Slide 11: Recommendation
Adopt to the HM software
Or establish a Core experiment for the next meeting