## Slide 1: Improved Chroma Intra Mode Signaling
L. Dong, W. Liu and A. Tabatabai
Jan. 21, 2011
JCTVC-D255

## Slide 2: Overview
In the current HM, Intra coded prediction units (PU) use angular prediction to generate prediction signal.
For chroma
  possible prediction directions are vertical, horizontal, DC, diagonal and “same as luma”.
  They are each assigned codeword from 0 – 4 and the mode is signaled in the bitstream.
Study shows that
  The most probable intra chroma mode is the “same as luma” mode.
  However, it is assigned the longest codeword.
Two changes are proposed to improve coding efficiency:
  Reassign codewords so that shortest codeword is used for most probable mode
  Codeword space reduction when luma mode is one of vertical, horizontal, DC and diagonal down right.

## Slide 3: Codeword re-assignment
Study shows that “same as luma” is the most probable mode for intra chroma direction.
This proposal proposes to assign codewords according to the table below
Intra Chroma Dir | Old bins/codeword | Proposed bins/codeword
vertical | 1 | 01
horizontal | 01 | 001
DC | 001 | 0001
diagnal down right | 0000 | 0000
same as luma | 0001 | 1

## Slide 4: Codeword Space Reduction
Chroma Dir | Luma Dir |  |  |  | 
 | vertical | horizontal | DC | diagonal | Others
vertical | n/a | 01 | 01 | 01 | 01
horizontal | 01 | n/a | 001 | 001 | 001
DC | 001 | 001 | n/a | 000 | 0001
diagnal down right | 000 | 000 | 000 | n/a | 0000
same as luma | 1 | 1 | 1 | 1 | 1
The 5 chroma modes are not always mutually exclusive,
  E.g. when the luma direction is vertical, the chroma mode “vertical” is redundant given the “same as luma” bit
  In this case, the “vertical” mode can be removed from the codeword list.
Codeword space reduction is proposed to further improve coding efficiency.

## Slide 5: Results
 | Intra High Efficiency |  |  | Intra Low Complexity |  | 
 | Y BD-rate (%) | U BD-rate (%) | V BD-rate (%) | Y BD-rate (%) | U BD-rate (%) | V BD-rate (%)
Class A | -0.8 | 0.0 | 0.3 | -0.6 | -0.3 | -0.1
Class B | -0.7 | 0.1 | 0.1 | -0.6 | -0.5 | -0.4
Class C | -0.7 | 0.1 | 0.2 | -0.7 | -0.5 | -0.4
Class D | -0.6 | 0.2 | 0.3 | -0.5 | -0.3 | -0.3
Class E | -1.1 | -0.5 | -0.2 | -0.5 | -0.1 | -0.2
All | -0.7 | 0.0 | 0.1 | -0.6 | -0.4 | -0.3
0.7% and 0.6% BD rate improvement for intra only configurations
The results have been cross-checked by Panasonic (JCTVC-D280)
Recommend to change current Chroma Intra Mode Prediction Table