## Slide 1: JCTVC-D257 Low complexity 32×32 transform by partial frequency transform
Qualcomm & Samsung Electronics
Presented by: Joel Sole

## Slide 2: Background
Large transforms (32×32 & 64×64) might be too complex
  Need to buffer intermediate coefficients after transform in one direction
At the Guangzhou meeting several proposals aimed at solving this issue
Two contributions with similar technology
  JCTVC-C209: Samsung Electronics, “Low-complexity 16x16 and 32x32 transforms and partial frequency transform”
  JCTVC-C237: Qualcomm, “Reduced complexity 32x32 transform by coefficient zero-out”
This contribution combines JCTVC-C209 and JCTVC-C237

## Slide 3: Technical Description
Modification of the 32×32 core: only the 16 lowest frequency coefficients are computed
  After the first 1-D forward transform, only 50℅ of the coefficients are buffered
  Some calculations to derive intermediate values can also be omitted
  Number of loops in the inverse transform is reduced
  Entropy coding part remains the same, except for the scan that is done on the 16×16 lower frequency square
# of operations / memory ratio | Chen 32×32 | 32×32 partial frequency
Additions | 12416 | 7776
Multiplications | 7424 | 4128
Shifts | 4224 | 3168
All | 24064 | 15072
Memory ratio | 1 | 0.5

## Slide 4: Results
BD-rate | Intra |  |  | Random access |  |  | Low Delay |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | 0.15 | 0.06 | -0.02 | 0.11 | 0.05 | 0.32 |  |  | 
Class B | 0.40 | 0.64 | 0.65 | 0.34 | 0.64 | 0.60 | 0.44 | 0.13 | 0.10
Class C | 0.19 | 0.40 | 0.30 | 0.22 | 0.23 | 0.21 | 0.17 | -0.04 | 0.06
Class D | 0.20 | 0.37 | 0.20 | 0.13 | 0.41 | 0.41 | 0.09 | -0.48 | 0.30
Class E | 0.57 | 0.50 | 0.49 |  |  |  | 0.06 | 0.13 | -0.38
All | 0.31 | 0.44 | 0.37 | 0.22 | 0.39 | 0.41 | 0.21 | -0.06 | 0.05
BD-rate for high efficiency
  No impact on the low complexity configuration
  *Thanks to MediaTek for the cross-check (in JCTVC-D135)

## Slide 5: Conclusions
The 32×32 partial frequency transform provides a good trade-off between complexity, memory requirements and performance
Propose to include this transform in HEVC Test Model

## Slide 6
Thank you!