## Slide 1: Parallel Processing Friendly Simplified Context Selection of Significance Map
Cheung Auyeung, Wei Liu
Sony
Jan 17, 2011
<number>
JVTVC-D260

## Slide 2: Summary
Objective
  Reduce the complexity and improve the parallel processing friendliness of context selection significant map of transform coefficients
Status
  Reduced the size of the neighborhood for context selection from 10 pixels to 5 pixels
  Improved potential parallelism by removing data dependency on the immediate adjacent pixel along the same diagonal scanning path.
  Removed data dependency on scan direction, the left and bottom boundary of the block.
  Achieved a maximum of 0.1% BD bitrate reduction.
Cross-Checking
  JCTVC-D242 (By TI. Thank you very much.)
  BD-Rate matched.
  Some differences in decoding timing estimation.
<number>

## Slide 3: HM Context of HE Significant Map
<number>
A
D
H
J
E
B
C
F
I
G
K
X
X
Context Mask at position X.
The context at X is based on the half of the sum of the significance of the light and dark purple positions.
Context Mask in a 16x16 Block.
Data Dependency of X on G and K pixel reduce parallelism

## Slide 4: Proposed Context of HE Significant Map
<number>
H
E
B
F
I
X
X
Proposed context mask at position X.
The context at X is based on the sum of the significance of the light purple positions.
Context Mask in a 16x16 Block.
Better parallelism: No data dependency of pixels in a diagonal scan line.
Less Complex: Smaller context mask than HM.

## Slide 5: Subset of HM getSigCtxInc()
UInt TComTrQuant::getSigCtxInc ( TCoeff* pcCoeff,
const UInt uiPosX,
const UInt uiPosY,
const UInt uiLog2BlkSize,
const UInt uiStride,
const bool bDownLeft )
{
UInt uiCtxInc = 0;
UInt uiSizeM1 = ( 1 << uiLog2BlkSize ) - 1;
if( uiLog2BlkSize <= 3 )
{
UInt uiShift = max<UInt>( 0, uiLog2BlkSize - 2 );
uiCtxInc = ( ( uiPosY >> uiShift ) << 2 ) + ( uiPosX >> uiShift );
}
else if( uiPosX <= 1 && uiPosY <= 1 )
{
uiCtxInc = ( uiPosY << 1 ) + uiPosX;
}
else if( uiPosY == 0 )
{
. . .
}
else if( uiPosX == 0 )
{
. . .
}
else
{
const int* pData = &pcCoeff[ uiPosX + uiPosY * uiStride ];
int iStride = uiStride;
int iStride2= iStride << 1;
UInt uiCnt = ( pData[ -iStride ] ? 1 : 0 );
uiCnt += ( pData[ -1 ] ? 1 : 0 );
uiCnt += ( pData[ -1 -iStride ] ? 1 : 0 );
if( uiPosX > 1 )
{
uiCnt += ( pData[ -2 ] ? 1 : 0 );
uiCnt += ( pData[ -2 -iStride ] ? 1 : 0 );
if( uiPosY < uiSizeM1 ) // data dependency on bottom boundary
{
uiCnt += ( pData[ -2 +iStride ] ? 1 : 0 );
}
}
if( uiPosY > 1 )
{
uiCnt += ( pData[ -iStride2 ] ? 1 : 0 );
uiCnt += ( pData[ -1 -iStride2 ] ? 1 : 0 );
if( uiPosX < uiSizeM1 ) // data dependency on right boundary
{
uiCnt += ( pData[ 1 -iStride2 ] ? 1 : 0 );
}
}
if( bDownLeft ) // data dependency on scan direction
{
if( uiPosX < uiSizeM1 ) // data dependency on right boundary
{
uiCnt += ( pData[ 1 -iStride ] ? 1 : 0 );
}
}
else
{
if( uiPosY < uiSizeM1 ) // data dependency on bottom boundary
{
uiCnt += ( pData[ -1 +iStride ] ? 1 : 0 );
}
}
uiCtxInc = 10 + min<UInt>( 4, ( uiCnt + 1 ) >> 1 );
}
return uiCtxInc;
}
<number>

## Slide 6: Complete Simplified getSigCtxInc()
Int TComTrQuant::getSigCtxInc ( TCoeff* pcCoeff,
const UInt uiPosX,
const UInt uiPosY,
const UInt uiLog2BlkSize,
const UInt uiStride,
const bool bDownLeft )
{
UInt uiCtxInc = 0;
if( uiLog2BlkSize <= 3 )
{
UInt uiShift = max<UInt>( 0, uiLog2BlkSize - 2 );
uiCtxInc = ( ( uiPosY >> uiShift ) << 2 ) + ( uiPosX >> uiShift );
}
else if( uiPosX <= 1 && uiPosY <= 1 )
{
uiCtxInc = ( uiPosY << 1 ) + uiPosX;
}
else if( uiPosY == 0 )
{
const int* pData = &pcCoeff[ uiPosX + uiPosY * uiStride ];
UInt uiCnt = ( pData[ -1 ] ? 1 : 0 );
uiCnt += ( pData[ -2 ] ? 1 : 0 );
uiCtxInc = 4 + uiCnt;
}
else if( uiPosX == 0 )
{
const int* pData = &pcCoeff[ uiPosX + uiPosY * uiStride ];
int iStride = uiStride;
int iStride2= iStride << 1;
UInt uiCnt = ( pData[ -iStride ] ? 1 : 0 );
uiCnt += ( pData[ -iStride2 ] ? 1 : 0 );
uiCtxInc = 7 + uiCnt;
}
else
{
const int* pData = &pcCoeff[ uiPosX + uiPosY * uiStride ];
int iStride = uiStride;
int iStride2= iStride << 1;
UInt uiCnt = ( pData[ -1 -iStride ] ? 1 : 0 );
uiCnt += ( pData[ -iStride ] ? 1 : 0 );
uiCnt += ( pData[ -1 ] ? 1 : 0 );
if( uiPosX > 1 )
{
uiCnt += ( pData[ -2 ] ? 1 : 0 );
}
if ( uiPosY > 1 )
{
uiCnt += ( pData[ -iStride2 ] ? 1 : 0 );
}
uiCtxInc = 10 + min<UInt>( 4, uiCnt);
}
return uiCtxInc;
}
<number>

## Slide 7: BD-Rate Compared to TMuC-0.9
<number>
 | Intra |  |  | 
 | Y BD-rate | U BD-rate | V BD-rate | % sig count
Class A | 0.0 | -0.1 | -0.1 | -0.42%
Class B | 0.1 | 0.0 | 0.0 | -0.75%
Class C | 0.0 | 0.0 | -0.1 | -0.01%
Class D | 0.0 | 0.0 | 0.0 | 0.05%
Class E | -0.1 | -0.1 | -0.2 | 0.16%
All | 0.0 | 0.0 | -0.1 | -0.19%
Enc Time[%] | #NUM! |  |  | 
Dec Time[%] | 100% |  |  | 
 | Random access |  |  | 
 | Y BD-rate | U BD-rate | V BD-rate | % sig count
Class A | 0.0 | 0.1 | 0.2 | -0.01%
Class B | 0.0 | 0.0 | -0.1 | -0.56%
Class C | 0.0 | -0.1 | -0.1 | 0.03%
Class D | -0.1 | 0.0 | 0.3 | 0.75%
Class E |  |  |  | 
All | 0.0 | 0.0 | 0.0 | 0.05%
Enc Time[%] | #NUM! |  |  | 
Dec Time[%] | 100% |  |  | 
 | Low delay |  |  | 
 | Y BD-rate | U BD-rate | V BD-rate | % sig count
Class A |  |  |  | 
Class B | -0.1 | -0.1 | -0.3 | 0.45%
Class C | -0.1 | -0.1 | -0.2 | 1.47%
Class D | -0.1 | -0.6 | 0.1 | 2.61%
Class E | -0.2 | -0.1 | -0.4 | 1.81%
All | -0.1 | -0.2 | -0.2 | 1.58%
Enc Time[%] | #NUM! |  |  | 
Dec Time[%] | 100% |  |  | 
Results of JCTVC-D260. compiled on Linux with GCC 4.5.1 64bit compiler. To obtain the decoder timing, the bitstreams were decoded on Intel Xeon® CPU X5355 @ 2.66Ghz with 48Gb RAM sequentially in Linux without outputting the decoded video.

## Slide 8: Conclusions
Proposed a more parallel processing friendly and lower complexity context selection method of significance map.
Results were cross-checked in similar manner as in CE11.
Propose to JCT-VC to consider it as a part of the next HM or for further study.
<number>