## Slide 1: JCTVC-D262 Parallel Context Processing for the significance map in high coding efficiency
J. Sole, R. Joshi. I.S. Cong, M. Coban, M. Karczewicz

## Slide 2: Background
CABAC is a well known throughput bottleneck in the video codec implementations
  Several contributions have addressed the issue
    “TI Parallel context processing (PCP) proposal”, JCTVC-C062
    “Parallelization of HHI_TRANSFORM_CODING”, JCTVC-C227
    “Context selection complexity in HEVC CABAC”, JCTVC-D244
    “Parallel processing friendly context processing for significance map coding in CABAC ”, JCTVC-D241
Significance map:
  Large percentage of bins at high bitrate
  Data dependencies in context selection
  Interleave of two syntax elements: significance and last
  Difficult to parallelize the encoding using speculative computing

## Slide 3: Significance Map Coding in HEVC
The significance map encoding is carried out by interleaving the bins of
  The significance of a coefficient (significant_coeff_flag) and
  The bin indicating whether the coefficient is the last significant within the block (last_significant_coeff_flag) when the flag significant_coeff_flag equals 1
Decision regarding encoding of the last_significant_coeff_flag for a particular transform coefficient is dependent on the significant_coeff_flag

## Slide 4: Explicit signaling of the last significant coefficient
Separate the encoding of the significant_coeff_flag and the last_significant_coeff_flag:
  First, code the position of the last significant coefficient
  Second, code the significance coefficient flags
Code the (X,Y) coordinates of the last significant coefficient
  X and Y coded independently
  Using unary code
  Context depend only on the row/column number and the block size

## Slide 5: Context Simplification
Two modifications in the context for the significance
  Diagonal neighbor is not included to further enhance parallelization
  If the last significant coefficient is found within the first 10 coefficients, then a set of contexts depending solely on the scan position is used
    Otherwise, regular contexts are used

## Slide 6: Results
BD-rate and encoding/decoding times
  * Thanks to Toshiba for the cross-check (JCTVC-D212)
BD-rate | Intra |  |  | Random access |  |  | Low delay |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.04 | -0.25 | -0.14 | -0.05 | -0.66 | -0.21 |  |  | 
Class B | 0.06 | -0.28 | -0.27 | 0.00 | -0.76 | -0.77 | -0.23 | -1.40 | -1.47
Class C | 0.06 | 0.01 | -0.01 | 0.06 | -1.09 | -1.01 | -0.14 | -1.23 | -1.30
Class D | -0.05 | -0.20 | -0.01 | 0.01 | -1.14 | -1.10 | -0.27 | -2.90 | -1.98
Class E | 0.27 | -0.22 | -0.67 |  |  |  | -0.01 | -0.67 | -2.32
All | 0.06 | -0.18 | -0.20 | 0.01 | -0.93 | -0.85 | -0.17 | -1.59 | -1.72
Enc T[%] | 96% |  |  | 101% |  |  | 100% |  | 
Dec T[%] | 99% |  |  | 100% |  |  | 102% |  | 

## Slide 7: Conclusions
Proposed an algorithm to parallelize the significance map coding
  Highly simplifies the contexts for highly occurring cases of the significance map and for the last flag
  Beneficial for the implementation of parallel algorithms by the separation of the significant coefficient and the last coefficient planes
  X and Y component are encoded independently, and thus, allowing further parallelization within the last coefficient encoding algorithm itself
  Parallelization and speculative computation of the significant coefficients become easier because the stopping point is known beforehand
  The worst-case scenario for the number of bins for last flag is reduced

## Slide 8
Thank you!