## Slide 1: Low Complexity Parametric ALF
Ehsan Maani
Wei Liu
Lina Dong
JCTVC-D270

## Slide 2: Adaptive Loop Filters
Adaptive Loop Filter
  Filter applied to the reconstructed image in the loop after de-blocking filter
  Purpose is to remove compression noise, artifacts, etc and present a better quality image
Current Technology
  Almost all existing ALF technologies consist of online-trained Wiener-Filters
  Filter coefficients are transmitted to decoder
  Additional control information is sometimes transmitted to signal whether the filter should be applied to certain blocks in an image
  Multiple passes are sometimes necessary to come up with optimum filter size, filter coefficients and filter control
Original image
Encoded image
Wiener Filter

## Slide 3: Parametric ALF
Parametric ALF is a completely new approach to the problem
  A set of fixed filters are defined based on parameters
  In this proposal we chose direction and bandwidth as the parameters
  Encoder finds the best filter (in the set) for each block of image. Indices of filters are transmitted to decoder to signal what filter should be used for a given block.
Frequency responses of three filters with same direction but different bandwidths

## Slide 4: PALF for HEVC - Luma
Filter set
  32 (8x4) fixed filters are pre-trained offline with the combination of
    8 directions, and
    4 bandwidths
  Plus one additional all-pass filter (no filtering)
  Filter size is 9x9 (symmetric) for all luma filters
Parameter signaling
  Control depth
    For each LCU, a maxDepth is decided and signaled to the decoder.
    This controls the parameter signal depth for each CU.
  PALF parameters signaled at Sub-CU
    When it is the leaf node in the CU quad-tree or depth=maxDepth
    Filter Bandwidth among {0, 1, 2, 3, 4}
      Filter strength of “0” means no filtering.
    If filter strength is not 0, direction is further signaled among {0, 1, 2, 3, 4, 5, 6, 7}
PALF parameter optimization is done for each LCU using only 1 pass
  This yields a maximum encoder delay of 1 row of LCU + 4 lines
An example of maxDepth = 2, PALF parameters are signaled at each node marked red in the figure above.

## Slide 5: PALF for HEVC – Chroma
Filter set
  As for luma, 32 filters with 8 directions and 4 bandwidths for each direction are defined for the two chroma channels
  Filter size is 5x5 for YUV420 sequences
Parameter signaling
  Both chroma channels share the same set of filter parameters
  Control depth
    Control depth for chroma is fixed to be 0 and not signaled
  PALF parameters
    Bandwidth of the filters are signaled the same way as Luma
    When filter bandwidth is not 0, direction is further signaled using two possible modes
      Explicit: indicate a direction to be used for chroma channels
      Implicit: use directions of Luma for the entire LCU. It will use strength signaled specifically for chroma, but directions and sub LCU on/off is copied from Luma

## Slide 6: Advantages of Parametric ALF
Parametric ALF
  Fixed filters provides possibilities for software and hardware optimization;
  Frame level delay is avoided at the encoder;
  Memory bandwidth access is reduced since no multiple pass operation is necessary.
Traditional ALF
  High computational complexity. Many operations are needed to find filter coefficients;
  Variable filter coefficients make software and hardware implementation optimization more difficult;
  Multiple pass processing at the encoder increases the delay, requires high memory bandwidth.

## Slide 7: Simulation Results
 | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | -3.6 | -1.7 | -1.0
Class B | -2.1 | -1.9 | -2.1
Class C | -2.1 | -1.7 | -2.7
Class D | -1.2 | -1.1 | -1.4
Class E | -3.3 | -3.9 | -4.3
All | -2.3 | -2.0 | -2.3
 | Random access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | -2.6 | -2.3 | -1.5
Class B | -3.4 | -6.4 | -5.8
Class C | -2.2 | -5.2 | -6.6
Class D | -1.6 | -4.1 | -4.8
Class E |  |  | 
All | -2.5 | -4.9 | -5.2
 | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  | 
Class B | -4.2 | -6.4 | -7.1
Class C | -3.7 | -8.1 | -10.6
Class D | -2.8 | -6.0 | -6.7
Class E | -5.1 | -4.1 | -4.0
All | -3.9 | -6.3 | -7.3

## Slide 8: Future Work
Propose the study of default fixed filters for low delay in loop filtering.