## Slide 1: JCTVC-D273: Modified derivation process of temporal motion vector predictor
Toshiyasu Sugio
Takahiro Nishi
Panasonic

## Slide 2
Motivation
Temporal MV predictor is important as one of the MVP candidates for AMVP
In the TMuC0.9-hm, if “collocated_from_l0_flag” is equal to 0, temporal MV predictor is derived as below,
current
picture
colPic
co-located
partition
target
prediction unit
mvL0Col
mvL0
mvL1
○
reference
picture
current
picture
colPic
co-located
partition
mvL0Col
mvL0
mvL1
×
×
target
prediction unit
reference
picture
mvL0 is available
 mvL0Col is added to MVP candidates as temporal MV
mvL1 is not available
 Nothing is added to MVP candidates as temporal MV
Case of collocated_from_l0_flag = 0

## Slide 3
current
picture
colPic
co-located
partition
mvL1Col
mvL0
mvL1
×
○
target
prediction unit
reference
picture
Proposed Method
If mvL0 in co-located partition were not available, availability of mvL1 is checked and, if available, mvL1 is used to derive temporal MV predictor
This is conceptually same as AVC specification, and it was modified to suit the TMuC0.9-hm

## Slide 4
collocated_from_l0_flag == 1 ?
use MvL1
as mvCol
use MvL0
as mvCol
Yes
No
Is B slice ?
MvL1 of co-located
partition is available ?
MvL0 of co-located
partition is available ?
Set
not available
use MvL0
as mvCol
use MvL1
as mvCol
MvL0 of co-located
partition is available ?
MvL1 of co-located
partition is available ?
Set
not available
Yes
Yes
Yes
Yes
Yes
No
No
No
No
No
Non-highlighted blocks are same as original TMuC0.9-hm process
Highlighted blocks are newly added in this proposal
Flowchart of proposed method

## Slide 5
Experimental results ( Anchor: TMuC0.9-hm )
A proposed method was implemented on TMuC0.9-hm software
It was tested for four inter coding configurations
(Anchor: TMuC0.9-hm)

## Slide 6
Proposed method saves bits for all sequences
BD rate for each sequences

## Slide 7
Conclusion
A modified derivation process of temporal MV predictor was proposed
It saves 0.4% bits for HE and 0.3% bits for LC on average in the RA case
  It saves the number of bits consistently for all sequences
  Reduction in BD rate was observed
  The complexity impact is negligible
We recommend that proposed method be adopted in the HM/WD of HEVC

## Slide 8
Thank you