## Slide 1: JCTVC-D274: Modified usage of predicted motion vectors in forward directional bi-predictive coding frame
Toshiyasu Sugio
Takahiro Nishi
Panasonic

## Slide 2
Motivation
The Special B-frames are used as an alternative of the conventional P-frames
  We referred them as “Bf-frames”
  Bf-frames use forward directional bi-prediction with reference list 0 and 1
When list 0 and 1 are identical, the prediction using only list 1 is disabled
  We referred it as list 1 “uni-prediction” in contrast with “bi-prediction”
Bf-frames just use forward directional bi-prediction and list 0 uni-prediction
There are some rooms for improvement in Bf-frame coding efficiency due to disabled list 1 uni-prediction
B
B
Bf
B
B
B
B
B
Bf
Bf
Bf
I
Bf
Bf
Bf
Bf
Bf
Bf
Random access scenario
Low delay scenario

## Slide 3
Proposed Method
This proposal includes the following four key points for Bf-frames:
  Uni-prediction in Skipped Prediction Units
  Bi-prediction in Direct Prediction Units
  Enhanced Reference Index Decision for Skipped and Direct PU
  Enhanced Temporal Motion Vector Predictor

## Slide 4
1. Uni-prediction in Skipped Prediction Units
Skipped PUs in the TMuC0.9-hm are using bi-prediction only
Accuracy of mvL1 for bi-prediction tends to be worse than mvL0 in Bf-frame
  The list 1 uni-prediction has been disable for Bf-frame So, the number of MV predictors for list 1 is usually less than that for list 0
 Performance of skipped PUs has been worsen by the prediction based on the list 1, and it cannot be recovered by residual signals due to the mode
Proposal 1: For skipped PUs in Bf-frame, only list 0 uni-prediction is used instead of bi-prediction

## Slide 5
2. Bi-prediction in Direct Prediction Units
An explicit signaling by the flag “inter_pred_idc” is used to switch bi-prediction or uni-prediction for direct PUs
In Bf-frame, difference between two RD-costs of bi-prediction and list 0 uni-prediction tends to be small in direct PUs
  Because one single reference frame is often used for both uni- and bi-prediction
  MV are likely to point the very near position
 it’s considered to be not worth sending that flag for such a small difference
Proposal 2: For direct PUs in Bf-frame,
Single prediction scheme is used and “inter_pred_idc” has been removed
 bi-prediction is used to combine with proposal 1
To keep a prediction mode which can reduce the motion vector overhead for bi-prediction

## Slide 6
3. Enhanced Reference Index Decision for Skipped/Direct PU
RefIdx of skipped and direct PUs are always set to 0
Even if there were plural of available MVs which refIdx are 1, spatially MVs are regarded to be not available due to having different refIdx
Proposal 3: For skipped and direct PUs,
RefIdx follow the majority of refIdx of neighboring PUs

## Slide 7
4. Enhanced Temporal Motion Vector Predictor
We proposed a modified derivation process of temporal MV predictor in JCTVC-D273
That modified process doesn’t work in Bf-frames
  Because mvL1 cannot be available when mvL0 is not available due to disabled list 1 uni-prediction
Proposal 4: In order to improve the coding efficiency in Bf-frame,
two temporal MV predictors (mvL0Col and mvL1Col) are added to MVP candidates
  these are derived from mvL0 and mvL1 of co-located partition, if available

## Slide 8
Experimental results
A proposed method was implemented on TMuC0.9-hm software
It was tested for four inter coding configurations
(Anchor: TMuC0.9-hm)

## Slide 9
Proposed method saves bits for almost all sequences
BD rate for each sequences (Random Access cases)

## Slide 10
Proposed method saves bits for all sequences
BD rate for each sequences (Low Delay cases)

## Slide 11
Conclusion
A modified usage of temporally/spatially predicted MV is proposed for Bf-frame
It saves 1.0% bits for HE and 2.2% bits for LC on average in the LD scenario
  It reduces encoding and decoding time slightly relative to TMuC0.9-hm

## Slide 12
Thank you