## Slide 1: Adaptive Coding of PredMode Syntax Elements (JCTVC-D275)
ZTE Corporation
Wen Zhang
Dong Wang
Yingjie Hong
Wen Zuo
Ming Li

## Slide 2: Outline
Introduction
Solution
  Overview & Implementation
Experimentation
  Test condition & Results
Conclusion
Future Work

## Slide 3: Introduction
Let PredMode stand for different inter-frame prediction modes.
In TMuC0.9-hm, several syntax elements were used to signal PredMode for CU/PU.
  i.e. SkipFlag, MergeFlag and the flags in codePredMode and codePartSize functions.
Fixed representing method is used while coding the PredMode related elements.
  Firstly encode SkipFlag, sencondly encode MergeFlag, then encode the flags in codePredMode and codePartSize functions.

## Slide 4: Introduction
The fixed representing method for PredMode is not always effective.
  i.e. if the occurrence of SKIP_MODE is not the largest one in current frame or slice.
  In this case, redundancy is obviously in codeword for PredMode according to principle of VLC.
This redundancy could be common issue while coding other syntax elements.
  Such as Cbf, PartSize, InterDir, MvpIdx.

## Slide 5: Solution -- Overview
Let representing method of syntax elements be adjusted adaptively at slice or frame level.
Our solution for PredMode has improved coding efficiency comparing to TMuC0.9-hm.
  The average gain of LoCo are -1.2% for RA, -0.6% for LD, while both encode and decode time decreased slightly.
  The average gain of HE are -0.1% for both RA and LD, meanwhile the encode and decode time remain almost unchanged.

## Slide 6: Solution -- Implementation
A new syntax element pred_mode_coding_type is added into P/B-slice header.
  As shown in Table 1.
It indicates coding type used in current slice for PredMode related elements.
It is updated for each slice according to the statistical results of the occurrence of different PredMode.
  Six coding types are defined in our solution for pred_mode_coding_type.
  as shown in Table 2.

## Slide 7: Solution -- Table 1

## Slide 8: Solution -- Table 2
SKIP_MERGE | Coding SkipFlag first, then MergeFlag
SKIP_INTER | Coding Skipflag first, then InterFlag
MERGE_SKIP | Coding MergeFlag first, then SkipFlag
MERGE_INTER | Coding MergeFlag first, then InterFlag
INTER_SKIP | Coding InterFlag first, then SkipFlag
INTER_MERGE | Coding InterFlag first then MergeFlag

## Slide 9: Experimentation -- Test Conditions
H/W | HP NT server E5506/2.13GHz
Compiler | vs.net 2005
OS | Windows NT server 2003
Guidance | JCTVC-C500
Anchor | TMuC0.9-hm
Configuration | HE ( RA, LD ); LC ( RA, LD )
Sequence | All Class A~E

## Slide 10: Experimentation -- Results
 | Random access |  |  | Random access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.2 | 0.0 | 0.0 | -1.2 | -0.8 | -0.8
Class B | -0.1 | -0.1 | -0.2 | -1.0 | -0.7 | -0.7
Class C | -0.1 | -0.1 | 0.0 | -1.4 | -1.1 | -1.1
Class D | -0.2 | -0.2 | -0.1 | -1.3 | -1.1 | -1.0
Class E |  |  |  |  |  | 
All | -0.1 | -0.1 | -0.1 | -1.2 | -0.9 | -0.9
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 102% |  |  | 100% |  | 
 | Low delay |  |  | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | -0.1 | -0.1 | -0.1 | -0.5 | -0.8 | -0.9
Class C | 0.0 | -0.1 | -0.2 | -0.6 | -0.8 | -0.6
Class D | -0.1 | -0.9 | 0.0 | -1.0 | -1.1 | -1.0
Class E | -0.3 | -0.4 | -0.3 | -0.1 | 0.0 | -0.1
All | -0.1 | -0.4 | -0.1 | -0.6 | -0.8 | -0.7
Enc Time[%] | 100% |  |  | 99% |  | 
Dec Time[%] | 99% |  |  | 97% |  | 

## Slide 11: Conclusion
An new adaptive coding method for PredMode at slice/frame level is proposed.
The proposed method has achieved coding efficiency improvement with even lower complexity.
From this point of view, we hope
  Adopt this adaptive coding method for PredMode into HEVC/HM.
  Establish an AHG/CE to further investigate adaptive coding method for other syntax elements.

## Slide 12: Future Work
Try to improve coding efficiency of proposed method for HE configurations.
  i.e. related context Models of CABAC may need to be rebuilt accordingly.
Try to investigate adaptive coding method at slice/frame level for other syntax elements.
  Cbf, PartSize, InterDir, MvpIdx, etc.
  Other residual, motion related elements.