## Slide 1: Summary and Improvements of DCIM (JCTVC-D279)
Ehsan Maani, Ali Tabatabai (Sony)
Virginie Drugeon (Panasonic) Tomoyuki Yamamoto (SHARP)
JCT-VC 4th Meeting: Daegu, KR, 20-28 January, 2011
Notes: <number>

## Slide 2: DCIM: Differential Coding of Intra Modes
Algorithm
  Add ‘neighbors suggested modes’ (DCIM modes) to original modes (UIP modes)
  DCIM mode (main) is decided based on the derived direction by applying sobel operater to the neighbor pixels
  Around the main DCIM mode, additional DCIM modes are added
<number>
UIP | 0 | ...
DCIM(k=0) | 1 | 1
DCIM(k=+1,-1) | 1 | 01x
DCIM(k=+2,-2) | 1 | 001x
DCIM(k=+3,-3) | 1 | 000x
Mode signaling

## Slide 3: DCIM Technology
DCIM Proposal
DCIM Key Features
HM Proposal
Enhances current UIP
Efficient signaling of directional information
Significant Coding & Visual Improvements
Notes: <number>

## Slide 4
BasketballDrive TMuC 0.9 IO, QP=32
Mode selection

## Slide 5
BasketballDrive DCIM IO, QP=32
Mode selection

## Slide 6: Objective evaluation (1)
<number>
DCIM (v1)
  Intra prediction modes
    UIP modes ... max 34 modes
    DCIM modes
  Cross-check
    verified by NEC, NHK, Panasonic
 | Intra |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -1.7 | -0.6 | -0.3 | -1.5 | -0.8 | -0.4
Class B | -2.1 | -1.1 | -1.2 | -2.2 | -1.8 | -1.9
Class C | -2.4 | -1.1 | -1.2 | -2.9 | -1.9 | -2.0
Class D | -1.5 | -0.4 | -0.3 | -1.8 | -0.8 | -1.0
Class E | -3.1 | -2.2 | -1.9 | -3.1 | -1.5 | -1.7
All | -2.1 | -1.1 | -1.0 | -2.3 | -1.4 | -1.5
Enc Time[%] | 108% |  |  | 115% |  | 
Dec Time[%] | 106% |  |  | 119% |  | 

## Slide 7: Objective evaluation (2)
<number>
DCIM (v2)
  Intra prediction modes
    UIP modes ... max 17 modes, modified MPM derivation
    DCIM modes
  Cross-check
    verified by NHK
 | Intra |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -1.8 | -0.9 | -0.5 | -1.8 | -0.8 | -0.4
Class B | -2.3 | -1.4 | -1.4 | -2.6 | -2.0 | -2.0
Class C | -2.5 | -1.3 | -1.4 | -3.0 | -1.9 | -2.1
Class D | -1.6 | -0.5 | -0.6 | -2.0 | -0.8 | -1.2
Class E | -3.3 | -2.1 | -1.9 | -3.2 | -1.5 | -1.6
All | -2.3 | -1.2 | -1.2 | -2.6 | -1.5 | -1.6
Enc Time[%] | 106% |  |  | 106% |  | 
Dec Time[%] | 106% |  |  | 117% |  | 

## Slide 8
<number>
DCIM (v1)
DCIM (v2)

## Slide 9
<number>
DCIM (v1)
DCIM (v2)

## Slide 10: Objective evaluation (3)
<number>
SHV sequences evaluation
  sequences
    steam_locomotive_train
    nebuta_festival
  Cross-check
    verified by NHK, NEC
 | Intra |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class SHV | -1.0 | -0.5 | -0.1 | -1.6 | -0.9 | -0.9
Enc Time[%] | 106% |  |  | 107% |  | 
Dec Time[%] | 104% |  |  | 114% |  | 

## Slide 11: Subjective evaluation
Evaluation (by NEC)
  BasketballDriva QP=37 and BasketballDrill QP=32
  Random Access
Observation
  Visual appearance is different
  No significant improvement/degradation as a video
  Significant improvement as a frame
<number>

## Slide 12: Conclusion
Improvement and comprehensive study of DCIM was done
Objective performance
  HE: 2.3% gain with 106/106 % encoding/decoding time
  LC: 2.6% gain with 106/117 % encoding/decoding time
Subjective performance
  Improves regions with strong edges
Recommend for HM
<number>