## Slide 1: Switching Interpolation Filter (SIF) scheme with low complexity decision algorithm
T. Yoshino, S. Naito (KDDI)

## Slide 2: Introduction
About this contribution
  Low-complexity solution for Selectable Interpolation Filter (SIF)
  Propose that low-complexity SIF be discussed in CE
Previous meeting (JCTVC-C183)
  6-tap SIF (8 sets of filter coefficients)
  Large computational cost for selecting the filter
Progress
  Low-complexity approach for selecting filter
  This low-complexity approach is based on [2]
[2] T. Yoshino et. al, "Low-complexity Scheme for Adaptive Interpolation
Filter Based on Amplitude Characteristic Analysis”, ICIP2010, Sep. 2010

## Slide 3: Coding Experiment
Additionally implemented on TMuC0.9
Low Complexity / Low Delay condition
Separable 8-tap (original) filter
Pre-defined 8 candidates of filter coefficients set
    [-18 31 -54 169 169 -54 31 -18]
    [ -3 18 -44 157 157 -44 18 -3]
    [ 10 3 -31 146 146 -31 3 10]
    [ 20 -10 -18 136 136 -18 -10 20]
    [ 20 -24 -4 136 136 -4 -24 20]
    [ 13 -31 10 136 136 10 -31 13]
    [ -3 -33 28 136 136 28 -33 -3]
    [-18 -26 44 128 128 44 -26 -18]

## Slide 4: Experimental results
 | Y BD-rate
Class B | -0.36
Class C | -0.37
Class D | -0.46
Class E | -0.48
All | -0.41
Enc Time [%] | 100
Dec Time [%] | 100
Summary of the results for LoDe/LoCo

## Slide 5: Conclusion
Summary of this contribution
  Switching Interpolation Filter (SIF) with low-complexity approach for selecting filter
  0.41% BD-rate against TMuC under LD/LC while maintaining encoding/decoding time
Conclusion
  Computational cost for selecting SIF candidate can be limited.
  Low complexity SIF approach based on D285 is discussed in CE.