## Slide 1: CE1：Huawei report on TMDMVD and STDM in HM
Huawei Tech Co. Ltd.

## Slide 2: Content
Abstract
STDM
TM-DMVD
Experiment result
Summary and Conclusion

## Slide 3: Abstract
Huawei proposed two DMVD techniques: TM-DMVD,STDM
In TMuC0.9, STDM implemented in B (non-GPB) slices and TM-DMVD implemented in P or GPB slices.
2.28% average bitsaving and extra decoding time is about 11% over that of anchor in RA-HE;
1.08% average bitsaving and extra decoding time is about 13% over that of anchor in LD-HE.

## Slide 4: STDM
Based on our previous approach, STDM implemented in B- (non-GPB) slices. Motion vector candidates are used for fast motion vector search, and the template in the cost calculations is removed from the previous proposal.
Ref0
Ref1
curPU

## Slide 5: STDM Process
During setting up new candidates, each existing candidate will create a mirrored MV ;
Find the best MV by

## Slide 6: TM-DMVD
Baed on our previous TM-DMVD, some improvement is done and implemented in 2Nx2N,2NxN, Nx2N and NxN of P or GPB pictures.

## Slide 7: TM-DMVD process
Candidates based template matching
Reference template interpolated by bilinear filter
Multiple reference pictures and multi-hypothesis prediction

## Slide 8: Performance STDM+TM-DMVD for Random Access
 | Random access |  |  | Random access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -3.16 | -3.06 | -2.89 | -2.24 | -2.17 | -2.23
Class B | -1.98 | -1.60 | -1.79 | -1.59 | -1.49 | -1.67
Class C | -2.01 | -2.01 | -2.23 | -1.49 | -1.64 | -1.86
Class D | -2.49 | -2.17 | -2.43 | -1.96 | -1.97 | -1.91
Class E |  |  |  |  |  | 
All | -2.28 | -2.06 | -2.23 | -1.75 | -1.75 | -1.86
Enc Time[%] | 173% |  |  | 172% |  | 
Dec Time[%] | 111% |  |  | 123% |  | 

## Slide 9: Performance STDM only for Random Access
 | Random access |  |  | Random access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -2.91 | -2.85 | -2.89 | -2.16 | -2.11 | -2.08
Class B | -1.72 | -1.48 | -1.54 | -1.47 | -1.24 | -1/37
Class C | -1.79 | -1.98 | -2.00 | -1.36 | -1.40 | -1.59
Class D | -2.13 | -1.95 | -2.16 | -1.86 | -1.78 | -1.75
Class E |  |  |  |  |  | 
All | -2.00 | -1.92 | -2.01 | -1.64 | -1.54 | -1.63
Enc Time[%] | 153% |  |  | 166% |  | 
Dec Time[%] | 105.69% |  |  | 116.99% |  | 

## Slide 10: Performance TM-DMVD only for Low Delay
 | Low delay |  |  | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | -0.88 | -0.98 | -1.48 | -0.5 | -0.3 | -0.3
Class C | -1.03 | -1.13 | -1.34 | -0.3 | -0.7 | -0.7
Class D | -0.92 | -1.55 | -1.13 | -0.2 | -0.5 | -0.4
Class E | -1.66 | -3.35 | -3.45 | -0.8 | -0.3 | -0.5
All | 1.08 | -1.6 | -1.7 | -0.4 | -0.4 | -0.5
Enc Time[%] | 157% |  |  | 162% |  | 
Dec Time[%] | 113.96% |  |  | 124.15% |  |