## Slide 1: CE6.b Report on Short Distance Intra Prediction Method
26/7/31
Xiaoran Cao, Xiulian Peng, Changcai Lai, Yunfei Wang,Yongbing Lin, Jizheng Xu, Lingzhi Liu, Jianhua Zheng, Yun He, Haoping Yu, Feng Wu
(Tsinghua, USTC, Mircosoft, HiSilion, Huawei)
Notes: <number>

## Slide 2
Agenda
Introduction
Algorithm description
Experimental results in CE6

## Slide 3: Introduction
Intra prediction in H.264/AVC/HM of HEVC using the adjacent boundary pixels of reconstructed neighboring square blocks to get the prediction of the entire coding block.
using the correlation between rectangles, lines and pixels are proposed
Page <number>

## Slide 4: Block partitions and Intra prediction in HM
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
TMuC (e.g. 64x64)
Sub-CU
Sub-CU

## Slide 5: Non-square partitions of SDIP
CU:32x32
In addition to the NxN partitions, the partitions can also be MxN:
16x16->4x16/16x4
->1x16/16x1
8x8->2x8/8x2
4x4->1x4 /4x1
116形6
2x8
1x16
4x16
16x16
1x4
8x8

## Slide 6: Unified SDIP intra prediction
UDI modes can be from 9 to 34 and the number of modes is configurable as HM
One UDI mode flag is identified for every 4x16/16x4 or 2x8/8x2 partition
four 1x16/16x1 partitions used the same mode that identified in 4x16/16x4 and similar for 1x4/4x1 partitions in 4x4 PU.
bidirectional intra prediction for mode 6
Square blocks in HM were used for chroma, candidate modes are updated according to the SDIP luma intra modes

## Slide 7: Transform and scan
The same transform matrices (2x2, 4x4, 8x8 and 16x16) in HM were reused in SDIP modes
the coefficients are scanned into a 1D buffer and then reorganized into a 4x4 or 8x8 block and coded

## Slide 8: Results of full serch without any fast method in CE6 test conditions
In this set of configurations, no any fast method was used, 17 modes are used for 1x4/4x1, 2x8/8x2 and 1x16/16x1 partitions，34 modes are used for 4x16/16x4 partitions .
Platform | CPU | Memory | Compiler
Windows Server 2008 R2 64 bits | 2xIntel Xeon L5420@2.5Ghz | 16GB | VS2010

## Slide 9: Results of full search configuration in CE6 test conditions
 | Intra |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -3.7 | -1.9 | -1.7 | -5.2 | -3.4 | -3.7
Class B | -3.5 | -1.4 | -1.6 | -5.3 | -2.2 | -3.1
Class C | -5.8 | -2.7 | -2.9 | -7.8 | -3.7 | -4.6
Class D | -5.8 | -2.8 | -2.9 | -7.4 | -3.9 | -4.3
Class E | -5.2 | -3.2 | -3.1 | -6.4 | -7.0 | -6.1
All | -4.8 | -2.4 | -2.4 | -6.5 | -3.9 | -4.3
Enc Time[%] | 294% |  |  | 246% |  | 
Dec Time[%] | 102% |  |  | 106% |  | 

## Slide 10: Results of Normal configuration in CE6 test conditions
In this normal configuration, SDIP mode was skipped when the RD costs of SIZE_NxN and SIZE_2Nx2N are smaller than a threshold value. 17 modes are used for 1x4/4x1, 2x8/8x2 and 1x16/16x1 partitions， 34 modes are used for 4x16/16x4 partitions.
Platform | CPU | Memory | Compiler
Windows Server 2008 R2 64 bits | 2xIntel Xeon L5420@2.5Ghz | 16GB | VS2010

## Slide 11: Results of Normal configuration in CE6 test conditions
Table1. Results of normal configuration
 | Intra |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -3.7 | -1.9 | -1.9 | -4.9 | -3.6 | -3.9
Class B | -3.2 | -1.5 | -1.7 | -4.9 | -2.6 | -3.5
Class C | -5.5 | -2.9 | -3.1 | -7.4 | -4.0 | -4.8
Class D | -5.6 | -3.0 | -3.0 | -7.1 | -4.1 | -4.5
Class E | -4.8 | -3.2 | -3.0 | -5.8 | -7.2 | -6.3
All | -4.6 | -2.5 | -2.5 | -6.1 | -4.1 | -4.5
Enc Time[%] | 200% |  |  | 182% |  | 
Dec Time[%] | 104% |  |  | 112% |  | 

## Slide 12: Results of Normal configuration
Table2. Comparison of coding efficiency for test sequences
 | All Intra High Efficiency | All Intra Low Complexity
sequence | BD-bitrate | BD-bitrate
BasketballPass_416x240_50 | -5.7% | -8.1%
BQSquare_416x240_60 | -6.6% | -7.0%
BlowingBubbles_416x240_50 | -6.0% | -6.9%
RaceHorses_416x240_30 | -4.3% | -6.4%
Average WQVGA | -5.6% | -7.1%
BasketballDrill_832x480_50 | -6.0% | -9.3%
BQMall_832x480_60 | -6.4% | -8.3%
PartyScene_832x480_50 | -5.9% | -6.2%
RaceHorses_832x480_30 | -3.7% | -5.8%
Average WVGA | -5.5% | -7.4%
vidyo1_720p_60 | -4.9% | -6.2%
vidyo3_720p_60 | -4.7% | -5.5%
vidyo4_720p_60 | -4.7% | -5.7%
Average 720P | -4.8% | -5.8%
Kimono1_1920x1080_24 | -1.5% | -2.2%
ParkScene_1920x1080_24 | -2.3% | -3.7%
Cactus_1920x1080_50 | -4.1% | -6.0%
BasketballDrive_1920x1080_50 | -4.5% | -7.2%
BQTerrace_1920x1080_60 | -3.5% | -5.1%
Average 1080P | -3.2% | -4.9%
Traffic_2560x1600_30_crop | -3.3% | -4.6%
PeopleOnStreet_2560x1600_30_crop | -4.1% | -5.2%
Average 1600P | -3.7% | -4.9%
Average | -4.6% | -6.1%

## Slide 13: Results of Faster configuration in CE6 test conditions
in addition to the SDIP early skip method, for 4x16 blocks, intra modes 26-33 were skipped and modes 18-25 were skipped for 16x4 partitions, in addition, 1x16/16x1 blocks used the best mode of corresponding 4x16/16x4 partitions.
Platform | CPU | Memory | Compiler
Windows Server 2008 R2 64 bits | 2xIntel Xeon L5420@2.5Ghz | 16GB | VS2010

## Slide 14: Results in CE6 test conditions
 | Intra |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -3.5 | -1.9 | -1.9 | -4.5 | -3.3 | -3.4
Class B | -3.0 | -1.4 | -1.7 | -4.4 | -2.5 | -3.2
Class C | -5.2 | -2.8 | -3.1 | -7.0 | -3.8 | -4.4
Class D | -5.4 | -2.9 | -2.9 | -6.8 | -3.9 | -4.2
Class E | -4.5 | -3.0 | -2.7 | -5.3 | -6.3 | -5.6
All | -4.3 | -2.4 | -2.5 | -5.7 | -3.8 | -4.1
Enc Time[%] | 161% |  |  | 146% |  | 
Dec Time[%] | 100% |  |  | 105% |  | 
Table 3. Resutls of faster configuration

## Slide 15: Results of Faster configuration
Table4. Comparison of coding efficiency for test sequences
 | All Intra High Efficiency | All Intra Low Complexity
sequence | BD-bitrate | BD-bitrate
BasketballPass_416x240_50 | -5.4% | -7.7%
BQSquare_416x240_60 | -6.3% | -6.9%
BlowingBubbles_416x240_50 | -5.6% | -6.6%
RaceHorses_416x240_30 | -4.1% | -6.1%
Average WQVGA | -5.4% | -6.8%
BasketballDrill_832x480_50 | -5.7% | -8.9%
BQMall_832x480_60 | -5.9% | -7.6%
PartyScene_832x480_50 | -5.7% | -6.0%
RaceHorses_832x480_30 | -3.4% | -5.4%
Average WVGA | -5.2% | -7.0%
vidyo1_720p_60 | -4.6% | -5.7%
vidyo3_720p_60 | -4.6% | -5.0%
vidyo4_720p_60 | -4.5% | -5.1%
Average 720P | -4.5% | -5.3%
Kimono1_1920x1080_24 | -1.4% | -2.0%
ParkScene_1920x1080_24 | -2.1% | -3.2%
Cactus_1920x1080_50 | -3.7% | -5.5%
BasketballDrive_1920x1080_50 | -4.2% | -6.8%
BQTerrace_1920x1080_60 | -3.4% | -4.8%
Average 1080P | -3.0% | -4.4%
Traffic_2560x1600_30_crop | -3.1% | -4.1%
PeopleOnStreet_2560x1600_30_crop | -4.0% | -4.8%
Average 1600P | -3.5% | -4.5%
Average | -4.3% | -5.7%

## Slide 16: Conclusion
SDIP shows 4.3% and 5.7% bit rate saving on average in faster configurations, under all intra high efficiency and low complexity conditions, respectively, Up to 8.9% bit rate saving is achieved on sequences with rich edges.
We recommend to adopt the SDIP into HM as an extension of traditional square NxN partitions, and further improve the Intra coding efficiency of HEVC.

## Slide 17
Notes: <number>