## Slide 1: JCTVC-D300: Improved Intra prediction for positive directions in UDI
Yongbing Lin, Changcai Lai,
Jianhua Zheng, Lingzhi Liu

## Slide 2: Observation
Positive direction in UDI can find two reference pixels form main and side arrays, respectively, which means both the arrays can be used to improve the prediction accuracy.
Mode 6 and mode 9 have the same texture direction of 45 degrees
An improved Intra predictor is proposed by taking place of the existing mode 6

## Slide 3: Intra predictor for positive directions
Prediction value is generated by using linear interpolation method
  P’(x, y) = (ref1*d2 + ref2*d1)/(d1+d2)
  d1 = y+1, d2 = x+1
  ref1 & ref2: reference pixels from main and side arrays
Mode 6 : an positive direction of 45 degrees, which means the two reference pixels are in integer position

## Slide 4: Test results
Common test condition for both Intra and Intra LOCO cases.
0.3% and 0.4% bit-rate reduction over HM0.9 for Intra and Intra LoCo configurations while keeping almost the same encoding and decoding time.
It is noticed that only the Intra prediction for mode 6 has been modified in current implementation. Other modes are not changed.

## Slide 5: Conclusion
Improve coding performance while keeping almost the same encoding and decoding time as anchor.
Suggestion to adopt the proposal for low-complexity applications