## Slide 1: JCTVC-D302: Intra coding improvements for slice boundary blocks
Yongbing Lin, Changcai Lai,
Jianhua Zheng, Lingzhi Liu

## Slide 2: Introduction
HEVC will support multiple slice partitioning
  to meet the requirement of video transmission over error-prone channel
Simulation on HM0.9-AHG-SLICES shows 5% gain drop for Intra and Intra loco configurations in cased of 1500bytes per slice
  Due to more slice boundary blocks are generated
We propose 2 Intra coding improvements for slice boundary blocks
  Intra prediction mode coding
  Reference pixel padding

## Slide 3: Coding of Intra prediction
Bit spending for Intra prediction mode coding can be saved by reducing the number of the candidate Intra prediction modes. For example,
  No vertical mode is used for the blocks at the top boundary of a slice. It is also true for the blocks at the left boundary of a slice
  For the upper-left corner block of a slice always uses DC mode. Thus bit for coding prediction mode is not required
Vertical mode
Horizontal
mode

## Slide 4: Reference pixel padding
Padding process for the unavailable reference pixels
  Padding with the closest pixel from its available neighbor block, instead of a fixed DC value, e.g. 128.
  The upper-left corner reference pixel is also padded
Current block at the top boundary of a slice.
( Its left neighbor block is available while its upper and upper-left neighbor blocks are not available. )
LeftBlock
available
copying

## Slide 5: Test results
The two improvements have been integrated into HM0.9-AHG-SLICES
Common test condition for both Intra and Intra LOCO cases, 1500bytes per slice
0.5% and 0.4% bit-rate reduction for Intra and Intra LoCo configurations while keeping almost the same encoding and decoding time

## Slide 6: Test results of single improvement
2. Performance of reference pixel padding
 | Intra |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.1 | -0.1 | -0.1 | -0.2 | -0.1 | -0.1
Class B | -0.1 | -0.1 | -0.1 | -0.2 | -0.1 | -0.1
Class C | -0.1 | -0.1 | -0.1 | -0.2 | -0.1 | -0.1
Class D | -0.1 | -0.1 | -0.1 | -0.2 | -0.1 | -0.1
Class E | -0.2 | -0.2 | -0.2 | -0.2 | -0.1 | -0.1
All | -0.1 | -0.1 | -0.1 | -0.2 | -0.1 | -0.1
Enc Time[%] | 101% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 101% |  | 
1. Performance of Intra mode coding
 | Intra |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.3 | 0.3 | 0.8 | -0.1 | 0.2 | 0.7
Class B | -0.5 | -0.2 | -0.2 | -0.3 | -0.2 | -0.1
Class C | -0.6 | -0.4 | -0.2 | -0.4 | -0.6 | -0.4
Class D | -0.3 | -0.2 | -0.1 | -0.2 | -0.2 | -0.3
Class E | -0.9 | -0.1 | 0.0 | -0.6 | 0.3 | -0.2
All | -0.5 | -0.2 | 0.0 | -0.3 | -0.1 | -0.1
Enc Time[%] | 102% |  |  | 103% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 

## Slide 7: Conclusion
Improve coding performance while keeping almost the same encoding and decoding time as anchor.
Suggestion to adopt the proposal for low-complexity applications