## Slide 1: CE7: Simplified MDDT scheme using symmetry-based scanning orders (JCTVC-D304)
26/7/29
Haitao Yang, Jiantong Zhou, Haoping Yu
Huawei Technologies
Notes: <number>

## Slide 2
Contents
Introduction
  SMDDT (Simplified MDDT)
SMDDT-ST
  SMDDT component 1 – Simplified Transform
SMDDT-SSO
  SMDDT component 2 – Symmetry-based Scanning Orders
RD performance
Complexity analysis
Closing remarks

## Slide 3: Introduction
SMDDT (Simplified MDDT)
  ST (Simplified Transform): 4 modes
  SSO (Symmetry-based Scanning Orders): 3 modes

## Slide 4: SMDDT-ST
Implemented as DCT/DST combination
Used in a mode dependent manner
For 4x4 and 8x8 TUs only

## Slide 5: SMDDT-SSO
The trained scanning orders are of symmetric properties (JCTVC-C106)
  Horizontal/Vertical symmetric
  Transposing symmetric
33 prediction directions in TMuC0.9 -> 3 SSO modes
(a) 33 prediction directions in TMuC0.9
(b) SSO modes

## Slide 6: SMDDT-SSO
For SSO mode 0, conventional zigzag scan is used
For SSO mode 1 & 2, two scanning orders are obtained through training
  Encode the sequences in the training set using TMuC0.9
  Get the statistics of the significant flag count of each block position inside a TU
  Sort the count in descending order to get the scanning order
In the implementation, SSO is used
  For 4x4 and 8x8 TUs in the HE case
  For all size TUs in the LC case

## Slide 7: RD performance
Gain of the SMDDT scheme in Intra HE/LC case
  -2.0%/-2.9%
Gain from SMDDT-ST in Intra HE/LC case
  -1.3%/-2.2%
Gain from SMDDT-SSO in Intra HE/LC case
  -0.7%/-0.7%

## Slide 8: Complexity analysis
The decoding time increase caused by the proposed SMDDT is small, 1%/3% in the Intra HE/LC case
SMDDT-ST
  4x4 and 8x8 DCT share the same implementation already in TMuC0.9
  8x8 DST is implemented as regular matrix multiplication
  4x4 DST is simplified using the method proposed in JCTVC-D046
SMDDT-SSO
  Two additional scanning orders besides zigzag needs to be stored
  For 4x4 and 8x8 TUs, the full scanning orders are stored. For TUs larger than 8x8, only first 64 scanning positions are stored in order.
  Conditional swap of the x and y component of a block position is performed in the implementation, negligible computational complexity

## Slide 9: Closing remarks
Additional scanning orders can improve the efficiency in the coding of intra coefficients
The number of scanning orders can be kept small if it is designed in a symmetric way
The additional scanning orders with symmetric features can be implemented efficiently
The proposed SMDDT scheme using symmetry-based scanning orders show good balance between the performance and the complexity
We suggest the simplified MDDT scheme with the proposed symmetry-based scanning orders is adopted in HM

## Slide 10
Notes: <number>