## Slide 1: Adaptive coefficients scanning for inter-frame coding
Huawei Tech. Co, Ltd

## Slide 2: Motivation
Structured textures still exist in the residual images after motion compensation. So the texture of reference block can represent the texture of the residual block
The coding image and its residual image

## Slide 3: Motivation
A relationship between residual block’s texture and transformed coefficients distribution
Relationship of residual texture and transformed coefficients distribution
When the residual block’s texture contains vertical edges, the non-zero transformed coefficients will fall along the horizontal direction. The reverse is also true.

## Slide 4: Introduction
three scanning patterns: new zigzag, horizontal and vertical patterns
(a) New zigzag scan (b) Horizontal scan (c) Vertical scan

## Slide 5: Introduction
the texture directions of the reference block need to be detected
calculating directional gradient
Horizontal gradient: SAD of two adjacent pixels in horizontal
direction
Vertical gradient: SAD of two adjacent pixels in vertical direction

## Slide 6: Introduction
If Horizontal gradient/Vertical gradient > threshold
Texture direction is vertical
Else if Vertical gradient/Horizontal gradient > threshold
Texture direction is horizontal
Else
Texture direction is diagonal

## Slide 7: Introduction
Relationship between the texture direction and scanning pattern
texture direction | Scanning pattern
horizontal | vertical
vertical | horizontal
diagonal | new zigzag

## Slide 8: Experimental results
 | Random access |  |  | 
 | Y BD-rate | U BD-rate | V BD-rate | % sig count
Class A | -0.3 | 0.1 | 0.1 | 1.97%
Class B | -0.4 | -0.1 | -0.1 | -3.13%
Class C | -0.4 | -0.1 | -0.1 | -3.14%
Class D | -0.4 | -0.1 | 0.0 | -2.17%
Class E |  |  |  | 
All | -0.4 | -0.1 | 0.0 | -1.62%
Enc Time[%] | 102% |  |  | 
Dec Time[%] | 102% |  |  | 
 | Low delay |  |  | 
 | Y BD-rate | U BD-rate | V BD-rate | % sig count
Class A |  |  |  | 
Class B | -1.2 | -0.2 | -0.1 | -5.34%
Class C | -1.2 | 0.0 | 0.1 | -3.17%
Class D | -1.2 | -0.5 | 0.0 | -4.03%
Class E | -0.7 | -0.2 | 0.1 | -12.37%
All | -1.1 | -0.2 | 0.0 | -6.23%
Enc Time[%] | 102% |  |  | 
Dec Time[%] | 103% |  |  | 

## Slide 9: Experimental results
Time | Enc | Dec
HE Random access | 102% | 102%
HE Low delay | 102% | 103%