## Slide 1: Fine Granularity Slice Partition
26/7/28
Qiu Shen
Qingpeng Xie
Haoping Yu
HUAWEI TECHNOLOGIES CO., LTD.
Notes: <number>

## Slide 2: Abstract
Follow the idea of Ericsson on fine granularity slice
Alternative slice partition
Slice start address signaling
Slice end address signaling for CABAC
Split flag deducing for slice start LCU
Page <number>

## Slide 3: Background
Ericsson proposed to define slices to be a sequence of CUs instead of a sequence of LCUs
Control the slice size more accurately
Page <number>

## Slide 4: Alternative Slice Partition
The sizes of LCUs are diversified for different video sequences, different bitrates and different coding modes.
Page <number>
  RaceHorses_832x480_20
  QP 32
  Intra: 100~500Bytes
  Inter: <150bytes

## Slide 5: Alternative Slice Partition
The slice can be partitioned based on CUs for large LCU size, and based on LCUs for small LCU size
Use a flag to indicate the type of slice partition
The flag can be included in SPS\PPS\Slice Header
Page <number>
slice_header( ) { | C | Descriptor
lcu_slice_flag | 2 | u(1)
} |  | 

## Slide 6: Slice Start Address Signaling
The slice start address is signaled hierarchically.
Page <number>
slice_header( ) { | C | Descriptor
slice_start_is_pic_start_flag | 2 | u(1)
if(slice_start_is_pic_start_flag){ |  | 
first_lcu_in_slice_minus_1 | 2 | u(v)
if(lcu_slice_flag==0){ |  | 
first_scu_is_zero_flag | 2 | u(1)
if(first_scu_is_zero_flag == 0) { |  | 
first_scu_in_slice_minus_1 | 2 | u(v)
} |  | 
} |  | 
} |  | 
} |  | 

## Slide 7: Slice End Address Signaling
For CABAC, it is necessary to indicate the end of slice.
Signal slice end address in slice header hierarchically.
Page <number>
slice_header( ) { | C | Descriptor
if(entropy_coding_mode_flag){ |  | 
slice_end_is_pic_end_flag | 2 | u(1)
if(slice_end_is_pic_end_flag==0) { |  | 
num_of_lcus_in_slice_minus1 | 2 | u(v)
if(lcu_slice_flag==0){ |  | 
last_scu_is_zero_flag | 2 | u(1)
if(last_scu_is_zero_flag == 0) { |  | 
last_scu_in_slice_minus_1 | 2 | u(v)
} |  | 
} |  | 
} |  | 
} |  | 
} |  | 

## Slide 8: Split Flag Deducing
Split flag for the first LCU in the slice can be deduced for some particular cases
Page <number>
coding_unit( ) { | C | Descriptor
if(CurrentCUInPicRange && CurrCodingUnitSize > MinCodingUnitSize ){ |  | 
if(LCUAddress != SliceStartLCUAddress){ |  | 
split_coding_unit_flag |  | 
}else{ |  | 
if(StartAddress>=SliceStartSCUAddress ) |  | 
split_coding_unit_flag | 2 | u(1) ¦ ae(v)
else if(StartAddress+ CurrCodingUnitSize < SliceStartSCUAddress) |  | 
split_coding_unit_flag=0 |  | 
else |  | 
split_coding_unit_flag=1 |  | 
} |  | 
} |  | 
… |  | 
} |  | 

## Slide 9: Simulation Results
Reports the performance of slice partition based on LCU and CU respectively
Slice setting: 1500bytes per slice
Page <number>
 | Slice partition based on LCU (ad-hoc group source code) | Slice partition based on CU
Randomaccess | 3.54% | 4.0%
Lowdelay | 2.10% | 2.5%
Intra | 4.76% | 5.4%
Randomaccess_loco | 3.61% | 4.0%
Lowdelay_loco | 2.09% | 2.3%
Intra_loco | 5.42% | 6.0%

## Slide 10: Conclusion
We proposed to adopt slice partition based on not only LCU but also CU
Proposed syntax changes can support both kinds of slices
For both kinds of slices, effect on coding efficiency is acceptable
Page <number>

## Slide 11
Notes: <number>