## Slide 1: JCTVC-D365 Fast Integer Transforms for the HM, and Complexity Analysis
Samsung Electronics Co., Ltd.
&
FastVDO LLC
Notes: <number>

## Slide 2: Introduction
In current HM design
  16x16, 32x32, 64x64 integer transform based on Chen’s fast DCT algorithm
This contribution presents
  1) Simplified quant/de-quant matrices of HM
  2) New integer transform with simplified quant/de-quant matrices
  3) New integer transform with lifting

## Slide 3: Simplification of quant/de-quant matrices
In current HM
  6 quantization and 6 de-quantization matrices which have same size with input block
  To compensate differences introduced by incorporating scaling into inverse quantization steps.
In this proposal
  Each quant/de-quant matrices are replaced as a scalar value
  No significant loss is introduced by this simplification.

## Slide 4: New integer transform with simplified quant/de-quant matrices (1)
Signal flow graph for new 32-point transform
  Proposed in JCTVC-C209, Geneva meeting

## Slide 5: New integer transform with simplified quant/de-quant matrices (2)
Integer approximation of sinusoidal
  All cosine and sine values are approximated to the type of q/2p (dyadic rationals)
  P controls dynamic range and coding gain of transform
Scaling factors
  Integrated into the quantization step to reduce the number of operations.

## Slide 6: New integer transform with lifting
Lifting implementation of new integer transform
  Bi-orthogonal
  Invertible
  Less number of multiplication
Multiplication-free conversion
  Factorization of multiplication into add and shift only

## Slide 7: Complexity: number of operations
Comparison to transforms in HM

## Slide 8: Complexity: dynamic range
Matrix norm-based estimation
  Maximum column/row sum norm
  Increment of dynamic range after 16-point and 32-point transform is within 4 and 5 bit for both HM’s and proposed transform, respectively.
 | HM 16T | New 16T | New 16T + lifting | HM 32T | New 32T | New 32T + lifting
Max. column sum norm | 10.28 | 10.29 | 12.20 | 20.52 | 20.51 | 21.53
Max. row sum norm | 11.25 | 11.25 | 16 | 22.63 | 22.63 | 32

## Slide 9: Results: simplified quant/de-quant matrices

## Slide 10: Results: new integer transform with simplified quant/de-quant matrices

## Slide 11: Results: new integer transform with lifting

## Slide 12: Conclusions
We presented 3 variants which improve current transform in HM
  Simplified quant/de-quant matrices
  New integer transform with simplified quant/de-quant matrices
  New integer transform with lifting
Experimental results show that all 3 variants do not significantly change the performance while reducing the complexity.
We therefore propose
  Adoption of simplification of quantization and de-quantization matrices to the current HM
  As a next step, creation of CE to investigate those issues in detail