## Slide 1: JCTVC-D366 - CE5: Improved intra prediction mode coding with LCEC
Marta Karczewicz, Xianglin Wang, Wei-Jung Chen (Qualcomm)
Arild Fuldseth (Cisco)

## Slide 2: Intra Prediction Mode Coding
Assigning VLC code number to the intra prediction mode:
  If chosen intra prediction mode is equal to the most probable mode iMostProbable, code number 0 is used.
  Otherwise code number n is assigned to the intra mode iDir using a single mapping table.
  iDir=iDir-1 if iDir > iMostProbable.
Ordering of intra modes (mapping table) is adaptive (same adaptation method used as for other syntax elements).
Two VLC tables used (4x4 block used as an example – 17 modes):
H0={1, 4, 4, 5, 5, 5, 5, 5, 5, 5, 5, 5, 5, 6, 6, 6, 6},
H1={2, 3, 4, 4, 4, 4, 4, 5, 5, 5, 5, 5, 5, 5, 5, 5, 5}.
Table H0 used when left and above intra modes same, table H1 otherwise.

## Slide 3
 | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.6 | -0.4 | -0.3
Class B | -0.5 | -0.2 | -0.2
Class C | -0.5 | -0.2 | -0.1
Class D | -0.4 | -0.1 | -0.1
Class E | -0.5 | -0.3 | -0.3
All | -0.5 | -0.2 | -0.2
 | Random access LoCo |  |  |  |  | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate |  |  | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.3 | -0.1 | 0.1 |  | Class A |  |  | 
Class B | -0.2 | -0.1 | -0.1 |  | Class B | 0.1 | 0.1 | 0.4
Class C | -0.2 | -0.1 | 0.0 |  | Class C | 0.0 | 0.0 | 0.0
Class D | -0.1 | -0.2 | 0.0 |  | Class D | 0.0 | 0.0 | 0.0
Class E |  |  |  |  | Class E | 0.0 | 0.0 | 0.0
All | -0.2 | -0.1 | 0.0 |  | All | -0.1 | -0.1 | -0.1