## Slide 1: JCTVC-D370 CE5: Improved coding of inter prediction mode with LCEC
Wei-Jung Chen, Xianglin Wang,
Marta Karczewicz

## Slide 2: Current Inter Prediction Mode Coding
Inter prediction mode contains Split, Skip, Merge, Direct, Inter_2Nx2N, Inter_2NxN , Inter_Nx2N, Inter_NxN, Intra_2Nx2N, and Intra_NxN.
Unary code for inter prediction mode coding.
One fixed VLC codebook for partition size coding.
Split flag
Skip flag
Merge flag
Direct flag
N
N
N
Partition Size
N
End
Y
Y
Y
Y
Inter prediction mode | Split | Skip | Merge | Direct | Others
codeword | 1 | 01 | 001 | 0001 | 0000

## Slide 3: Proposed Approach
Unary code with codebook adaptation for inter prediction mode coding.
CU-depth dependent fixed VLC codebooks for partition size coding.
Split | 1
Skip | 01
Merge | 001
Direct_L0 | 0001
Direct_L1 | 00001
Direct_Bi | 000001
Others | 000000
Split | 1
Skip | 01
Direct_L0 | 001
Merge | 0001
Direct_L1 | 00001
Direct_Bi | 000001
Others | 000000
Split | 1
Skip | 01
Direct_L0 | 001
Direct_L1 | 0001
Merge | 00001
Direct_Bi | 000001
Others | 000000

## Slide 4: Simulation Results-Inter prediction mode coding
 | Random access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | -1.9 | -1.6 | -1.4
Class B | -1.9 | -1.7 | -1.6
Class C | -1.6 | -1.5 | -1.5
Class D | -1.7 | -1.6 | -1.4
Class E |  |  | 
All | -1.8 | -1.6 | -1.5
 | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  | 
Class B | -1.4 | -1.5 | -1.5
Class C | -1.1 | -1.5 | -1.5
Class D | -1.2 | -1.5 | -1.7
Class E | -3.0 | -3.5 | -3.4
All | -1.6 | -1.9 | -1.9

## Slide 5: Counter Adaptation
Replacing current direct-swapping based adaptation scheme with counter based adaptation.
  Effective when small number of symbols is coded.
  After encoding of each symbol the counter for this symbol is increased. If the current symbol’s counter is greater than the counter of the symbol with the codeword index smaller by one, the codeword indices of these symbols are swapped.
  Added to block flag coding and {inter_pre_idc, ref_idx} pair coding

## Slide 6: Simulation Results
 | Random access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | -1.9 | -1.6 | -1.4
Class B | -1.9 | -1.7 | -1.6
Class C | -1.6 | -1.5 | -1.5
Class D | -1.7 | -1.6 | -1.4
Class E |  |  | 
All | -1.8 | -1.6 | -1.5
 | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  | 
Class B | -1.4 | -1.5 | -1.5
Class C | -1.1 | -1.5 | -1.5
Class D | -1.2 | -1.5 | -1.7
Class E | -3.0 | -3.5 | -3.4
All | -1.6 | -1.9 | -1.9
 | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.1 | -0.1 | 0.1
Class B | 0.0 | 0.2 | 0.2
Class C | 0.0 | 0.0 | 0.1
Class D | -0.1 | 0.0 | 0.0
Class E | -0.2 | 0.3 | 0.2
All | -0.1 | 0.1 | 0.1
 | Random access LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | -2.1 | -1.7 | -1.6
Class B | -1.9 | -1.6 | -1.5
Class C | -1.8 | -1.4 | -1.6
Class D | -1.8 | -1.6 | -1.4
Class E |  |  | 
All | -1.9 | -1.6 | -1.5
 | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  | 
Class B | -1.8 | -1.0 | -1.2
Class C | -1.5 | -1.6 | -1.4
Class D | -1.7 | -1.4 | -1.2
Class E | -3.3 | -3.1 | -3.1
All | -2.0 | -1.7 | -1.6
Inter prediction mode coding
Inter prediction mode coding
+counter based adaptation

## Slide 7: Conclusion
Based on the results, we recommend the improved scheme for LCEC inter mode coding to be adopted into HM.
We also recommend using counter based adaptation for some short VLC table to achieve better coding performance

## Slide 8
Thank you