## Slide 1: JCTVC-D374 - CE5: Improved coefficient coding with LCEC

## Slide 2: Intra Modifications – Coefficients Coding
The mapping table between {levelID, run} and code number cn depends on the maximum possible run value maxrun, 29 tables for different values of maxrun. Same tables used for inter and intra.
Proposal - add mapping for intra blocks, with additional dependency on parameter n equal to 0 if the absolute value of any of the coefficient coded is larger than 1. Otherwise, n is equal to the number of non-zero coded coefficients.
  The value of cn is calculated given values of levelID, run, maxrun and n.

## Slide 3
 | Intra LoCo |  |  | Random access LoCo |  |  | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -2.1 | -1.4 | -1.2 | -0.7 | -0.6 | -0.6 |  |  | 
Class B | -1.4 | -1.3 | -1.2 | -0.5 | -1.3 | -1.4 | -0.1 | -1.6 | -1.9
Class C | -1.5 | -0.9 | -0.9 | -0.5 | -1.1 | -1.0 | -0.1 | -2.2 | -2.0
Class D | -1.8 | -1.1 | -1.0 | -0.6 | -2.0 | -1.8 | -0.1 | -2.7 | -2.7
Class E | -1.2 | -0.8 | -0.9 |  |  |  | 0.0 | -0.9 | -1.1
All | -1.6 | -1.1 | -1.0 | -0.6 | -1.3 | -1.3 | -0.1 | -1.9 | -2.0
Enc Time[%] | 100% |  |  | 99% |  |  | 101% |  | 
Dec Time[%] | 100% |  |  | 96% |  |  | 98% |  | 

## Slide 4: Intra Modifications – Scans
3 fixed scans used, zig-zag, horizontal, vertical, choice dependent on prediction direction. Horizontal and vertical are flipped version of each other, scans are not trained – obtained by a formula.
Two sets of fixed scans tested:
Scan adaptation:
  Scan statistics are updated by incrementing the counter at a scan position whenever a non-zero coefficient is encountered.
  The incremented scan position’s counter is compared with the counter for the previous position in the scan order.

## Slide 5
 | Fixed scans 1 |  |  | Fixed scans 2 |  |  | Fixed scans 2, adaptation |  | 
 | Intra LoCo |  |  | Intra LoCo |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -1.1 | -0.3 | 0.1 | -2.2 | -1.5 | -1.4 | -3.2 | -2.5 | -2.5
Class B | -2.1 | -2.3 | -2.1 | -2.5 | -2.7 | -2.7 | -3.5 | -3.6 | -3.6
Class C | -2.4 | -1.8 | -1.7 | -2.4 | -1.9 | -1.9 | -3.0 | -2.3 | -2.4
Class D | -2.9 | -1.9 | -2.1 | -2.9 | -2.1 | -2.2 | -3.2 | -2.3 | -2.4
Class E | -1.0 | 0.9 | 0.5 | -2.9 | -2.5 | -2.3 | -3.4 | -3.0 | -2.8
All | -2.1 | -1.3 | -1.4 | -2.6 | -2.2 | -2.2 | -3.3 | -2.8 | -2.8
Enc Time[%] | 102% |  |  | 101% |  |  | 101% |  | 
Dec Time[%] | 101% |  |  | 98% |  |  | 100% |  | 

## Slide 6
 | Intra LoCo |  |  | Random access LoCo |  |  | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -3.2 | -2.5 | -2.5 | -1.3 | -1.2 | -1.2 |  |  | 
Class B | -3.5 | -3.6 | -3.6 | -1.6 | -2.2 | -2.4 | -0.4 | -1.9 | -2.2
Class C | -3.0 | -2.3 | -2.4 | -1.1 | -1.7 | -1.7 | -0.2 | -2.2 | -2.0
Class D | -3.2 | -2.3 | -2.4 | -1.0 | -2.0 | -2.0 | -0.3 | -2.7 | -2.7
Class E | -3.4 | -3.0 | -2.8 |  |  |  | -0.4 | -1.1 | -0.9
All | -3.3 | -2.8 | -2.8 | -1.3 | -1.9 | -1.9 | -0.3 | -2.0 | -2.0
Enc Time[%] | 113% |  |  | 99% |  |  | 105% |  | 
Dec Time[%] | 101% |  |  | 98% |  |  | 100% |  | 

## Slide 7: 16x16 Block Coding
Code number cn assignment to the {levelID, run} pair:
  Intra blocks - same method used as for 8x8 blocks.
  Inter blocks - 8x8 blocks tables used, when maxrun<28.Otherwise:
  if (levelID==0)
  cn=run;
  else
  cn=maxrun+run+2;
Code number cn assignment to {levelID, lastPos} pair:
  if (levelID ==0)
    cn=((lastPos + (lastPos >>4))>>4)+ lastPos;
  else
  if (lastPos <15)
  cn=16*(lastPos +1);
    else
  cn = 256* levelID + lastPos;

## Slide 8
 | Mod VLC, Adaptive Scan |  |  | Mod VLC, Adaptive Scan, new RDOQ |  |  | Mod VLC, Adaptive Scan, new RDOQ, 16x16 |  | 
 | Intra LoCo |  |  | Intra LoCo |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -3.2 | -2.5 | -2.5 | -4.4 | -1.7 | -1.6 | -6.8 | -2.3 | -2.1
Class B | -3.5 | -3.6 | -3.6 | -4.9 | -2.9 | -3.1 | -7.2 | -3.1 | -3.5
Class C | -3.0 | -2.3 | -2.4 | -4.1 | -2.4 | -2.8 | -5.3 | -2.7 | -3.0
Class D | -3.2 | -2.3 | -2.4 | -4.2 | -2.4 | -2.8 | -5.4 | -2.8 | -3.2
Class E | -3.4 | -3.0 | -2.8 | -4.5 | -2.4 | -2.4 | -6.7 | -3.8 | -3.7
All | -3.3 | -2.8 | -2.8 | -4.4 | -2.5 | -2.7 | -6.2 | -3.0 | -3.2
Enc Time[%] | 113% |  |  | 95% |  |  | 102% |  | 
 |  | Random access LoCo |  |  | Random access LoCo |  |  | Random access LoCo | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -1.3 | -1.2 | -1.2 | -1.7 | -0.2 | -0.1 | -2.6 | 0.4 | 0.2
Class B | -1.6 | -2.2 | -2.4 | -2.2 | -1.4 | -1.8 | -3.4 | -0.8 | -1.5
Class C | -1.1 | -1.7 | -1.7 | -1.4 | -1.1 | -1.5 | -2.1 | -0.9 | -1.1
Class D | -1.0 | -2.0 | -2.0 | -1.4 | -1.6 | -1.8 | -2.1 | -1.7 | -2.0
Class E |  |  |  |  |  |  |  |  | 
All | -1.3 | -1.9 | -1.9 | -1.7 | -1.2 | -1.5 | -2.6 | -0.9 | -1.3
Enc Time[%] | 99% |  |  | 98% |  |  | 102% |  | 
 | Low delay LoCo |  |  | Low delay LoCo |  |  | Low delay LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  |  |  |  | 
Class B | -0.4 | -1.9 | -2.2 | -1.0 | -1.3 | -1.6 | -2.9 | 0.4 | -0.3
Class C | -0.2 | -2.2 | -2.0 | -0.9 | -2.3 | -2.2 | -2.1 | -1.6 | -1.9
Class D | -0.3 | -2.7 | -2.7 | -1.0 | -2.5 | -2.5 | -2.2 | -2.8 | -2.7
Class E | -0.4 | -1.1 | -0.9 | -1.1 | 1.2 | 0.0 | -2.6 | 2.3 | 0.8
All | -0.3 | -2.0 | -2.0 | -1.0 | -1.4 | -1.7 | -2.5 | -0.5 | -1.1
Enc Time[%] | 105% |  |  | 102% |  |  | 108% |  | 

## Slide 9: Backup

## Slide 10
 | Fixed scans 2 |  |  | Fixed scans 2, adaptation |  | 
 | Intra LoCo |  |  | Intra LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.3 | 0.3 | 0.2 | 0.2 | -0.3 | -0.4
Class B | -0.5 | -0.8 | -0.9 | -0.7 | -1.1 | -1.3
Class C | -0.5 | -0.6 | -0.7 | -0.3 | -0.6 | -0.7
Class D | -0.5 | -0.6 | -0.7 | -0.1 | -0.4 | -0.5
Class E | -1.0 | -1.1 | -0.9 | -0.8 | -1.3 | -1.0
All | -0.5 | -0.6 | -0.7 | -0.4 | -0.8 | -0.8